## Slide 1: Bus & Naming Scheme
Computer System Engineering, Fall 2018. (IPADS, SJTU)
Physical address space
Yubin Xia

## Slide 2: Review: Layers

## Slide 3: Review: A Canonical Device
Status
Address
Data
Command
Registers
Micro-controller (CPU)
Memory (DRAM or SRAM or both)
Other Hardware-specific Chips
Interface
Internals

## Slide 4: Review: Interrupt & DMA
Using Polling
Using Interrupt
Without DMA
With DMA

## Slide 5: Review: Methods of Device Interaction
Method-1: PIO through I/O instructions
  On x86, in and out instructions
  I/O port name space
  Must be executed in privileged mode (kernel mode)
Method-2: Memory-mapped I/O
  Using LOAD and STORE
  Physical address space
  Can also be executed in unprivileged mode (user mode)

## Slide 6: Case Study: IDE Disk Driver

## Slide 7: IDE Protocol
Wait for drive to be ready (0x1F7)
  Read Status Register until drive is READY and not BUSY
Write parameters to command registers (0x1F2 – 0x1F6)
  Sector count
  Logical block address (LBA) of the sectors to be accessed
  Drive number
    Master=0x00 or slave=0x10, as IDE permits just two drives
Start the I/O (0x1F7)
  By issuing read/write to command register
  Write READ / WRITE command to command register
Address 0x1F0 = Data Port
Address 0x1F1 = Error
Address 0x1F2 = Sector Count
Address 0x1F3 = LBA low byte
Address 0x1F4 = LBA mid byte
Address 0x1F5 = LBA hi byte
Address 0x1F6 = 1B1D TOP4LBA: B=LBA, D=drive
Address 0x1F7 = Command/status

## Slide 8: IDE Protocol
Data transfer (for writes)
  Wait until drive status is READY and DRQ (drive request for data)
  Write data to data port
Handle interrupts
  In the simplest case, handle an interrupt for each sector transferred
  More complex approaches allow batching and thus one final interrupt when the entire transfer is complete
Error handling
  After each operation, read the status register
  If the ERROR bit is on, read the error register for details
Address 0x1F0 = Data Port
Address 0x1F1 = Error
Address 0x1F2 = Sector Count
Address 0x1F3 = LBA low byte
Address 0x1F4 = LBA mid byte
Address 0x1F5 = LBA hi byte
Address 0x1F6 = 1B1D TOP4LBA: B=LBA, D=drive
Address 0x1F7 = Command/status

## Slide 9: IDE Disk Driver using PIO
static int ide_wait_ready() {
while (((int r = inb(0x1f7)) & IDE_BSY) || !(r & IDE_DRDY))
; // loop until drive isn’t busy
}
static void ide_start_request(struct buf *b) {
ide_wait_ready();
outb(0x3f6, 0); // generate interrupt
outb(0x1f2, 1); // how many sectors?
outb(0x1f3, b->sector & 0xff); // Block address here ...
outb(0x1f4, (b->sector >> 8) & 0xff); // ... and here
outb(0x1f5, (b->sector >> 16) & 0xff); // ... and here!
outb(0x1f6, 0xe0 | ((b->dev&1)<<4) | ((b->sector>>24)&0x0f));
if(b->flags & B_DIRTY){
outb(0x1f7, IDE_CMD_WRITE); // this is a WRITE
outsl(0x1f0, b->data, 512/4); // transfer data too!
} else {
outb(0x1f7, IDE_CMD_READ); // this is a READ (no data)
}
}
Address 0x1F0 = Data Port
Address 0x1F1 = Error
Address 0x1F2 = Sector Count
Address 0x1F3 = LBA low byte
Address 0x1F4 = LBA mid byte
Address 0x1F5 = LBA hi byte
Address 0x1F6 = 1B1D TOP4LBA: B=LBA, D=drive
Address 0x1F7 = Command/status
Status
Register
(0x1F7):
7: BUSY
6: READY
5: FAULT
4: SEEK
3: DRQ
2: CORR
1: IDDEX
0: ERROR
Error
Register
(0x1F1):
7: BBK
6: UNC
5: MC
4: IDNF
3: MCR
2: ABRT
1: T0NF
0: AMNF
BBK = Bad Block
UNC = Uncorrectable data error
MC = Media Changed
IDNF = ID mark Not Found
MCR = Media Change Requested
ABRT = Command aborted
T0NF = Track 0 Not Found
AMNF = Address Mark Not Found

## Slide 10: IDE Disk Driver using PIO
void ide_rw(struct buf *b) {
acquire(&ide_lock);
for (struct buf **pp = &ide_queue; *pp; pp=&(*pp)->qnext)
; // walk queue
*pp = b; // add request to end
if (ide_queue == b) // if q is empty
ide_start_request(b); // send req to disk
while ((b->flags & (B_VALID|B_DIRTY)) != B_VALID)
sleep(b, &ide_lock); // wait for completion
release(&ide_lock);
}

## Slide 11: IDE Disk Driver using PIO
void ide_intr() {
struct buf *b;
acquire(&ide_lock);
if ((b = idequeue) == 0) {
release*&idelock); return;
}
idequeue = b-> next;
if (!(b->flags & B_DIRTY) && ide_wait_ready() >= 0)
insl(0x1f0, b->data, 512/4); // if READ: get data
b->flags |= B_VALID;
b->flags &= ~˜B_DIRTY;
wakeup(b); // wake waiting process
if (ide_queue != 0) // start next request
ide_start_request(ide_queue); // (if one exists)
release(&ide_lock);
}

## Slide 12: Review: IDE Driver using PIO
Q: What is the process of disk write?
  CPU waits for disk to be ready (ide_wait_ready)
  CPU sends WRITE request to disk (which block to write? LBA)
  CPU transfers data to the disk (outsl(0x1f0, b->data, 512/4))
  CPU waits (CPU switches to another thread)
  …
  Disk finishes write (data maybe in disk’s buffer)
  Disk sends an interrupt to CPU
  CPU wakes up the waiting thread

## Slide 13: Review: IDE Driver using PIO
Q: What is the process of disk read?
  CPU waits for disk to be ready (ide_wait_ready)
  CPU sends READ request to disk (which block to read? LBA)
  CPU waits (CPU switches to another thread)
  … (can be a long time)
  Disk finishes read (data now in disk’s buffer)
  Disk sends an interrupt to CPU
  CPU reads data from disk’s buffer to memory (insl(0x1f0, b->data, 512/4))
  CPU wakes up the waiting thread

## Slide 14: BUS: a hardware layer

## Slide 15: A Hardware Layer: the Bus

## Slide 16: Bus Features
A set of wires
  Comprising address, data, control lines that connect to a bus interface on each module
Broadcast link
  Every module hears every message
  Bus address: identify the intended recipient, as the name
Bus arbitration protocol
  Decide which module may send or receive message at any particular time
  Bus arbiter (optional): a circuit to choose which modules can use the bus

## Slide 17: Bus Transaction
Source module requires exclusive use of the bus: the data sender
Source module places a bus address of the destine module on the bus
Source module signals READY wire to alert the other module
The destine module singles ACKNOWLEDGE wire after copied the data
  If synchronized, then READY & ACKNOWLEDGE are not needed, just need to check the address lines on each clock cycle
Source module releases the bus

## Slide 18: Memory Load Example: LOAD 1742, R1
Processor #2 => all bus modules: {1742, READ, 102}

## Slide 19: Memory Load Example: LOAD 1742, R1
Memory 1 recognizes the address is within its range
  By examining just a few high-order address bits

## Slide 20: Memory Load Example: LOAD 1742, R1
Memory 1 acknowledges and processor 2 releases the bus
Memory 1 performs the internal operation to get the value
  value <- READ (1742)

## Slide 21: Memory Load Example: LOAD 1742, R1
Memory1 => all bus modules: {102, value}

## Slide 22: Memory Load Example: LOAD 1742, R1
Processor 2 is waiting for this result, just copies the data on the bus to its register R1

## Slide 23: Memory Load Example: LOAD 1742, R1
Processor 2 acknowledges and memory 1 releases the bus

## Slide 24: Sync VS. Async
Sync data transfer
  Source & destination cooperate through a shared clock
Async data transfer
  Source and destination cooperate through explicit signal line
    E.g., acknowledge line

## Slide 25: DMA on Bus

## Slide 26: DMA Example
BIOS
Memory
Disk
Processor 1
101
256-511
3072-4095
121-124
Processor #1 => all bus modules: {121, WRITE, 11742}
  Disk acknowledge and write the value 11742 to its control register
Processor #1 => all bus modules: {122, WRITE, 3328}
Processor #1 => all bus modules: {123, WRITE, 256}
Processor #1 => all bus modules: {124, WRITE, 1}
102
Processor 2

## Slide 27: DMA Example
BIOS
Memory
Disk
Processor 1
101
256-511
3072-4095
121-124
Disk => all bus modules: {3328, WRITE, data[11742]}
  Memory acknowledge and save data[11742]
Disk => all bus modules: {3329, WRITE, data[11743]}
... (loop)
Disk => all bus modules: {3583, WRITE, data[11997]}
102
Processor 2

## Slide 28: DMA Example
BIOS
Memory
Disk
Processor 1
101
256-511
3072-4095
121-124
When transferring is finished, disk controller SENDs message to the processor
  Just like keyboard controller does when press a key
Processor will enter interrupt handler next cycle
Now the processor knows that the DMA is done
102
Processor 2

## Slide 29: Summary

## Slide 30: Summary
CPU interacts with physical memory
  Through system bus that connects each other
  Using physical address to name memory content
CPU interacts with a device
  Also using physical address (aka., bus address)
  Polling, interrupt and DMA
  I/O instruction (PIO) or MMIO

## Slide 31: Summary
Processor
Memory
I/O Device
load/store
PIO (in/out)
/MMIO (load/store)
DMA
Memory Load/Store
  Between CPU and memory
  Physical memory address space
I/O Operations
  MMIO: map device memory and registers into physical address space
DMA
  Also using physical address

## Slide 32: Questions
Q: How are the physical addresses assigned?
  Memory physical addresses: by BIOS
  Some devices (e.g., keyboard, IDE): fixed for all time
  Other devices: assigned by the OS

## Slide 33: Questions
Q: Why not map the whole disk to memory?
  So that the CPU can access a byte on the disk directly by system bus
  1. Too large
  2. Too slow
The principle of least astonishment:
People are part of the system. The design should match the user’s experience, expectations, and mental models

## Slide 34: Naming Scheme
Naming: the glue of modules

## Slide 35: Naming in General
ipads.se.sjtu.edu.cn – hostname
steven@apple.com - email
steven – username
EAX - x86 processor register name
main() - function name
WebBrowser - class name
/courses/cse/index.html - path name (fully-qualified)
index.html - path name (relative)
http://ipads.se.sjtu.edu.cn/courses/cse/index.html - URL
13918275839- Phone number
202.120.40.188 - IP Address

## Slide 36: Naming a Disk
File name: /dev/sda1
  As a special type of inode: device inode
  8,0 as (major, minor)
PCI address (name): 19:00.0
  SCSI storage controller: LSI Logic / Symbios Logic SAS1068E PCI-Express Fusion-MPT SAS (rev 08)

## Slide 37: Naming for Modularity
Retrieval: e.g., using URL to get a web page
Sharing: e.g., passing an object reference to a function
  Save space as well: only sending the name, not the object
Hiding: e.g., using a file name without knowing file system
  Can support access control: use an object only if knowing its name
  E.g., Windows has many undocumented API
User-friendly identifiers: e.g., “homework.txt” instead of 0x051DE540
Indirection: e.g., OS can move the location of the file data without notifying the user
  Have you ever defragmented your hard driver?

## Slide 38: Addresses as Names
Software uses these names in an obvious way
  E.g., memory addresses
Hardware modules connected to a bus
  Use bus addresses (a kind of name) for interconnection

## Slide 39: Naming Schemes
A naming schemes contains three parts:
  1. Set of all possible names
    You cannot use ‘for’ as a variable in C
  2. Set of all possible values
  3. Look-up algorithm to translate a name into a value
    or a set of values, or “none”

## Slide 40: Naming Model

## Slide 41: Naming Terminology
Binding – A mapping from a name to value
  Unbind is to delete the mapping
  A name that has a mapping is bound
A name mapping algorithm resolves a name

## Slide 42: Naming Context
Type-1: context and name are separated
  E.g., inode number’s context is the file system
Type-2: context is part of the name
  E.g., xiayubin@sjtu.edu.cn
Name spaces with only one possible context are called universal name spaces
  Example: credit card number, UUID, email address

## Slide 43: Determining Context - 1
Hard code it in the resolver
  Examples: Many universal name spaces work this way
Embedded in name itself
  cse@sjtu.edu.cn:
    Name = “cse”
    Context = “sjtu.edu.cn”
  /ipads.se.sjtu.edu.cn/courses/cse/README :
    Name = “README”
    Context = “/ipads.se.sjtu.edu.cn/courses/cse”

## Slide 44: Determining Context - 2
Taken from environment (Dynamic)
  Unix cmd: “rm foo”:
    Name = “foo”, context is current dir
    Question: how to find the binary of “rm” command?
  Read memory 0x7c911109:
    Name = “0x7c911109”,
    Context is thread’s address space
Many errors in systems due to using wrong context

## Slide 45: Name Mapping Algorithms - 1
Table lookup
  Find name in a table
    E.g., Phone book
  Context: which table?
    Implicit VS. explicit
    Default context

## Slide 46: Name Mapping Algorithms - 2
Recursive lookup
  E.g., “/usr/bin/rm”
  First find “usr” in “/”, then find “bin” in “/usr”, then “rm”
  Each look-up process is the same
Multiple lookup
  Recall: how to find “rm” without absolute name?
  $PATH
    E.g., “/usr/local/sbin:/usr/local/bin:/usr/sbin:/usr/bin:/sbin:/bin”
  Look-up in a predefined list of context

## Slide 47: Interpreter Naming API
value ← RESOLVE(name, context)
  Return the mapping of name in the context
status ← BIND(name, value, context)
  Establish a name to value mapping in the context
status ← UNBIND(name, context)
  Delete name from context
list ← ENUMERATE(context)
  Return a list of all bindings
result ← COMPARE(name1, name2)
  Check if name1 and name2 are equal

## Slide 48: FAQ of Naming Scheme - 1
What is the syntax of names?
What are the possible value?
What context is used to resolve names?
Who specifies the context?
Is a particular name global (context-free) or local?

## Slide 49: FAQ of Naming Scheme - 2
Does every name have a value?
  Or, can you have “dangling” names?
Can a single name have multiple values?
Does every value have a name?
  Or, can you name everything?
Can a single value have multiple names?
  Or, are there synonyms?
Can the value corresponding to a name change over time?