## Slide 1: File System Review
Computer System Engineering, Fall 2019. (IPADS, SJTU)
Where are we now
Yubin Xia

## Slide 2: The Naming Layers of the UNIX FS (version 6)

## Slide 3: An Example: Find Blocks of "/programs/pong.c"

## Slide 4: Two Types of Links (Synonyms)
  Add link "assignment" to "Mail/new-assignment"
    Hard link
      No new file is created
      Just add a binding between a string and an existing inode
      Target inode reference count is increased
      If target file is deleted, the link is still valid
    Soft link
      A new file is created, the data is the string "Mail/new-assignment"
      Target inode reference count is not increased
      If target file is deleted, the link is not valid
Soft link can create cycle by SYMLINK("a", "a")
Notes: Here comes a demo~

## Slide 5: FAT File System
File allocation table (FAT)
  Organize files as linked lists
No inode
  File metadata: name & size
  Metadata are saved in dirs
Root dir at sector 0
Link? Permission?

## Slide 6: FAT (File Allocation Table) File System
File 31, Block 0
File 31, Block 1
File 31, Block 2
Disk Blocks
FAT
N-1:
0:
0:
N-1:
31:
file number
free
memory
File is collection of disk blocks
FAT is linked list 1-1 with blocks
File Number is index of root of block list for the file
File offset (o = < B, x > )
Follow list to get block #
Unused blocks  FAT free list

## Slide 7: File Cursor Sharing
3
115
index
Process A
fd_table
fd
3
116
index
Process B
fd
3
116
index
C is B's child
fd
Process A, B and C all open just one file with inode number 23
Process A and B open the same file, not share file cursor
Process B and C share the file cursor
23
128
23
240
...
inode num
file cursor
index
115
116
file_table
1
refcnt
2
Note: this refcnt is not the refcnt of inode!

## Slide 8: File Open & Read Timeline
open("/foo/bar", O_RDONLY)
Why "write" on bar inode in a read operation? Why no "write" on foo inodes?

## Slide 9: Layers: One Deeper Futher

## Slide 10: IDE Disk Driver using PIO
static int ide_wait_ready() {
while (((int r = inb(0x1f7)) & IDE_BSY) || !(r & IDE_DRDY))
; // loop until drive isn't busy
}
static void ide_start_request(struct buf *b) {
ide_wait_ready();
outb(0x3f6, 0); // generate interrupt
outb(0x1f2, 1); // how many sectors?
outb(0x1f3, b->sector & 0xff); // Block address here ...
outb(0x1f4, (b->sector >> 8) & 0xff); // ... and here
outb(0x1f5, (b->sector >> 16) & 0xff); // ... and here!
outb(0x1f6, 0xe0 | ((b->dev&1)<<4) | ((b->sector>>24)&0x0f));
if(b->flags & B_DIRTY){
outb(0x1f7, IDE_CMD_WRITE); // this is a WRITE
outsl(0x1f0, b->data, 512/4); // transfer data too!
} else {
outb(0x1f7, IDE_CMD_READ); // this is a READ (no data)
}
}
Address 0x1F0 = Data Port
Address 0x1F1 = Error
Address 0x1F2 = Sector Count
Address 0x1F3 = LBA low byte
Address 0x1F4 = LBA mid byte
Address 0x1F5 = LBA hi byte
Address 0x1F6 = 1B1D TOP4LBA: B=LBA, D=drive
Address 0x1F7 = Command/status
Status
Register
(0x1F7):
7: BUSY
6: READY
5: FAULT
4: SEEK
3: DRQ
2: CORR
1: IDDEX
0: ERROR
Error
Register
(0x1F1):
7: BBK
6: UNC
5: MC
4: IDNF
3: MCR
2: ABRT
1: T0NF
0: AMNF
BBK = Bad Block
UNC = Uncorrectable data error
MC = Media Changed
IDNF = ID mark Not Found
MCR = Media Change Requested
ABRT = Command aborted
T0NF = Track 0 Not Found
AMNF = Address Mark Not Found

## Slide 11: BUS: a hardware layer

## Slide 12: A Hardware Layer: the Bus

## Slide 13: Bus Features
A set of wires
  Comprising address, data, control lines that connect to a bus interface on each module
Broadcast link
  Every module hears every message
  Bus address: identify the intended recipient, as the name
Bus arbitration protocol
  Decide which module may send or receive message at any particular time
  Bus arbiter (optional): a circuit to choose which modules can use the bus

## Slide 14: Bus Transaction
Source module requires exclusive use of the bus: the data sender
Source module places a bus address of the destine module on the bus
Source module signals READY wire to alert the other module
The destine module singles ACKNOWLEDGE wire after copied the data
  If synchronized, then READY & ACKNOWLEDGE are not needed, just need to check the address lines on each clock cycle
Source module releases the bus

## Slide 15: Memory Load Example: LOAD 1742, R1
Processor #2 => all bus modules: {1742, READ, 102}

## Slide 16: Memory Load Example: LOAD 1742, R1
Memory 1 recognizes the address is within its range
  By examining just a few high-order address bits

## Slide 17: Memory Load Example: LOAD 1742, R1
Memory 1 acknowledges and processor 2 releases the bus
Memory 1 performs the internal operation to get the value
  value <- READ (1742)

## Slide 18: Memory Load Example: LOAD 1742, R1
Memory1 => all bus modules: {102, value}

## Slide 19: Memory Load Example: LOAD 1742, R1
Processor 2 is waiting for this result, just copies the data on the bus to its register R1

## Slide 20: Memory Load Example: LOAD 1742, R1
Processor 2 acknowledges and memory 1 releases the bus

## Slide 21: Sync VS. Async
Sync data transfer
  Source & destination cooperate through a shared clock
Async data transfer
  Source and destination cooperate through explicit signal line
    E.g., acknowledge line

## Slide 22: DMA on Bus

## Slide 23: DMA Example
BIOS
Memory
Disk
Processor 1
101
256-511
3072-4095
121-124
Processor #1 => all bus modules: {121, WRITE, 11742}
  Disk acknowledge and write the value 11742 to its control register
Processor #1 => all bus modules: {122, WRITE, 3328}
Processor #1 => all bus modules: {123, WRITE, 256}
Processor #1 => all bus modules: {124, WRITE, 1}
102
Processor 2

## Slide 24: DMA Example
BIOS
Memory
Disk
Processor 1
101
256-511
3072-4095
121-124
Disk => all bus modules: {3328, WRITE, data[11742]}
  Memory acknowledge and save data[11742]
Disk => all bus modules: {3329, WRITE, data[11743]}
... (loop)
Disk => all bus modules: {3583, WRITE, data[11997]}
102
Processor 2

## Slide 25: DMA Example
BIOS
Memory
Disk
Processor 1
101
256-511
3072-4095
121-124
When transferring is finished, disk controller SENDs message to the processor
  Just like keyboard controller does when press a key
Processor will enter interrupt handler next cycle
Now the processor knows that the DMA is done
102
Processor 2

## Slide 26: Summary

## Slide 27: Summary
CPU interacts with physical memory
  Through system bus that connects each other
  Using physical address to name memory content
CPU interacts with a device
  Also using physical address (aka., bus address)
  Polling, interrupt and DMA
  I/O instruction (PIO) or MMIO

## Slide 28: Summary
Processor
Memory
I/O Device
load/store
PIO (in/out)
/MMIO (load/store)
DMA
Memory Load/Store
  Between CPU and memory
  Physical memory address space
I/O Operations
  MMIO: map device memory and registers into physical address space
DMA
  Also using physical address

## Slide 29: Questions
Q: How are the physical addresses assigned?
  Memory physical addresses: by BIOS
  Some devices (e.g., keyboard, IDE): fixed for all time
  Other devices: assigned by the OS

## Slide 30: Questions
Q: Why not map the whole disk to memory?
  So that the CPU can access a byte on the disk directly by system bus
  1. Too large
  2. Too slow
The principle of least astonishment:
People are part of the system. The design should match the user's experience, expectations, and mental models
Q: now Intel's 3D-xpoint is 512GB memory, why disk?

## Slide 31: Crash Consistency

## Slide 32: An Example: Append a File
Inside of I[v1]:
  owner : yubin
  permissions : read-only
  size : 1
  pointer : 4
  pointer : null
  pointer : null
  pointer : null
Inside of I[v2]:
  owner : yubin
  permissions : read-only
  size : 2
  pointer : 4
  pointer : 5
  pointer : null
  pointer : null

## Slide 33: Bathtub Curve
  gross manufacturing defects
  accumulated ware and tear cause failure
  run for a while before shipping

## Slide 34: Availability
Counting the number of nines
  E.g. 99.9% has 3-nines availability
  Often used in marketing
Corresponding down time
  E.g. 3-nines -> 8 hour/year
  E.g. 5-nines -> 5 min/year
  E.g. 7-nines -> 3 sec/year
  Without any information about MTTF
More fine-grained
  Fail-soft, as in 8.3

## Slide 35: Systematically Applying Redundancy
Masking error
  Analog system designer: margin
  Digital system designer: redundancy
Outline
  Coding: incremental redundancy
  Replication: massive redundancy
  Voting
  Repair

## Slide 36: ALL_OR_NOTHING_PUT
if (data1 = data2) and (data2 = data3) return // State 1 or 7, no repair
if (data1 = data2)
CAREFUL_PUT (data1, all_or_nothing_sector.S3) return // State 5 or 6.
if (data2 = data3)
CAREFUL_PUT (data2, all_or_nothing_sector.S1) return // State 2 or 3.
CAREFUL_PUT (data1, all_or_nothing_sector.S2) // State 4, go to state 5
CAREFUL_PUT (data1, all_or_nothing_sector.S3 // State 5, go to state 7
Notes: The choice of which to use is arbitrary; as shown the procedure copies the new value in sector S1 to both sectors S2 and S3.

## Slide 37: RAID 5 (Spread Out the Parity)
Can recover from single-disk failure
Requires N+1 disks (not 2N)
Better performance if stripe a single file across multiple data disks
Writes are spread across disks

## Slide 38: Recovering FS Metadata from Crash
1. Synchronous meta-data update + fsck
  During check, synchronize metadata, such as file size
2. Soft update (FreeBSD fs modified on FFS)
  not covered in this course
3. Logging (ext 3/4), xv6-rev6 and following versions
  Before doing actual meta-data update, log the event
  After crash, recover from log

## Slide 39: Problem of fsck: Too Slow
How long would fsck take?
  an example server: fsck takes 10 minutes per 70GB disk w/ 2 million inodes
  clearly reading many inodes sequentially, not seeking
  still a long time, probably linear in disk size
Consider the example before:
  Scan the disk for only three disk block writes
  Just like find a key by searching the entire house

## Slide 40: Barrier: Flush the Disk
Disk's write buffer
  Disk will inform the OS the write is complete when it simply has been placed in the disk's memory cache
  But the data is not on disk yet! No durability! No order!
One solution: disable the buffer
Another solution: using flush operation
  Force the disk to write data to disk media
  Aka., disk write barrier
However, disks may not do as they claim…
  Some disks just ignore the flush operation to be faster
  "the fast almost always beats out the slow, even if it is wrong" --- Kahan

## Slide 41: Logging / Journaling

## Slide 65: Journaling without ordering