## Slide 1: Introduction to Network
Computer System Engineering, Fall 2019. (IPADS, SJTU)
As a component, and as a system itself
Yubin Xia

## Slide 2: Layers in Network
Application
  Can be thought of as a fourth layer
  Not part of the network
End-to-end layer
  Everything else required to provide a comfortable application interface
Network layer
  Forwarding data through intermediate points to the place it is wanted
Link layer
  Moving data directly from one point to another

## Slide 3: OSI, TCP/IP & Protocol Stack
7th Application Layer
6th Presentation Layer
4th Transport Layer
3th Network Layer
2nd Link Layer
1st Physical Layer
Application Layer
HTTP
TCP
Ethernet
UDP
IP
PPP
…
SMTP
POP3
FTP
…
ICMP
ARP & RARP
Transport Layer
5th Session Layer
Network Layer
Link Layer
End-to-end Layer
Network Layer
Link Layer
OSI
TCP/IP
CSE
WiFi
Fiber
TD-LTE
FDD
…

## Slide 4: The Internet "Hour Glass" Protocols
More people, more useful
  Value to me = N
  Value to society is N2
Network, dumb vs. smart
  Standardize vs. flexibility
Network is a black box
  Simplify the system that uses it
Notes: The more people that use a network, the more useful it is for everybody.
Value to me is proportional to N people using the same net.
Value to society is proportional to N^2.

## Slide 5: Packet Encapsulation
22Bytes
20Bytes
20Bytes
4Bytes
64 to 1500 Bytes

## Slide 6: Application Layer
Entities
  Client and server
  End-to-end connection
Name space: URL
Protocols
  HTTP, FTP, POP3, SMTP, etc.
What to care?
  Content of the data: video, text, …
<html>
<head>
<title>Google</title>
<script>window.google=…..
</script>
</head>
<body> … </body>
</html>

## Slide 7: Transport Layer
Entities
  Sender and receiver
  Proxy, firewall, etc.
  End-to-end connection
Name space: port number
Protocols: TCP, UDP, etc.
What to care?
  TCP: Retransmit packet if lost
  UDP: nothing

## Slide 8: Packet Format of TCP & UDP

## Slide 9: Network Layer (the Internet Layer, IP Layer)
Network entities
  Gateway, bridge
  Router, etc.
Name space
  IP address
Protocols
  IP, ICMP (ping)
What to care?
  Next hop decided by route table

## Slide 10: IP Datagram (Packet, Package)
Header
10101011101010101010010101010100101010100
11010010101010010101111111010000011101111
10100001011101010100110101011110100000101
00100000000010101000011010000111111010101
......... 1011011001010100011001001010110
Data

## Slide 11: IP Route Table

## Slide 12: Link Layer (& Physical Layer)
Network entities
  Hub, switcher, etc.
  Twisted line, cable line, etc.
Name space
  No name needed
Protocols
  Ethernet, ATM, etc.
  ARP, RARP, etc.
What to care?
  Physical transfer, error detection, etc.

## Slide 13: Frame Format of Ethernet

## Slide 14: TCP/IP Architecture
Application
Transport
Internet
Network Interface
Application
Transport
Internet
Network Interface
Internet
Network Interface
Network 1
Network 2
Machine A
Machine B
Router/Gateway
Notes: Transfer of information across networks through gateways/routers
Corresponding to OSI network layer: routing and congestion control
Global unique IP address and IP packets
Best-effort connectionless IP packet transfer: no setup, routed independently, robust, out of order, duplicate, or lose of packet

## Slide 15: TCP/IP Architecture
Each layer adds/strips off its own header
Each layer may split up higher-level data
Each layer multiplexes multiple higher layers
Each layer is (mostly) transparent to higher layers

## Slide 16: Link Layer
From a node to its physical neighbor

## Slide 17: The Link Layer
The bottom-most layer of the three layers
Purpose: moving data directly from one physical location to another
1. Physical transmission
2. Multiplexing the link
3. Framing bits & bit sequences
4. Detecting transmission errors
5. Providing a useful interface to the up layer

## Slide 18: Physical Transmission using Shared Clock
Example-1: moving a bit from register-1 to register-2 on the same chip
  Run a wire to connect output of reg-1 to input of reg-2
  Wait till reg-1's output has settled & signal has propagated to reg-2
  Reg-2 read input the next clock tick
  Assumption: propagation can be done within one clock
How to send data between two modules without sharing a clock?

## Slide 19: Physical Transmission without Shared Clock
Three-wire ready/acknowledge protocol
  1. A places data on data line
  2. A changes value on the ready line
  B sees the ready line change, reads value on the data line, then changes the acknowledge line
B: when to look at the data line? (ready is set)
A: when to stop holding the bit value on the data line? (ack is set)

## Slide 20: Parallel Transmission
Propagation time ∆t
  It takes more than 2x∆t to send one bit
  The max data rate is 1/(2∆t)
Parallel transmission
  Use N parallel data lines to achieve N/(2∆t)
  E.g., SCSI, printer, etc.

## Slide 21: Serial Transmission
Ready/acknowledge protocol
  ∆t grows significantly, which limits the data rate
Serial transmission
  Send a stream of bits down a single line
  Without waiting for any response from the receiver
  Expect the receiver can recover the bits with no additional signal
  Higher rates, longer distance, fewer wires
  E.g., USB, SATA

## Slide 22: Signal Transmission on Analog Line
It is hard for B to understand the signal
  B doesn't have a copy of A's clock, so when to sample the signal?

## Slide 23: VCO: Voltage Controlled Oscillator
How to make two ends agree on the data rate without clock line?
The receiver run a VCO at about the same data rate
  VCO's output is multiplied by the voltage of incoming signal
  The product is suitably filtered and sent back to adjust the VCO
  VCO will finally be locked to both the frequency and phase of the arriving signal: phase-locked loop
  Then the VCO becomes a clock source for the receiver
Problem: if no transition in the stream (e.g., a lot of zero), the phase-locked loop cannot synchronize

## Slide 24: Manchester Code
Solution: sender encodes the data to ensure transitions
Phase encoding: at least 1 level transition for a bit
  Manchester code: 0 -> 01, 1 -> 10
  Max data rate is only half, but simple enough
Manchester
Encoding
Polar NRZ
1
0
1
0
1
1
0
0
1

## Slide 25: How to Share a Connection?
Isochronous communication (telephone communication)
  Needs prior arrangement between switches
  Connection: set up and tear down
  Stream: continuous bits flows out of a phone
Asynchronous communication (data communication)
  Message: burst, ill-suited to fixed size and spacing of isochronous frames
  Connectionless, asynchronous

## Slide 26: Isochronous Multiplexing
Telephone network
  Leverage "virtual link" for connection
  "network is busy" when no available time slot

## Slide 27: Isochronous - TDM
64 Kbps each phone, 45 Mbps link
8-bit block (frame), 8000 frames per second
5624 bit times or 125 us
703 simultaneous conversations (what if there is a 704th calling?)
Q: Why the voice is still continuous, instead of fragmented?

## Slide 28: Data Communication Network
Data communication network usually contains burst communication
Different from the telephone network

## Slide 29: Frame and Packet: Asynchronous Link
Frame can be of any length, carried at any time that the link is free
Packet: a variable-length frame with its guidance info
Connectionless transmission: no state maintained
Segment and reassemble
Packet voice: replacing many parts of isochronous network

## Slide 30: Multiplexing / Demultiplexing
Multiplex using a queue: switch need memory/buffer
Demultiplex using information in packet header
  Header has destination
  Switch has a forwarding table that contains information about which link to use to reach a destination
Switch

## Slide 31: Framing Frames
Where a frame begins and ends
Independent from framing bits
  Some model separates link layer to 2: one for bits and one for frames
Simple method
  Choose a pattern of bits, e.g., 7 one-bits in a row, as a frame-separator
  Bit stuffing: if data contains 6 ones in a row, then add an extra bit (0)

## Slide 32: Error Handling
Error detection code
  Adding redundancy: e.g., checksum at the end
What to do if detect an error
  Error correction code: with enough redundancy
    Where noise is well understood, e.g., disk
  Ask sender to resend: sender holds frame in buffer
  Let receiver discard the frame
  Blending these techniques

## Slide 33: Coding: Incremental Redundancy
Forward error correction
  Perform coding before storing or transmitting
  Later decode the data without appealing to the creator
Hamming distance
  Number of 1 in A ⊕ B , ⊕ is exclusive OR (XOR)
  If H-distance between every legitimate pair is 2
    000101, can only detect 1-bit flip
  If H-distance between every legitimate pair is 3
    Can only correct 1 bit flip
  If H-distance between every legitimate pair is 4
    Can detect 2-bit flip, correct 1-bit flip

## Slide 34: Example-1: Simple Parity Check
2 bits -> 3 bits
  Detect 1-bit errors
  8 patterns total
Only 4 correct patterns
  00 -> 000
  11 -> 110
  10 -> 101
  01 -> 011
Hamming distance of this code is 2
  1-bit flipping will cause incorrect pattern

## Slide 35: Example-2: 4-bit -> 7-bit
4 bits -> 7 bits (56 using only extra 7)
  3 extra bits to distinguish 8 cases
  e.g. 1101 -> 1010101
Correct 1-bit errors
  1010101 -> 1010001 : P1 & P4 not match
  1010101 -> 1110101 : P2 not match
1
1
0
1
0
1
0
1
1
0
1
0
1
0
1
1
0
1
0
1
0
Not Match | Error
None | None
P1 | P1
P2 | P2
P4 | P4
P1 & P2 | P3
P1 & P4 | P5
P2 & P4 | P6
P1 & P2 & P4 | P7
1 2 3 4 5 6 7