## Slide 1: System Performance - 2
Computer System Engineering, Fall 2019. (IPADS, SJTU)
Fighting bottlenecks
Yubin Xia

## Slide 2: Review: How to Improve Performance
Step-1. measure the system, and compare it to our system model, to find the bottleneck
Step-2. relax the bottleneck

## Slide 3: Review: Performance Metrics
Computer Systems can be viewed as interconnected modules
★ Capacity
★ Latency
★ Throughput
★ Utilization

## Slide 4: Review: Latency & Throughput
When processing is serial:
Throughput = 1 / (Latency)
When processing is parallel:
Throughput has no direct relationship with latency
How to improve throughput? Reduce latency & Increase paralleling

## Slide 5: Review: Improving Performance at 3 Layers
Get faster hardware
Fix application: better algorithm, fewer features (not in CSE)
General system optimization techniques:
  Batching
  Caching
  Concurrency
  Parallelism (scheduling)
Hardware
System
Application

## Slide 6: Fighting Bottlenecks

## Slide 7: Why Performance Bottleneck?
1. Physical limitation
  Speed of light
  The capacity of memory
  …
2. Sharing
  Several users share a device
  Several clients share a server

## Slide 8: How to Improve Performance?
1. Measure the system to find the bottleneck
2. Relax the bottleneck
  Batch requests
  Cache data
  Exploit concurrency
  Exploit parallelism (by scheduling)

## Slide 9: Batching
Frequently it is possible to group requests for more efficiency
  Amortize overheads of processing
  Schedule requests for better performance
Examples: N messages vs. one message with N requests Disks:
  Always transfer a bunch of bytes (sector or block)
  Schedule the disk motions

## Slide 10: Caching
Use knowledge of workload: memory abstractions
  Keep common requests in a fast local memory
  Check the local memory every access
CPU cache – Cache 1ns, Memory 100ns, 90% hit rate
  AverageLatency = 0.9 x 1ns + 0.1 x 100ns = 10.9 ns (100ns -> 10.9ns)
Used everywhere there are memory abstractions
  Processors, file systems, TLBs, browsers, DNS, etc.

## Slide 11: Memory Hierarchy
Intel Core-i5 Memory Architecture

## Slide 12: Dallying
Procrastination sometimes helps
  Temp files – deleted before written to disk
Examples:
  Caches – Write back policy: write absorption
  Database transactions – group commit
    Might hold your ATM request until others arrive to do batching

## Slide 13: Speculation
Guessing at an operation and performing it ahead a time
  Need to be able to undo changes if wrong
Examples:
  Processors guess at branches, memory access
  File systems guess at next file block needed (prefetching)
  Easier if space of possibilities is small
  Branch prediction versus value prediction

## Slide 14: Speculative Execution in CPU
This is the process of executing an instruction in anticipation that it might be used
  This provides instruction level parallelism
For instance in a conditional statement, both the instructions in a condition might be executed
Depending on the condition, only one of the execution is retired or committed
  The other instruction is flushed from the pipeline
Tomasulo algorithm describes these details

## Slide 15: Out-of-order Execution
Multiple instructions executed regardless of the actual program order
  lw $3, 100($4) in execution, cache miss
  sub $5, $6, $7 can execute during the cache miss
  add $2, $3, $4 waits until the miss is satisfied
The instructions are fetched, decoded and prepared for execution and pushed into a reservation station
Those instructions without data dependencies will execute in no specific order
  Others will stall until dependency is satisfied (resolving data hazards)

## Slide 16: Challenges
Batching, dallying, and speculation introduce complexity
  They introduce concurrency
  Coordination is difficult to get right

## Slide 17: Case: I/O Bottleneck

## Slide 18: The I/O Bottleneck
Bits read from a disk encounter two potential transfer rate limits:
  The rate at which bits spin under the heads on their way to a buffer
  The rate at which the I/O channel or I/O bus can transfer the contents

## Slide 19: The I/O Bottleneck
Average seek latency: about 8 milliseconds
  Time to move the head over 1/3 of the disk
The average rotational latency: 4.17 milliseconds
  The disks spin at 7200 rotations/minute
  One rotation every 8.33 milliseconds (60/7200)
  On average, the disk has to wait a half rotation for the desired block to be under the disk head

## Slide 20: A Typical Modern 400 Gigabyte Disk
Has 16,383 cylinders, or about 24 megabytes per cylinder
Would have 8 two-sided platters and thus 16 read/write heads
Would be 24/16 = 1.5 megabytes per track
When rotating at 7200 revolutions per minute (120 per second)
The bits will go by a head at 180 megabytes per second (1.5 x 120)

## Slide 21: Bottleneck
The IDE bus: 66 MB/S is common
The Serial ATA-3 bus: 6 Gbps
With IDE bus: The electronics would be the bottleneck
  at 66 MB/S
With SATA-3 bus: The mechanics would be the bottleneck
  at 180 MB/S

## Slide 22: Latency of 4-KB Data Accessing (Using IDE)
The latency of reading a 4 kilobyte block chosen at random:
avg seek time + avg rotation latency + transmission of 4 kilobytes
  = 8 + 4.17 + (4 / (66 × 1024)) × 1000 milliseconds
  = 8 + 4.17 + 0.06 milliseconds
  = 12.23 milliseconds
The throughput for reading randomly-chosen blocks one by one is:
  = 1000/12.23 × 4 kilobytes per second
  = 327 kilobytes/second

## Slide 23: Round-1: No Optimization
1 in ← OPEN ("in", READ) // open "in" for reading
2 out ← OPEN ("out", WRITE) // open "out" for reading
3
4 while not ENDOFFILE (in) do
5 block ← READ (in, 4096) // read 4 kilobyte block from in
6 block ← COMPUTE (block) // compute for 1 millisecond
7 WRITE (out, block, 4096) // write 4 kilobyte block to out
8 CLOSE (in)
9 CLOSE (out)
reading 4 kilobyte + 1 millisecond of computation + writing 4 kilobyte
  = 12.23 + 1+ 12.23 milliseconds
  = 25.46 milliseconds

## Slide 24: Round-2
Modify the file system
  to layout the blocks of a file contiguously
  to prefetch an entire track of data on each read
Average seek time + 1 rotational delay
  = 8 + 8.33 milliseconds = 16.33 milliseconds

## Slide 25: Round-2
File system issues 1 read request per 384 (1.5 MB per track / 4 KB) loop iterations
The average time for 384 iterations is:
reading 1536 kilobyte + 384× (1 millisecond of computation + writing 4 kilobyte)
  = 16.33 + 384 × (1 + 12.23) millisecond
  = 16.33 + 5080.32 milliseconds
  = 5096.65 milliseconds
Thus, the average time for a loop iteration is 5096.65/384 = 13.27 milliseconds

## Slide 26: Round-3
Improve by dallying & batching write requests
Write to buffer in RAM and flush when buffer is full
Latency = (16.33 + 384 + 16.33)/384 milliseconds
= 1.09 milliseconds

## Slide 27: Round-4
Prefetch the next track before the 385th READ
Overlap computation and I/O completely
The average time around the loop is 1 millisecond
The bottleneck now is the CPU

## Slide 28: Cache Policies
Multi-level Memory

## Slide 29: Analyzing Multilevel Memory Systems
Only consider the adjacent pair of levels
  View it as a two level multilevel memory system
  The 1st is primary device, the 2nd is secondary device

## Slide 30: Locality of Reference and Working Sets
In many situations most memory references are to a small set of addresses for significant periods of time
As the application progresses, the area of concentration of access shifts, but its size still typically remains small
Called "locality of reference"
  Temporal locality and spatial locality
  Thrashing: repeated movement of data back and forth between two levels

## Slide 31: Multilevel Memory Management Policies
Each level of multilevel memory system can be characterized by 4 items
  The string of references directed to that level
  The bring-in policy for that level
  The removal policy for that level
  The capacity of the level

## Slide 32: Page-removal Policies
First-in, first-out (FIFO) page-removal policy
  Remove the page that has been in the primary device the longest
Belady's anomaly
  Performance drops with a larger primary device capacity!
Optimal (OPT) page-removal policy
  Choose for removal the page that will not be needed for the longest time
Least-recently-used (LRU) page-removal policy
  The page in the primary device that has not been used for the longest time

## Slide 33: First-in, First-out (FIFO) Page-Removal Policy
The page for removal is the one that has been in the primary device the longest

## Slide 34: Belady's Anomaly
Increase of missing-page exception numbers with a larger primary device capacity

## Slide 35: Stack Algorithms
Subset property
  For the optimal policy, at all times, the pages it keeps in the 3-page memory is a subset of that it keeps in the 4-page memory
No Belady's anomaly if subset property holds
  At all times and for every possible capacity of primary device, it creates a total ordering for pages at a given time

## Slide 36: OPT (Optimal) Page-Removal Policy
Always choose for removal the page that will not be needed for the longest time

## Slide 37: LRU
It is confirmed as an error, in errata part I.
Notes: It is confirmed as an error, in errata part I.

## Slide 38: Least-recently-used (LRU) Page Removal Policy
A program that runs from top to bottom
  the virtual memory that is larger than primary device
LRU: always evicts exactly the wrong page
Most-recently-used (MRU) page-removal policy

## Slide 39: Comparative Analysis of Different Policies
Ways of deciding the following two things:
  How large the primary memory device should be?
  Which page removal policy to use?
Collecting traces of the reference strings of typical programs
Simulate the multilevel memory manager with:
  Different configurations - Size of primary device
  Page removal policy - Traces of memory access

## Slide 40: Stack Algorithms for LRU
It can perform a simulation for all possible primary memory size with a single pass through a given reference string

## Slide 41: Efficiency of Page-Removal Policies
Clock page-removal algorithm
  Base on a hardware setting bit
  Reference bit
  Move clockwise
  If T, set F
  Choose as the victim otherwise
Random removal policy
  For TLB
Directed mapping

## Slide 42: Scheduling

## Slide 43: Scheduling
Algorithm that assigns requests to resources
Processor time – Threads
Physical memory – Address spaces
Printers – Printer jobs
Disks – Disk requests
Networks – Packets
Memory bus – Memory requests

## Slide 44: Challenges of Scheduling
Easy, if number of requests ≤ resources
Difficulty: Lack of information
  Packet scheduling and streaming media
Difficulty: Lack of mechanism to enforce policies
  Give high priority to CPU, but can't get to disk or network
Difficulty: Getting mechanism right
  Many schedulers break rather than gracefully degrade under load

## Slide 45: Example: Livelock under Overload
Web news server overloaded
  Most of the time is spend to handle interrupt and drop requests
  No progress at all!

## Slide 46: The Ideal Scheduler
Mini latency: How long a service takes? E.g., Move mouse, cursor moves
Max throughput: Max jobs / time. E.g., Web server pages/second
Low overheads: Scheduler doesn't use any resources
Fairness: everyone gets to make progress, no one starves
Scales linearly up to capacity: Graceful handling of overload
System-level goal may conflict with the needs of individual threads
  System: minimal preemption
  Apps: finish as soon as possible

## Slide 47: Measuring the Request's Response
Turn-around time: The length of time from when a request arrives at a service until it completes
Response time: The length of time from when a request arrives at a service until it starts producing output
Waiting time: The length of time from when a request arrives at a service until the service starts processing the request

## Slide 48: First Come First Server (FCFS)
Fairness paramount
Good for printer scheduler

## Slide 49: First Come First Server (FCFS)
For the processor
  One thread that periodically waits for I/O but mostly computes
  Several threads that perform mostly I/O operations
For the scheduler
  It runs the I/O-bound threads first
  Then runs the computation intensive thread
  All quickly finished computations and waiting for I/O

## Slide 50: Convoy Effect
When I/O devices are idle
  The I/O-bound threads will quickly finish computations and start I/O
  The processor-bound thread will run for a long time
  I/O-bound operations will finish I/O and queuing for computation
  All the I/O devices will become idle!
When processor is idle
  The processor-bound thread finishes computation and starts I/O
  The I/O-bound threads will quickly finish computations and start I/O
  Processor will become idle!
CPU
Device

## Slide 51: Shortest-Job-First
Chooses the job that has the shortest expected run time
Require a prediction of the running time of a job before running
Starvation: several short jobs makes a long job starve

## Slide 52: Round-Robin
Select the first job from queue as in the first-come first-serve policy
Stop the job after some period of time, and select a new job

## Slide 53: Comparing the Three Policies
Wait time before start
Wait time till done
Amount of work: A:3, B:5, C:2

## Slide 54: Priority Scheduling Policy
Priority Scheduling Policy
  Assign each job a priority number (static vs. dynamic)
  Select the job with the highest priority number
  Must have some rule to break ties
Modern CPU schedulers have
  Priorities: Run job with the highest priority
  Round Robin: Alternate among jobs of same priority, preempt a job if it holds CPU too long

## Slide 55: CPU Scheduling Policy
Assign priorities to jobs
  Give high priorities to I/O-bound jobs
  Give low priorities to CPU-bound jobs
  Handles I/O-bound and CPU-bound jobs nicely

## Slide 56: CPU Scheduling Policy
Challenge: distinguish I/O-bound and CPU-bound
Look at past behavior to predict the future
  Linux: Priority of job is function of amount of CPU it has used
Counterintuitive:
  More CPU a job uses/needs, the lower its priority
  The less CPU it uses, the higher its priority
  Avoids starvation problems: Not running gives task a higher priority

## Slide 57: The Priority Inversion Problem
Problem: what if a high priority thread waits for a low priority one which holding a lock?
Solution: priority inheritance

## Slide 58: Real-Time Scheduling
Missed deadline = incorrect behavior
Soft real time: Display video frame every 30th of sec
Hard real time: "apply-breaks" process in your car
Scheduling more than one thing: memory, network bandwidth, CPU all at once

## Slide 59: Earliest Deadline First (EDF)
Keep the queue of jobs sorted by deadline
Run the first of the queue
Minimize the total lateness of all the jobs
How to know deadline?
  Specified by tasks themselves
  In the form of (C, P), C for second, P for period
  The scheduler rejects new task if sum(Ci/Pi) > 1

## Slide 60: Disk Scheduling: Goals
Minimize time spent waiting on disk mechanisms
  Moving the disk arm
  Waiting for sector to rotate under disk heads
Fairness
  Should not make requests wait too long

## Slide 61: Disk Scheduling
First-come first-serve
Elevator Algorithm

## Slide 62: Disk Scheduling
Shortest-Seek-First
Elevator Algorithm

## Slide 63: Performance VS. Security

## Slide 64: Cache Side Channel
Infer data by memory access time!
if (x)
mov %eax a[0];
else
mov %eax a[1];

## Slide 65: The Meltdown Vulnerability
An inaccessible kernel address is moved to a register, raising an exception.
Subsequent instructions are executed out of order before the exception is raised, leaking the data from the kernel address through the indirect memory access.

## Slide 66: The Meltdown Vulnerability
key = 0x01
Kernel
User
Mapped with kernel privilege in page table
Access key
Permission Error!

## Slide 67: Meltdown
key = 0x01
Kernel
User
Mapped with kernel privilege in page table
Meltdown
Can access key!

## Slide 68: Meltdown
key = 0x01
Kernel
User
CPU
Instruction
Effect
Cache
Memory
Meltdown

## Slide 69: Meltdown
key = 0x01
Kernel
User
CPU
Load key, %rax
%rax = 1
Instruction
Effect
Reorder
Execution
Permission Error!
1
2
Cache
Memory
buf
(Attack buffer)
Meltdown
… | buf[0] | buf[1] | buf[2] | … | buf[n] | …
Load buf[%rax], %rbx
Access buf[1]
Key = 1

## Slide 70: Meltdown
Rollback status
w/o cache status!
key = 0x01
Kernel
User
CPU
Load key, %rax
%rax = 1
Instruction
Effect
Reorder
Execution
Permission Error!
1
2
Cache
Memory
buf
(Attack buffer)
Meltdown
Key = 1
buf[1]
… | buf[0] | buf[1] | buf[2] | … | buf[n] | …
Load buf[%rax], %rbx
Access buf[1]
3
Exception
Access
buf[1]
Fill buf[1]
to cache
2
2

## Slide 71: Meltdown
Rollback status
w/o cache status!
key = 0x01
Kernel
User
CPU
Load key, %rax
%rax = 1
Instruction
Effect
Reorder
Execution
Permission Error!
1
2
Cache
Memory
buf
(Attack buffer)
Meltdown
Key = 1
buf[1]
… | buf[0] | buf[1] | buf[2] | … | buf[n] | …
Load buf[%rax], %rbx
Access buf[1]
3
Access
buf[1]
Fill buf[1]
to cache
2
2
Exception
Attacker finds that buf[1] is in the cache, so that key equals to 1!