## Slide 1: Fault Tolerant
Computer System Engineering, Fall 2020 (IPADS, SJTU)
Building reliable system from unreliable components
Yubin Xia

## Slide 2: Review: Atomicity: All-or-Nothing
An action is atomic if happens completely or not at all
  Atomicity makes it much easier to reason about failures
  Need to think about the consequences of the action happening or not happening, but not about the action partially happening

## Slide 3: Review: Commit Point

## Slide 4: Review: Shadow Copy
Does the shadow copy approach work in general?
  + Works well for a single file
  - Hard to generalize to multiple files or directories
    Have to place all files in a single directory, or rename subdirs
  - Requires copying the entire file for any (small) change
  - Only one operation can happen at a time
  - Only works for operations that happen on a single computer, single disk

## Slide 5: Review: Transaction Terminology
xfer(bank, a, b, amt):
begin
bank[a] = bank[a] – amt
bank[b] = bank[b] + amt
if bank[a] < 0:
abort //Not enough funds
else:
commit
xfer(bank, a, b, amt):
begin
write (a, read(a) – amt)
write (b, read(b) – amt)
if read (a) < 0:
abort //Not enough funds
else:
commit
Notes: not everything can be a transaction.

## Slide 6: Review: Read & Write with Cache
recover(log):
commits = {}
for record r in log[len(log)-1] .. log[0]:
if r.type == commit:
commits.add(r.tid)
if r.type == update and r.tid not in commits:
cell_write(r.var, r.old_val) // undo
for record r in log[0] .. log[len(log)-1]:
if r.type == update and r.tid in commits:
cell_write(r.var, r.new_value) // redo
Cell Storage
A 110
B 70
+-------+------+--------+-------+------+--------+-------+
TID | T1 | T1 | T1 | T2 | T2 | T2 | T3 |
OLD | A=0 | B=0 | | A=100 | B=50 | | A=80 |
NEW | A=100 | B=50 | COMMIT | A=80 | B=70 | COMMIT | A=110 |
+-------+------+--------+-------+------+--------+-------+
Cache
A 110
B 70

## Slide 7: Magnetic Disk Fault Tolerance

## Slide 8: Magnetic Disk Fault Tolerance
Using disk as durable storage
  Low cost, large capacity, non-volatility
  Internal power can prevent data loss at power-off
Three/four nested layers
  Raw storage, fail-fast storage, careful storage
  Optional: durable storage

## Slide 9: Magnetic Disk Fault Modes
Mechanical wear and tear
A bumping may cause a head to hit the surface
  Head crush may also create cloud of dust
  Results in several sectors decaying: decay set
Electronic components in the controller age
  E.g. clock timing and signal detection circuits
  Cause previously good data to become unreadable, or bad data to be written
  Soft or hard errors
Seek error
  Arm moves to a wrong track

## Slide 10: ALL_OR_NOTHING_PUT
procedure ALMOST_ALL_OR_NOTHING_PUT (data, all_or_nothing_sector)
CAREFUL_PUT(data, all_or_nothing_sector.S1)
CAREFUL_PUT (data, all_or_nothing_sector.S2)
CAREFUL_PUT (data, all_or_nothing_sector.S3)
procedure ALL_OR_NOTHING_GET (reference date,all_or_nothing_sector)
CAREFUL_GET (data1, all_or_nothing_sector.S1)
CAREFUL_GET (data2, all_or_nothing_sector.S2)
CAREFUL_GET (data3, all_or_nothing_sector.S3)
if (data1 = data2) data ← data1
else data ← data3
Notes: Why "Almost"?
- Not repair previous damage

## Slide 11: ALL_OR_NOTHING_PUT
procedure ALL_OR_NOTHING_PUT (data, all_or_nothing_sector)
CHECK_AND_REPAIR (all_or_nothing_sector)
ALMOST_ALL_OR_NOTHING_PUT (data, all_or_nothing_sector)
procedure CHECK_AND_REPAIR (all_or_nothing_sector) // Ensure copies match
CAREFUL_GET (data1, all_or_nothing_sector.S1)
CAREFUL_GET (data2, all_or_nothing_sector.S2)
CAREFUL_GET (data3, all_or_nothing_sector.S3)

## Slide 12: ALL_OR_NOTHING_PUT
if (data1 = data2) and (data2 = data3) return // State 1 or 7, no repair
if (data1 = data2)
CAREFUL_PUT (data1, all_or_nothing_sector.S3) return // State 5 or 6.
if (data2 = data3)
CAREFUL_PUT (data2, all_or_nothing_sector.S1) return // State 2 or 3.
CAREFUL_PUT (data1, all_or_nothing_sector.S2) // State 4, go to state 5
CAREFUL_PUT (data1, all_or_nothing_sector.S3 // State 5, go to state 7
Notes: The choice of which to use is arbitrary; as shown the procedure copies the new value in sector S1 to both sectors S2 and S3.

## Slide 13: Durable Storage: RAID 1
Tolerate error
  Hard errors reported by careful layer are masked by reading from other replicas
Untolerated error
  Decay on the same sector of all the replicas, status = BAD
  OS crashes during a DURABLE_PUT
  Decay in a way that is undetectable
Redundant Array of
Independent Disks

## Slide 14: Improving on RAID-1
Clerk: periodically checks for decays
  Td as the period, must short enough
Tolerated error
  Hard errors reported by careful layer are masked by reading from one of the other replicas
  Data of a single decay set decays, is discovered by the clerk, and is repaired, all within Td of the decay event
Untolerated error
  The OS crashes during DURABLE_PUT
  All decay sets fail with Td
  The data of some sector decays in a way undetectable

## Slide 15: RAID 4 (Dedicated Parity Disk)
Can recover from single-disk failure
Requires N+1 disks (not 2N)
Performance benefits if stripe a single file across multiple data disks
- All writes hit the parity disk

## Slide 16: RAID 5 (Spread Out the Parity)
Can recover from single-disk failure
Requires N+1 disks (not 2N)
Better performance if stripe a single file across multiple data disks
Writes are spread across disks

## Slide 17: Question
Q: Can RAID solve the crash consistency problem in the beginning of this lecture?
  No. There is a semantic gap between block layer and file layer: block layer cannot tell metadata and data

## Slide 18: Disk Failure Prediction
Predictive Failure Analysis (PFA)
  By IBM at first, in 1992
  For monitoring the likelihood of hard disk drives to fail
Disk PFA: Measuring several key parameters
  E.g., the flying height of heads
  The drive firmware compares the measured parameters against predefined thresholds
  If the drive appears likely to fail soon, the system sends notification to the disk controller
https://en.wikipedia.org/wiki/Predictive_failure_analysis

## Slide 19: Fault Tolerance
" It's good to learn from your mistakes. It's better to learn from other people's mistakes."
- Warren Buffett

## Slide 20: War Stories: MAXC & Alto
MAXC
A time-sharing computer system
  Using Intel 1103: 1KB memory
Fault tolerant
  Extra bits for each 36-bit
  Single-error-correction
  Double-error-detection
Result
  Solidly reliable
  No errors were reported
Alto
A personal workstation
  Using the same Intel memory chip
Fault tolerant
  One parity bit for each 16-bit
  Error-detection only
Result
  Frequent memory-parity failures!
  1. Bit-map display: Bravo
  2. Pattern-sensitive 1103

## Slide 21: War Stories: MAXC & Alto
Lesson-1:
  There is no such thing as a small change in a large system
  A new software can bring down previously working hardware
  You are never quite sure just how close to the edge of the cliff you are standing
Lesson-2:
  Experience is a primary source of information about failures
  It is nearly impossible, without specific prior experience, to predict what kinds of failures you will encounter in the field

## Slide 22: War Stories: MAXC & Alto, Chap-2
Back to MAXC: why so few errors at that time?
  Hardware reports both corrected errors and uncorrectable errors
  But software only logged uncorrectable errors!
Lessons
  Safety margin principle is important when system implement automatic error masking
  Otherwise, you may be standing on the edge again

## Slide 23: War Stories: MAXC & Alto, Chap-3
New machine: Alto-2
  Using new memory chip with 4096 bits
  Single-error-correction, double-error-detection, again, flawlessly!
  Two years later, an implementation mistake is discovered
  Neither error correction nor detection was working on 1/4 cards!
Lessons
  Never assume the h/w does as it says in the spec
  It is harder than it looks to test the FT features of a FT sys
  Just because it seems to be working does not mean it actually is

## Slide 24: Nowadays
Memory chip does become better
  Errors often do not lead to failures
  Bit-flip can be benign
But there are still errors
  Sometimes, failure is blamed on something else
  You never know it h/w error or s/w error

## Slide 25: Fault, Error, Failure
Basic Concepts

## Slide 26: Fault, Error, Failure
Fault can be latent or active
  If active, get wrong data or control signals
Error is the results of active fault
  E.g. violation of assertion or invariant of spec
  Discovery of errors is ad hoc (formal specification?)
Failure happens if an error is not detected and masked
  Not producing the intended result at an interface

## Slide 27: Failure in System and Subsystem
The failure of a subsystem is a fault of a system
  The fault may cause an error that leads to the failure of the larger subsystem
  Unless the larger subsystem detects the error and masks it
Examples
  A flat tire -> detects the error by failure of a subsystem
  Miss an appointment -> the person notices a error
  Change to a spare tire -> masked the error

## Slide 28: Different Types of Faults
Fault Types |  | Types
Software fault |  | Programming mistakes
Hardware fault |  | A gate whose output is stuck at the value ZERO
Design fault |  | Assign too little memory in a telephone switch
Implementation fault |  | Installing less memory than the design called for
Operations fault |  | Running a weekly payroll twice last Friday
Environment fault |  | Lightning strikes a power line causing a voltage surge
Transient fault |  | Cosmic ray caused single bit flipped (soft error)
Persistent fault |  | A bit is stuck at zero (hard error)

## Slide 29: Tolerating Active Faults
Do nothing: let higher layer solve the failure
  The more layers, the more difficult
Be fail-fast: report the problem
  E.g., Ethernet stops sending and broadcasts when collision
Be fail-safe: transfer incorrect values to acceptable ones
  E.g., blinking red light in all directions
Be fail-soft: continues to operate with degradation
  E.g., airplane with three engines continues to fly if one has failure
Mask the error: makes incorrect value right

## Slide 30: MTTF & Availability

## Slide 31: MTTF, MTTR, MTBF
MTTF: mean time to failure
MTTR: mean time to repair
MTBF: mean time between failure
MTBF = MTTF + MTTR
TBF-1
TBF-2
TBF-3
TTF-1
TTF-2
TTF-3
TTR-2
TTR-1
TTR-3

## Slide 32: MTBF
Web page snapshot

## Slide 33: Measuring MTBF
Two purposes: evaluating & predicting
  The more reliable, the longer it takes to evaluate
  Not measure directly, but use proxies to estimate its value
One way to measure "MTBF"
  E.g. 3.5-inch disk's MTTF is 700,000 hours (80 years!)
  Guess: ran 7,000 disks for 1,000 hours and 10 failed
  If the failure process were memoryless, then OK
  "expected operational lifetime" is only 5 years

## Slide 34: Bathtub Curve
  gross manufacturing defects
  accumulated ware and tear cause failure
  run for a while before shipping

## Slide 36
Bairavasundaram et al., SIGMETRICS 2007

## Slide 37: Frequency of Hardware Replacement
Wang et al., DSN 2017

## Slide 38: Availability
Counting the number of nines
  E.g. 99.9% has 3-nines availability
  Often used in marketing
Corresponding down time
  E.g. 3-nines -> 8 hour/year
  E.g. 5-nines -> 5 min/year
  E.g. 7-nines -> 3 sec/year
  Without any information about MTTF
More fine-grained
  Fail-soft, as in 8.3

## Slide 39: Availability in Practice
Carrier airlines (2002 FAA fact book)
  99.9993% availability, 41 accidents, 6.7M departures
911 Phone service (1993 NRIC report)
  99.994%, 29 minutes per line per year
Standard phone service (various sources)
  99.99+%, 53+ minutes per line per year
End-to-end Internet Availability
  95% - 99.6%

## Slide 40: Redundancy

## Slide 41: Systematically Applying Redundancy
Masking error
  Analog system designer: margin
  Digital system designer: redundancy
Outline
  Coding: incremental redundancy
  Replication: massive redundancy
  Voting
  Repair

## Slide 42: Recall: Coding for Incremental Redundancy
Forward error correction
  Perform coding before storing or transmitting
  Later decode the data without appealing to the creator
Hamming distance
  Number of 1 in A ⊕ B , ⊕ is exclusive OR (XOR)
  If H-distance between every legitimate pair is 2
    000101, can only detect 1-bit flip
  If H-distance between every legitimate pair is 3
    Can only correct 1 bit flip
  If H-distance between every legitimate pair is 4
    Can detect 2-bit flip, correct 1-bit flip

## Slide 43: Replication: Massive Redundancy
Redundancy in bridge building
  Material strength: 5 or 10 times as strong as min
  Heavy-handed, but simple and effective
Replication
  Replicas: identical multiple copies
  E.g. Quad component by Shannon & Moore
    Can tolerate single short circuit and single open circuit, and others
  Mask failures silently

## Slide 44: Voting
NMR: N-modular redundancy (supermodule)
  E.g. TMR (3MR) and 5MR
  Voter: compare the outputs with the same inputs
  Can be applied at any level of module
Fail-vote: NMR with a majority voter
  Raise an alert if any replicas disagree with majority
  Signal a failure if no majority
  Fail-fast only if any two replicas fail in different ways
    If two replicas fail in same way, then not fail-fast

## Slide 45: Voting
The probability that an incorrect result will be accepted by the voter is that it is no more than:
Assume the voter is perfectly reliable, which is not practical
  Voter should also be replicated
  Everything should be replicated
  Recursive: voters belong to next module
  Final voter should be the client

## Slide 46: Voting
TMR can improve reliability
  If R(T) = 0.999, TMR's R(T) = 0.999997
But MTTF can be smaller
  If MTTF is 6,000 hours and fails independently, and the mechanism of failure is memoryless
  6,000 hours in only 2,000 hours of flying, first fail
  3,000 hours next and cause the second fail
  5,000 hours < 6,000 hours

## Slide 47: MTTF-replica and MTTF-system
If MTTF-replica = 1, N replicas total
  Expected time until 1st failure is MTTF-replica/N
  Expected time from then until the 2nd is MTTF-replica/(N-1)
  Expected time until the system of N replicas fails is
  For large N is approximately ln(N)
If mission time is long compared with MTTF-replica
  Simple replication escalates the cost while providing little benefit

## Slide 48: Repair
Return to fail-vote TMR supermodel
  Requires at least two replicas be working
  The rate of failure of 2 replicas is 2/MTTF
  If replacement takes 1 hour, chance is 1/3000
  Once replaced, expect to fly another 2000 hours until next engine failure
  If we have unlimited replacement for 10,000 hours
    MTTF = 6 million hours

## Slide 49
In another word
  Although MTTF is reduced by the factor of 3
  The availability of repair has increased MTTF by a factor equal to the ratio of the MTTF to MTTR of the remaining 2 engines
Disk with 3 replicas
  If MTTF is 5-year, repair in 10 hours

## Slide 50: Review Overly Optimistic Assumptions
Disks fail independently?
  Same vendor, same fault
  Earthquake, whose MTTF is less than 3650 years
Disk failures are memoryless?
  Bathtub curve
Repair is a memoryless process?
  Stock enough spares
Repair is done flawlessly?
  Replace the wrong disk, forget to copy data, etc.

## Slide 51: Summary
Systems have faults. We have to take them into account and build reliable, fault-tolerant systems. Reliability always comes at a cost: there are tradeoffs between reliability and cost, reliability and simplicity, etc.
Our main tool for improving reliability is redundancy. One form of redundancy is replication, which can be used to combat many things including disk failures (important, disk failures mean lost data).
RAID replicates data across disks in a smart way: RAID 5 protects against single-disk failures while maintaining good performance.

## Slide 52: More Case Studies

## Slide 53: The U.S. National Archives
Preserve electronic records e.g., email
  Daily incremental backups
  periodic complete backups
  audit logs for tracking actions
June 18-21, 1999, 43,000 emails disappeared
  The audit log had been turned off for better performance
  The contractor’s employees never backup
  Archives never verify the existence of backup copies
  Lesson: Avoid rarely used components, must be tested periodically

## Slide 54: Hospital Operating Room in Newark, New Jersey
Hospital operating room, with three backup generators
August 14, 2003, a widespread power grid failure
  One backup generator caught fire from an oil leak
  Another backup generator shut down due to overload
  Hospital engineering turned off many circuit
  Main power was interrupted to the OR
  1. Rarely used component may not have been maintained properly
  2. Human makes mistakes

## Slide 55: World-Flight of Northwest Airline
2:05 p.m. on March 23, 2000
  All communications dropped out
  Six cables were accidentally bored through
  Both primary and secondary!
  Pilots resorted to manual procedures
  Radio links were used
  125 flights had to be cancelled
  1. MTTF depend on that replicas are independent
  2. FT measuring is difficult to test

## Slide 56: British: Telehouse’s Electricity
Safe against “fire, flooding, bombs, sabotage”
  Especial protection against power failure
  Including two independent connections to power grid
  A room full of batteries, two diesel generators
  Can detect failures automatically then switch
  May 8, 1997…“It was due to human error.”, which is not detectable
  Identifying each potential fault and evaluate the risk is first step
  People are part of the system, mistakes made by authorized operators are typically a bigger threat than trees falling on power lines

## Slide 57: Kerosene Light in Radin, Poland
A town of Radin has a electricity generator
  One day the machine broke
  Darkness descended upon all of the streets
  Even worse than the days without electricity
  Every house had a kerosene light
  Single point of failure: Centralization reduces robustness
  Adding redundancy to a centralized design takes planning and adds to the cost

## Slide 58: The SOHO Mission Interrupt
SOHO spacecraft was lost on June 25, 1998
  “… a direct result of operational errors, a failure to adequately monitor spacecraft status, and an erroneous decision which …”
  Five distinct direct causes of the loss
  Three indirect causes in design process
  Three indirect causes in operations procedures
  1. Complex systems fail for complex reasons
  2. When some components are people, multi-failures are too common