## Slide 1: End-to-end Layer Best-effort is not enough
IPADS, Shanghai Jiao Tong University
https://www.sjtu.edu.cn
SE3331-1 (2023 Fall)
xx

## Slide 2: Review: Control-plane VS. Data-plane
Control-plane
  Control the data flow by defining rules
  E.g., the routing algorithm
Data-plane
  Copies data according to the rules
  Performance critical
  E.g., the IP forwarding process

## Slide 3: NAT

## Slide 4
CASE: Ethernet Mapping
Mapping Internet to Ethernet

## Slide 5: Case Study: Mapping Internet to Ethernet
Listen-before-sending rule, collision
Ethernet: CSMA/CD
  Carrier Sense Multiple Access with Collision Detection
Ethernet type
  Experimental Ethernet, 3 mpbs
  Standard Ethernet, 10 mbps
  Fast Ethernet, 100 mbps
  Gigabit Ethernet, 1000 mbps

## Slide 6: Overview of Ethernet
A half duplex Ethernet
  The max propagation time is less than the 576 bit times, the shortest allowable packet
  So that two parties can detect a collision together
  If collision: wait random first time, exponential backoff if repeat
A full duplex & point-to-point Ethernet
  No collisions & the max length of the link is determined by the physical medium

## Slide 7: Difference between Hub and Switch
Hub
  A frame is "broadcast" to every one of its ports
  A 10/100Mbps hub must share its bandwidth with each port
Switch
  Keeps a record of the MAC addresses of all the devices
  A 10/100Mbps switch will allocate a full 10/100Mbps to each of its ports

## Slide 8: Broadcast Aspects of Ethernet
Broadcast network
  Every frame is delivered to every station
  (Compare with forwarding network)
ETHERNET_SEND
  Pass the call along to the link layer
ETHERNET_HANDLE
  Simple, can even be implemented in hardware

## Slide 9: Broadcast Aspects of Ethernet
procedure ETHERNET_HANDLE (net_packet, length)
destination ← net_packet.target_id
if destination = my_station_id
then
GIVE_TO_END_LAYER (net_packet.data,
net_packet.end_protocol,
net_packet.source_id)
else
ignore packet
no need to do any forwarding

## Slide 10: Broadcast Aspects of Ethernet
procedure ETHERNET_HANDLE (net_packet, length)
destination ← net_packet.target_id
if destination = my_station_id
or destination = BROADCAST_ID
then
GIVE_TO_END_LAYER (net_packet.data,
net_packet.end_protocol,
net_packet.source_id)
else
ignore packet

## Slide 11: Layer Mapping: Attach Ethernet to Forwarding Network
L sends a RPC to N by sending to station 18 of link 1
L sends a RPC to E by sending to K, E may have 15 as address, as well as M
15

## Slide 12: Layer Mapping
The Internet network layer
  NETWORK_SEND (data, length, RPC, INTERNET, N)
  NETWORK_SEND (data, length, RPC, ENET, 18)
L must maintain a table

## Slide 13: ARP (Address Resolution Protocol)
NETWORK_SEND ("where is M?", 11, ARP, ENET, BROADCAST)
NETWORK_SEND ("M is at station 15", 18, ARP, ENET, BROADCAST)
L asks E's Ethernet address, E does not hear the Ethernet broadcast, but the router at station 19 does, and it sends a suitable ARP response instead
Manage forwarding table as a cache

## Slide 14: ARP & RARP Protocol
Name mapping: IP address <-> MAC address

## Slide 15: ARP & RARP

## Slide 16: Network Topology
Take SJTU network for example
  Subnet: usually like 192.168.0.2 or 10.0.0.2
  Gateway: usually like 192.168.0.1
    Get the global IP address: 202.120.40.82
    A gateway usually has two (or more) IP address
  Proxy: get proxy's address
    E.g., 106.185.46.164 (Japan)

## Slide 17: Network Topology

## Slide 18: How to Use socket to Access www.baidu.com ?
You code as if your PC connect directly with Baidu
  Call connect() with Baidu's IP address
But how does the system find next hop?

## Slide 19: Putting All Together
App: I want to send a packet to Baidu, here is the packet with Baidu's IP in its header as target IP, and client's IP as source IP (Node-C)
OS: I don't know how to get to Baidu, I'll just send it to the router (gateway). But I cannot change the source IP of the packet, so I'll just change the MAC target address of the packet to the router's MAC address

## Slide 20: Putting All Together
The router-1 (gateway): I get a packet with my MAC as target address. Is it my IP? No… So I'll just forward it to next hop, by changing the target MAC address to next hop's MAC address (NAT: change source IP and source port as well)
Router-2: I connect directly to Baidu, I'll just change the target MAC address to Baidu

## Slide 21: ARP Spoofing
Construct spoofed ARP replies
A target computer could be convinced to send frames destined for computer A to instead go to computer B
Computer A will have no idea that this redirection took place
This process of updating a target computer's ARP cache is referred to as "ARP poisoning"

## Slide 22
A
IP:10.0.0.1
MAC:aa:aa:aa:aa
B
IP:10.0.0.2
MAC:bb:bb:bb:bb
Hacker
IP:10.0.0.3
MAC:cc:cc:cc:cc
switch
IP | MAC
10.0.0.2 | bb:bb:bb:bb
ARP cache
IP | MAC
10.0.0.1 | aa:aa:aa:aa
ARP cache
Spoofed ARP reply
IP:10.0.0.2
MAC:cc:cc:cc:cc
Spoofed ARP reply
IP:10.0.0.2
MAC:cc:cc:cc:cc
Spoofed ARP reply
IP:10.0.0.2
MAC:cc:cc:cc:cc

## Slide 23
A
IP:10.0.0.1
MAC:aa:aa:aa:aa
B
IP:10.0.0.2
MAC:bb:bb:bb:bb
Hacker
IP:10.0.0.3
MAC:cc:cc:cc:cc
switch
IP | MAC
10.0.0.2 | cc:cc:cc:cc
ARP cache
IP | MAC
10.0.0.1 | aa:aa:aa:aa
ARP cache
A's cache is poisoned

## Slide 24: ARP Spoofing
Now all the packets that A intends to send to B will go to the hacker's machine
Cache entry would expire, so it needs to be updated by sending the ARP reply again
  How often?
  depends on the particular system
  Usually every 40s should be sufficient
In addition the hacker may not want his Ethernet driver talk too much
  Accomplish with ifconfig -arp

## Slide 25: Man-in-the-Middle Attack
A hacker inserts his computer between the communications path of two target computers
The hacker will forward frames between the two target computers so communications are not interrupted
E.g., Hunt, Ettercap, etc.
  Can be obtained easily in many web archives

## Slide 26: Man-in-the-Middle Attack
The attack is performed as follows:
  Suppose X is the hacker's computer
  T1 and T2 are the targets
  X poisons the ARP cache of T1 and T2
  T1 associates T2's IP with X's MAC
  T2 associates T1's IP with X's MAC
  All of T1 and T2's traffic will then go to X first, instead of directly to each other

## Slide 27
T1
IP:10.0.0.1
MAC:aa:aa:aa:aa
T2
IP:10.0.0.2
MAC:bb:bb:bb:bb
Hacker
IP:10.0.0.3
MAC:cc:cc:cc:cc
switch
IP | MAC
10.0.0.2 | bb:bb:bb:bb
ARP cache
IP | MAC
10.0.0.1 | aa:aa:aa:aa
ARP cache
Spoofed ARP reply
IP:10.0.0.2
MAC:cc:cc:cc:cc
Spoofed ARP reply
IP:10.0.0.2
MAC:cc:cc:cc:cc
Spoofed ARP reply
IP:10.0.0.2
MAC:cc:cc:cc:cc

## Slide 28
T1
IP:10.0.0.1
MAC:aa:aa:aa:aa
T2
IP:10.0.0.2
MAC:bb:bb:bb:bb
Hacker
IP:10.0.0.3
MAC:cc:cc:cc:cc
switch
IP | MAC
10.0.0.2 | cc:cc:cc:cc
ARP cache
IP | MAC
10.0.0.1 | aa:aa:aa:aa
ARP cache
T1's cache is poisoned

## Slide 29
T1
IP:10.0.0.1
MAC:aa:aa:aa:aa
T2
IP:10.0.0.2
MAC:bb:bb:bb:bb
Hacker
IP:10.0.0.3
MAC:cc:cc:cc:cc
switch
IP | MAC
10.0.0.2 | cc:cc:cc:cc
ARP cache
IP | MAC
10.0.0.1 | aa:aa:aa:aa
ARP cache
Forged ARP replies
IP:10.0.0.1
MAC:cc:cc:cc:cc
Forged ARP replies
IP:10.0.0.1
MAC:cc:cc:cc:cc

## Slide 30
T1
IP:10.0.0.1
MAC:aa:aa:aa:aa
T2
IP:10.0.0.2
MAC:bb:bb:bb:bb
Hacker
IP:10.0.0.3
MAC:cc:cc:cc:cc
switch
IP | MAC
10.0.0.2 | cc:cc:cc:cc
ARP cache
IP | MAC
10.0.0.1 | cc:cc:cc:cc
ARP cache
T2's cache is poisoned

## Slide 31
T1
IP:10.0.0.1
MAC:aa:aa:aa:aa
T2
IP:10.0.0.2
MAC:bb:bb:bb:bb
Hacker
IP:10.0.0.3
MAC:cc:cc:cc:cc
switch
IP | MAC
10.0.0.2 | cc:cc:cc:cc
ARP cache
IP | MAC
10.0.0.1 | cc:cc:cc:cc
ARP cache
Message intended to send to T2
Hacker will
relay the
message

## Slide 32
T1
IP:10.0.0.1
MAC:aa:aa:aa:aa
T2
IP:10.0.0.2
MAC:bb:bb:bb:bb
Hacker
IP:10.0.0.3
MAC:cc:cc:cc:cc
switch
IP | MAC
10.0.0.2 | cc:cc:cc:cc
ARP cache
IP | MAC
10.0.0.1 | cc:cc:cc:cc
ARP cache
Hacker will relay the message
Message
intended to
send to T1

## Slide 33: Defenses against ARP Spoofing
No Universal defense (!)
Use static ARP entries
  Cannot be updated; Spoofed ARP replies are ignored
  ARP table needs a static entry for each machine on the network
  Large overhead
    Deploying these tables; Keep the table up-to-date
Arpwatch
  A free UNIX program which listens for ARP replies on a network
  Build a table of IP/MAC associations and store it in a file
  When a MAC/IP pair changes (flip-flop), an email is sent to an administrator

## Slide 34
End-to-end Layer

## Slide 35: The End-to-end Layer
Network layer has no guarantees on:
  Delay - Order of arrival
  Certainty of arrival - Accuracy of content
  Right place to deliver
End-to-end layer
  No single design is likely to suffice
  Transport protocol for each class of application

## Slide 36: Famous Transport Protocols
UDP (User Datagram Protocol)
  Be used directly for some simple applications
  Also be used as a component for other protocols
TCP (Transmission Control Protocol)
  Keep order, no missing, no duplication
  Provision for flow control
RTP (Real-time Transport Protocol)
  Built on UDP
  Be used for streaming video or voice, etc.
No "one size fits all"

## Slide 37: Assurance of End-to-end Protocol
Assurance of at-least-once delivery
Assurance of at-most-once delivery
Assurance of data integrity
Assurance of stream order & closing of connections
Assurance of jitter control
Assurance of authenticity and privacy
Assurance of end-to-end performance

## Slide 38: 1. Assurance of At-least-once Delivery
RTT (Round-trip time)
  to_time + process_time + back_time (ack)
At least once on best effort network
  Send packet with nonce
  Sender keeps a copy of the packet
  Resend if timeout before receiving acknowledge
  Receiver acknowledges a packet with its nonce
Try limit times before returning error to app

## Slide 39: 1. Assurance of At-least-once Delivery
Dilemma
  1. The data was not delivered
  2. The data was delivered, but no ACK received
  No way to know which situation
At-least-once delivery
  No absolute assurance for at-least-once
  Ensure if it is possible to get through, the message will get through eventually
  Ensure if impossible to confirm delivery, app will know
  No assurance for no-duplication

## Slide 40: How to Decide Timeout?
Fixed timer: dilemma of fixed timer
  Too short? unnecessary resend
  Too long? take long time to discover lost packets
Adaptive timer
  E.g., adjust by currently observed RTT, set timer to 150%
  Exponential back-off: doubling from a small timer
NAK (Negative AcKnowledgment)
  Receiver sends a message that lists missing items
  Receiver can count arriving segments rather than timer
  Sender can have no timer (only once per stream)

## Slide 41: Fixed Timer is Evil
Fixed timers lead to congestion collapse in NFS
Emergent phase synchronization of periodic protocols
Wisconsin time server meltdown

## Slide 42: Emergent Phase Synchronization of Periodic Protocols
Periodic polling
  E.g. picking up mail, sending "are-you-there?"
  A workstation sends a broadcast packet every 5 minutes
  All workstations try to broadcast at the same time
Each workstation
  Send a broadcast
  Set a fixed timer
Lesson: Fixed timers have many evils. Do not assume that unsynchronized periodic activities will stay that way

## Slide 43: Wisconsin Time Server Meltdown
NETGEAR added a feature to wireless router
  Logging packets -> timestamp -> time server (SNTP) -> name discovery -> 128.105.39.11
  Once per second (!) until receive a response
  Once per minute or per day after that
Wisconsin Univ.
  On May 14, 2003, at about 8:00 am
  From 20,000 to 60,000 requests per second, filtering 23457
  After one week, 270,000 requests per second, 150Mbps

## Slide 44: Wisconsin Time Server Meltdown
Lesson(s)
  Fixed timers, again
  Fixed Internet address
  The client implements only part of a protocol
    There is a reason for features likes the "go away" response in SNTP

## Slide 45: How to Decide Timeout?
Fixed timer: dilemma of fixed timer
  Too short: unnecessary resend
  Too long: take long time to discover lost packets
Adaptive timer
  E.g., adjust by currently observed RTT, set timer to 150%
  Exponential back-off: doubling from a small timer
NAK (Negative AcKnowledgment)
  Receiver sends a message that lists missing items
  Receiver can count arriving segments rather than timer
  Sender can have no timer (only once per stream)

## Slide 46: RTT Could be Highly Variable

## Slide 47: Calculating RTT and Timeout (in TCP)
Exponentially Weighted Moving Average
  Estimate both the average rtt_avg and the deviation rtt_dev
  Procedure calc_rtt(rtt_sample)
    rtt_avg = a*rtt_sample + (1-a)*rtt_avg; /* a = 1/8 */
    dev = absolute(rtt_sample – rtt_avg);
    rtt_dev = b*dev + (1-b)*rtt_dev; /* b = 1/4 */
  Procedure calc_timeout(rtt_avg, rtt_dev)
    Timeout = rtt_avg + 4*rtt_dev

## Slide 48: How to Decide Timeout?
Fixed timer: dilemma of fixed timer
  Too short: unnecessary resend
  Too long: take long time to discover lost packets
Adaptive timer
  E.g., adjust by currently observed RTT, set timer to 150%
  Exponential back-off: doubling from a small timer
NAK (Negative AcKnowledgment)
  Receiver sends a message that lists missing items
  Receiver can count arriving segments rather than timer
  Sender can have no timer (only once per stream)

## Slide 49: 2. Assurance of At-most-once Delivery
At-least-once delivery
  Remember state at the sending side
  Tends to generate duplicated requests
At-most-once delivery
  Maintains a table of nonce at the receiving side
  The table may grow indefinitely
    Space and search time
    Tombstones (something that cannot be deleted forever)
  Another way: Make the application tolerate duplicated requests
    Recall the NFS collapse case: server wastes time to execute duplicated requests

## Slide 50: Duplicate Suppression
Monotonically increasing sequence number
  Receiver discards smaller nonce, only holds the last nonce, one per sender
  Now, the old nonce is a tombstone!
Use a different port for each new request
  Should never reuse the old port number
  But, the old port is now tombstone!

## Slide 51: Duplicate Suppression
Accept the possibility of making a mistake
  E.g., if sender always gives up after five RTT (cannot ensure at-least-once), then receiver can safely discard nonces that are older than five RTT
  It is possible that a packet finally shows up after long delay (solution: wait long time)
Receiver crashes and restarts: lose the table
  One solution is to use a new port number each time the system restarts
  Another is to ignore all packets until the number of RTT has passed since restarting, if sender tries limit times
Anyway, duplicate suppression makes the system complex

## Slide 52: 3. Assurance of Data Integrity
Data integrity
  Receiver gets the same contents as sender
Reliable delivery protocol
  Sender: adds checksum to the end-to-end layer
  Receiver: recalculates the checksum, discards if not match
Q: Is it redundant since link layer provides checksum?
  No. Besides network, there could be other errors, e.g., in memory copying
The assurance is not absolute
  What if a packet is mis-delivered and the receiver ACK?

## Slide 53: 4. Segments and Reassembly of Long Messages
Bridge the difference between message and MTU
  Message length: determined by application
  MTU: determined by network
Segment contains ID for where it fits
  E.g., "message 914, segment 3 of 7"
  Can be used for at-least-once and at-most-once delivery
Reassembly
  Out-of-order, mingled with other message's segments
  Allocating a buffer large enough to hold the message

## Slide 54: When Out of Order…
Solution-1: Receiver only ACK in order packets, discards others
  Waste of bandwidth
Solution-2: ACK every packet and hold early packets in buffer, release the buffer when all in order
  Need using large buffer when waiting for a bad packet
Solution-3: Combine the two above
  Discard if buffer is full
  New problem: how much buffer?
Speedup for common case
  NAK to avoid timeout
  If NAKs are causing duplicates, stop NAKs
TCP is based on ACK, not NAK

## Slide 55: Closing of Connections
Open a stream
  Create a record to keep track of which elements have been sent, received, acknowledged
Close a stream
  When finish, it needs to report an end-of-stream
  Both ends need to agree last element is OK and then close
  1. Alice sends close request to Bob with stream record ID
  2. Bob checks and agrees, sends a close ACK
  3. Alice receives ACK, turn off sender, discard record
  4. Alice sends "all done" to Bob
  5. Bob receives "all done" and discard stream record
<- What if duplicate?
55

## Slide 56: 5. Assurance of Jitter Control
Real-time
  When reliability is less important than timely delivery
  A few error in a movie may not be noticed
  Jitter: variability in delivery time
Strategy
  Basic: delay all arriving segments

## Slide 57: 5. Assurance of Jitter Control
Measure the distribution of delays in a chart showing delay time vs. frequency of that delay
Choose an acceptable frequency of delivery failure
Determine Dlong that longer than 99% delay
Determine the shortest delay, Dshort
Calculate number of segment buffer:
  Dheadway is average delay between arriving segments

## Slide 58: 6. Assurance of Authenticity and Privacy
Internet is dangerous
  Hostile intercepts and maliciously modifies packets
  Violate a protocol with malicious intent
Key-based mathematical transformations to data
  Sign and verify: establish the authenticity of the source and integrity of contents
  Encrypt and decrypt: maintain privacy of contents
Consideration
  False sense of security, worse than no assurance

## Slide 59: 6. Security: Asymmetric Encryption
Public Key VS. Private Key
  Public key: encrypt to identify reader (only me can read this)
  Private key: encrypt to identify writer (yes, it's me who wrote this)
  Poor performance, so just used to exchange symmetric key
Questions
  What is a certificate? Why using a CA (Certificate Authority)?
  How to exchange a symmetric key in HTTPS or SSH?
  What is the root of trust?
  Will be addressed later, in Security part

## Slide 60: 7. End-to-end Performance
Multi-segment message questions
  Trade-off between complexity and performance
  Lock-step protocol

## Slide 61: Overlapping Transmissions
Pipelining technique

## Slide 62: Overlapping Transmissions
Packets or ACK may be lost
  Sender holds a list of segments sent, check it off when receives ACK
  Set a timer (according to RTT) for last segment
If list of missing ACK is empty, OK
If timer expires, resend packets and another timer

## Slide 63: Fixed Window
Receiver tells the sender a window size
Sender sends window
Receiver acks each packet as before
Window advances when all packets in previous window are acked
  E.g., packets 4-6 sent, after 1-3 ack'd
If a packet times out -> resend packets
Still much idle time

## Slide 64: Sliding Window
Sender advances the window by 1 for each in-sequence ACK it receives
  Reduces idle periods
  Pipelining idea
But what's the correct value for the window?
  We'll revisit this question
  First, we need to understand windows

## Slide 65: Handling Packet Loss

## Slide 66: Chose the Right Window Size
If window is too small
  Long idle time
  Underutilized network
If window too large
  Congestion

## Slide 67: Sliding Window Size
window size ≥ round-trip time × bottleneck data rate
Sliding window with one segment in size
  Data rate is window size / RTT
Enlarge window size to bottleneck data rate
  Data rate is window size / RTT
Enlarge window size further
  Data rate is still bottleneck
  Larger window makes no sense
- Receive 500 KBps
- Sender 1 MBps
- RTT 70ms
- A segment carries 0.5 KB
- Sliding window size = 35KB (70 segment)

## Slide 68: Self-pacing: Sliding Window Size
Although the sender doesn't know the bottleneck, it is sending at exactly that rate
Once sender fills a sliding window, cannot send next data until receive ACK of the oldest data in the window
The receiver cannot generate ACK faster than the network can deliver data elements
RTT estimation still needed

## Slide 69
TCP Congestion Control

## Slide 70: Congestion
Definition: Too many packets present in (a part of) the network causes packet delay and loss that degrades performance.
Network & End-to-end layers share the responsibility for handling congestion
1. Network layer
  Directly experiences the congestion
  Ultimately determine what to do with the excess packets
2. End-to-end layer
  Control to reduce the sending rate, is the most effective way

## Slide 71: Network Congestion

## Slide 72: Why Congest?
If all of a sudden, streams of packets begin arriving on three or four input lines and all need the same output line, a queue will build up
If there is insufficient memory to hold all of them, packets will be lost
Adding more memory may help up to a point, but
  Nagle (1987) realized that if routers have an infinite amount of memory, congestion gets worse, not better
  This is because by the time packets get to the front of the queue, they have already timed out (repeatedly) and duplicates have been sent

## Slide 73: Load Shedding: Setting Window Size
For performance:
  window size ≥ round-trip time × bottleneck data rate
For congestion control:
  window size ≤ min(RTT x bottleneck data rate, Receiver buffer)
  Congestion window
2 windows become 1
  to achieve best performance and avoid congestion

## Slide 74: Congestion Control
Basic idea:
  Increase congestion window slowly
  If no drops -> no congestion yet
  If a drop occurs -> decrease congestion window quickly
Use the idea in a distributed protocol that achieves:
  Efficiency: i.e., uses the bottleneck capacity efficiently
  Fairness, i.e., senders sharing a bottleneck get equal throughput (if they have demands)

## Slide 75: AIMD (Additive Increase, Multiplicative Decrease)
Every RTT:
  No drop: cwnd = cwnd + 1
  A drop: cwnd = cwnd / 2

## Slide 76: Problems with AIMD
Increases very slowly at the beginning
Initial window size is 1
  Probably too small in practice
Solution: do multiplicative increase at the beginning
  Congestion_window init = 1
  Initially, do Congestion_window ← 2 * Congestion_window each RTT until we hit congestion
  Named "slow start" (even though it's exponentially fast!)

## Slide 77: Retrofitting TCP

## Slide 78: Retrofitting TCP
1. Slow start: one packet at first, then double until
  Sender reaches the window size suggested by the receiver
  All the available data has been dispatched
  Sender detects that a packet it sent has been discarded
2. Duplicate ACK
  When receiver gets an out-of-order packet, it sends back a duplicate of latest ACK
3. Equilibrium
  Additive increase & multiplicative decrease
4. Restart, after waiting a short time

## Slide 79: Fairness between Links

## Slide 80: AIMD Leads to Efficiency and Fairness

## Slide 81: Q: Why not Additive Decrease
It does not converge to fairness
  from a congested point, (x',y'), reducing each by 1 worsens fairness and takes us away from the "ideal" outcome

## Slide 82: Weakness of TCP
If routers have too much buffering, causes long delays
Packet loss is not always caused by congestion
  Consider wireless network: if losing packet, sender may send faster instead
TCP does not perform well in datacenters
  High bandwidth, low delay situations
TCP has a bias against long RTTs
  Throughput inversely proportionally to RTT
  Consider when sending packets really far away vs really close
Assumes cooperating sources, which is not always a good assumption

## Slide 83: Summary of Congestion Window
Reliability Using Sliding Window
  Tx Rate = W / RTT
Congestion Control
  W = min(Receiver_buffer, cwnd)
  Congestion window is adapted by the congestion control protocol to ensure efficiency and fairness
  TCP congestion control uses AIMD which provides fairness and efficiency in a distributed way