## Slide 1: Network Layer All about routing
IPADS, Shanghai Jiao Tong University
https://www.sjtu.edu.cn
SE3331-1 (2025 Fall)
Credits to Katrina LaCurts, MIT

## Slide 2: Review: OSI, TCP/IP & Protocol Stack
7th Application Layer
6th Presentation Layer
4th Transport Layer
3th Network Layer
2nd Link Layer
1st Physical Layer
Application Layer
HTTP
TCP
Ethernet
UDP
IP
PPP
…
SMTP
POP3
FTP
…
ICMP
ARP & RARP
Transport Layer
5th Session Layer
Network Layer
Link Layer
End-to-end Layer
Network Layer
Link Layer
OSI
TCP/IP
CSE
WiFi
Fiber
TD-LTE
FDD
…

## Slide 3: Review: Simple Parity Check
2 bits -> 3 bits
  Detect 1-bit errors
  8 patterns total
Only 4 correct patterns
  00 -> 000
  11 -> 110
  10 -> 101
  01 -> 011
Hamming distance of this code is 2
  1-bit flipping will cause incorrect pattern

## Slide 4: Network Layer

## Slide 5: IP: Best-effort Network
1. Best-effort network
  If it cannot dispatch, may discard a packet
2. Guaranteed-delivery network
  Also called store-and-forward network, no discarding data
  Work with complete messages rather than packets
  Use disk for buffering to handle peaks
  Tracks individual message to make sure none are lost
In real world
  No absolute guarantee
  Guaranteed-delivery: higher layer; best-effort: lower layer

## Slide 6: Duplicate Packets and Suppression
Discarding packets is common case
  Many network protocols include timeout and resend mechanism
When a congested forwarder discards a packet
  Client does not receive a response as quickly as originally hoped
  Users may prepared for duplicate requests and responses
  Detecting duplicates may or may not be important

## Slide 7: The Network Layer
Addressing interface
  Network attachment points
  Network address
  Source & destination
NETWORK_SEND
  (segment_buffer, destnation, network_protocol, end_layer_protocol)
NETWORK_HANDLE
  (packet, network_protocol)

## Slide 8: Managing the Forwarding Table: Routing
Routing (or path-finding)
  Constructing the tables
Impractical by hand
  Determining the best paths requires calculation
  Recalculating the table when links change
  Recalculating the table when link fails
  Adapt according to traffic congestion
Static routing vs. adaptive routing
  Adaptive routing requires exchange of info

## Slide 9: IP Route Table
Interface 1 … Interface N

## Slide 10: Control-plane VS. Data-plane
Control-plane
  Control the data flow by defining rules
  E.g., the routing algorithm
Data-plane
  Copies data according to the rules
  Performance critical
  E.g., the IP forwarding process

## Slide 11
Routing
How to generate the routing table?

## Slide 12: Goal of A Routing Protocol
Allow each switch to know, for every node dst in the network, a route to dst
Allow each switch to know, for every node dst in the network, a minimum-cost route to dst
Build a routing table at each switch, such that routing_table[dst] contains a minimum-cost route to dst

## Slide 13: Distributed Routing: 3 Steps in General
Nodes learn about their neighbors via the HELLO protocol
Nodes learn about other reachable nodes via advertisements
Nodes determine the minimum-cost routes (of the routes they know about)

## Slide 14: Two Types of Routing Protocol
Protocol 1: Link-state
  A node's advertisements contain a list of its neighbors and its link costs to those nodes
  Nodes advertise to everyone their costs to their neighbors
    via flooding
  Integrate using Dijkstra's shortest path algorithm
Protocol 2: Distance-vector
  Nodes advertise to neighbors with their cost to all known nodes
  Update routes via Bellman-Ford integration

## Slide 15: link-state routing: disseminate full topology information so that nodes can run a shortest-path algorithm
link state
7
2
1
5
3
5
3
A
F
C
E
D
B
4
1

## Slide 16: link-state routing: disseminate full topology information so that nodes can run a shortest-path algorithm
its link costs to each of its neighbors
link state
what’s in an advertisement
7
2
1
5
3
5
3
A
F
C
E
D
B
4
1

## Slide 17: link-state routing: disseminate full topology information so that nodes can run a shortest-path algorithm
its link costs to each of its neighbors
link state
what’s in an advertisement
7
2
1
5
3
5
3
A
C
F E
D
B
4
1
A’s advertisement: [(B,7),(D,2),(F,1)]

## Slide 18: link-state routing: disseminate full topology information so that nodes can run a shortest-path algorithm
link state
what’s in an advertisement
its link costs to each of its neighbors
who gets a node’s advertisement
7
2
1
5
3
5
3
A
C
F E
D
B
4
1
A’s advertisement: [(B,7),(D,2),(F,1)]

## Slide 19: link-state routing: disseminate full topology information so that nodes can run a shortest-path algorithm
link state
what’s in an advertisement
its link costs to each of its neighbors
who gets a node’s advertisement
effectively, every other node (via flooding)
7
2
1
5
3
5
3
A
C
F E
D
B
4
1
A’s advertisement: [(B,7),(D,2),(F,1)]

## Slide 20: link-state routing: disseminate full topology information so that nodes can run a shortest-path algorithm
link state
what’s in an advertisement
its link costs to each of its neighbors
who gets a node’s advertisement
effectively, every other node (via flooding)
7
2
1
5
3
5
3
A
C
F E
D
B
4
1
A’s advertisement: [(B,7),(D,2),(F,1)]

## Slide 21: link-state routing: disseminate full topology information so that nodes can run a shortest-path algorithm
link state
what’s in an advertisement
its link costs to each of its neighbors
who gets a node’s advertisement
effectively, every other node (via flooding)
7
2
1
5
3
5
3
A
C
F E
D
B
4
1
A’s advertisement: [(B,7),(D,2),(F,1)]

## Slide 22: link-state routing: disseminate full topology information so that nodes can run a shortest-path algorithm
link state
what’s in an advertisement
its link costs to each of its neighbors
who gets a node’s advertisement
effectively, every other node (via flooding)
7
2
1
5
3
5
3
A
C
F E
D
B
4
1
A’s advertisement: [(B,7),(D,2),(F,1)]

## Slide 23: link-state routing: disseminate full topology information so that nodes can run a shortest-path algorithm
link state
what’s in an advertisement
its link costs to each of its neighbors
who gets a node’s advertisement
effectively, every other node (via flooding)
7
2
1
5
3
5
3
A
C
F E
D
B
4
1
A’s advertisement: [(B,7),(D,2),(F,1)]

## Slide 24: link-state routing: disseminate full topology information so that nodes can run a shortest-path algorithm
link state
what’s in an advertisement
its link costs to each of its neighbors
who gets a node’s advertisement
effectively, every other node (via flooding)
7
2
1
5
3
5
3
A
C
F E
D
B
4
1
A’s advertisement: [(B,7),(D,2),(F,1)]

## Slide 25: link-state routing: disseminate full topology information so that nodes can run a shortest-path algorithm
link state
what’s in an advertisement
its link costs to each of its neighbors
who gets a node’s advertisement
effectively, every other node (via flooding)
7
2
1
5
3
5
3
A
C
F E
D
B
4
1
A’s advertisement: [(B,7),(D,2),(F,1)]

## Slide 26: link-state routing: disseminate full topology information so that nodes can run a shortest-path algorithm
link state
what’s in an advertisement
its link costs to each of its neighbors
who gets a node’s advertisement
effectively, every other node (via flooding)
7
2
1
5
3
5
3
A
C
F E
D
B
4
1
A’s advertisement: [(B,7),(D,2),(F,1)]

## Slide 27: link-state routing: disseminate full topology information so that nodes can run a shortest-path algorithm
link state
what’s in an advertisement
its link costs to each of its neighbors
who gets a node’s advertisement
effectively, every other node (via flooding)
7
2
1
5
3
5
3
A
C
F E
D
B
4
1
A’s advertisement: [(B,7),(D,2),(F,1)]

## Slide 28: link-state routing: disseminate full topology information so that nodes can run a shortest-path algorithm
its link costs to each of its neighbors
effectively, every other node (via flooding)
link state
what’s in an advertisement
who gets a node’s advertisement
7
2
1
5
3
5
3
A
C
F E
D
B
4
1
A’s advertisement: [(B,7),(D,2),(F,1)]
nodes keep track of which advertisements they’ve forwarded so that they don’t re-forward them

## Slide 29: link-state routing: disseminate full topology information so that nodes can run a shortest-path algorithm
its link costs to each of its neighbors
effectively, every other node (via flooding)
link state
what’s in an advertisement
who gets a node’s advertisement
7
2
1
5
3
5
3
A
C
F E
D
B
4
1
A’s advertisement: [(B,7),(D,2),(F,1)]
nodes keep track of which advertisements they’ve forwarded so that they don’t re-forward them
they can also be a bit smarter about flooding, and not forward an advertisement back to the node that sent it

## Slide 30: link-state routing: disseminate full topology information so that nodes can run a shortest-path algorithm
its link costs to each of its neighbors
effectively, every other node (via flooding)
link state
what’s in an advertisement
who gets a node’s advertisement
7
2
1
5
3
5
3
A
F
C
E
D
B
4
1
nodes integrate advertisements by running Dijkstra’s Algorithm

## Slide 31: link-state routing: disseminate full topology information so that nodes can run a shortest-path algorithm
its link costs to each of its neighbors
effectively, every other node (via flooding)
link state
what’s in an advertisement
who gets a node’s advertisement
7
2
1
5
3
5
3
A
F
C
E
D
B
4
1
dst ¦ route ¦ cost |  |  |  | 
B | ¦ | A-B | ¦ | 7
C | ¦ | ? | ¦ | ∞
D | ¦ | A-D | ¦ | 2
E | ¦ | ? | ¦ | ∞
F | ¦ | A-F | ¦ | 1
A’s routing table

## Slide 32: Link-state Routing
Keep track of W, the set of nodes haven't processed yet
  Initially, W is all nodes in the network
Keep track of the current costs and routes to all of the nodes. Initially:
  routing_table[self] = Self; routing_table[anyone else] = ?
  cost_table[self] = 0; cost_table[anyone else] = infinity
While W is not empty:
  1. u = the node in W we have the minimum cost to so far
  2. Remove u from W
  3. For every neighbor v of u: d = cost_table[u] + cost(u, v) if d < cost_table[v] cost_table[v] = d routing_table[v] = routing_table[u]

## Slide 33: link-state routing: disseminate full topology information so that nodes can run a shortest-path algorithm
its link costs to each of its neighbors
effectively, every other node (via flooding)
link state
what’s in an advertisement
who gets a node’s advertisement
7
2
1
5
3
5
3
A
F
C
E
D
B
4
1
dst ¦ route ¦ cost |  |  |  | 
B | ¦ | A-B | ¦ | 7
C | ¦ | ? | ¦ | ∞
D | ¦ | A-D | ¦ | 2
E | ¦ | ? | ¦ | ∞
F | ¦ | A-F | ¦ | 1
A’s routing table

## Slide 34: link-state routing: disseminate full topology information so that nodes can run a shortest-path algorithm
its link costs to each of its neighbors
effectively, every other node (via flooding)
link state
what’s in an advertisement
who gets a node’s advertisement
7
2
1
5
3
5
3
A
F
C
E
D
B
4
1
dst ¦ route ¦ cost |  |  |  | 
B | ¦ | A-B | ¦ | 7
C | ¦ | ? | ¦ | ∞
D | ¦ | A-D | ¦ | 2
E | ¦ | ? | ¦ | ∞
F | ¦ | A-F | ¦ | 1
A’s routing table

## Slide 35: link-state routing: disseminate full topology information so that nodes can run a shortest-path algorithm
its link costs to each of its neighbors
effectively, every other node (via flooding)
link state
what’s in an advertisement
who gets a node’s advertisement
7
2
1
5
3
5
3
A
F
C
E
D
B
4
1
dst ¦ route ¦ cost |  |  |  | 
B | ¦ | A-B | ¦ | 7
C | ¦ | ? | ¦ | ∞
D | ¦ | A-D | ¦ | 2
E | ¦ | ? | ¦ | ∞
F | ¦ | A-F | ¦ | 1
A’s routing table

## Slide 36: link-state routing: disseminate full topology information so that nodes can run a shortest-path algorithm
its link costs to each of its neighbors
effectively, every other node (via flooding)
link state
what’s in an advertisement
who gets a node’s advertisement
7
2
1
5
3
5
3
A
F
C
E
D
B
4
1
F does not provide A with a better route to D
dst ¦ route ¦ cost |  |  |  | 
B | ¦ | A-B | ¦ | 7
C | ¦ | ? | ¦ | ∞
D | ¦ | A-D | ¦ | 2
E | ¦ | ? | ¦ | ∞
F | ¦ | A-F | ¦ | 1
A’s routing table

## Slide 37: link-state routing: disseminate full topology information so that nodes can run a shortest-path algorithm
its link costs to each of its neighbors
effectively, every other node (via flooding)
link state
what’s in an advertisement
who gets a node’s advertisement
7
2
1
5
3
5
3
A
F
C
E
D
B
4
1
dst ¦ route ¦ cost |  |  |  | 
B | ¦ | A-B | ¦ | 7
C | ¦ | ? | ¦ | ∞
D | ¦ | A-D | ¦ | 2
E | ¦ | ? | ¦ | ∞
F | ¦ | A-F | ¦ | 1
A’s routing table

## Slide 38: link-state routing: disseminate full topology information so that nodes can run a shortest-path algorithm
its link costs to each of its neighbors
effectively, every other node (via flooding)
link state
what’s in an advertisement
who gets a node’s advertisement
7
2
1
5
3
5
3
A
F
C
E
D
B
4
1
= the cost from A to F + the cost from F to E
dst ¦ route ¦ cost |  |  |  | 
B | ¦ | A-B | ¦ | 7
C | ¦ | ? | ¦ | ∞
D | ¦ | A-D | ¦ | 2
E | ¦ | A-F | ¦ | 6
F | ¦ | A-F | ¦ | 1
A’s routing table

## Slide 39: link-state routing: disseminate full topology information so that nodes can run a shortest-path algorithm
its link costs to each of its neighbors
effectively, every other node (via flooding)
link state
what’s in an advertisement
who gets a node’s advertisement
7
2
1
5
3
5
3
A
F
C
E
D
B
4
1
dst ¦ route ¦ cost |  |  |  | 
B | ¦ | A-B | ¦ | 7
C | ¦ | ? | ¦ | ∞
D | ¦ | A-D | ¦ | 2
E | ¦ | A-F | ¦ | 6
F | ¦ | A-F | ¦ | 1
A’s routing table

## Slide 40: link-state routing: disseminate full topology information so that nodes can run a shortest-path algorithm
its link costs to each of its neighbors
effectively, every other node (via flooding)
link state
what’s in an advertisement
who gets a node’s advertisement
7
2
1
5
3
5
3
A
F
C
E
D
B
4
1
dst ¦ route ¦ cost |  |  |  | 
B | ¦ | A-B | ¦ | 7
C | ¦ | ? | ¦ | ∞
D | ¦ | A-D | ¦ | 2
E | ¦ | A-F | ¦ | 6
F | ¦ | A-F | ¦ | 1
A’s routing table

## Slide 41: link-state routing: disseminate full topology information so that nodes can run a shortest-path algorithm
its link costs to each of its neighbors
effectively, every other node (via flooding)
link state
what’s in an advertisement
who gets a node’s advertisement
7
2
1
5
3
5
3
A
F
C
E
D
B
4
1
dst ¦ route ¦ cost |  |  |  | 
B | ¦ | A-B | ¦ | 7
C | ¦ | ? | ¦ | ∞
D | ¦ | A-D | ¦ | 2
E | ¦ | A-F | ¦ | 6
F | ¦ | A-F | ¦ | 1
A’s routing table

## Slide 42: link-state routing: disseminate full topology information so that nodes can run a shortest-path algorithm
its link costs to each of its neighbors
effectively, every other node (via flooding)
link state
what’s in an advertisement
who gets a node’s advertisement
7
2
1
5
3
5
3
A
F
C
E
D
B
4
1
dst ¦ route ¦ cost |  |  |  | 
B | ¦ | A-B | ¦ | 3
C | ¦ | ? | ¦ | ∞
D | ¦ | A-D | ¦ | 2
E | ¦ | A-F | ¦ | 6
F | ¦ | A-F | ¦ | 1
A’s routing table

## Slide 43: link-state routing: disseminate full topology information so that nodes can run a shortest-path algorithm
its link costs to each of its neighbors
effectively, every other node (via flooding)
link state
what’s in an advertisement
who gets a node’s advertisement
7
2
1
5
3
5
3
A
F
C
E
D
B
4
1
dst ¦ route ¦ cost |  |  |  | 
B | ¦ | A-B | ¦ | 3
C | ¦ | ? | ¦ | ∞
D | ¦ | A-D | ¦ | 2
E | ¦ | A-F | ¦ | 6
F | ¦ | A-F | ¦ | 1
A’s routing table

## Slide 44: link-state routing: disseminate full topology information so that nodes can run a shortest-path algorithm
its link costs to each of its neighbors
effectively, every other node (via flooding)
link state
what’s in an advertisement
who gets a node’s advertisement
7
2
1
5
3
5
3
A
F
C
E
D
B
4
1
dst ¦ route ¦ cost |  |  |  | 
B | ¦ | A-B | ¦ | 3
C | ¦ | A-D | ¦ | 7
D | ¦ | A-D | ¦ | 2
E | ¦ | A-F | ¦ | 6
F | ¦ | A-F | ¦ | 1
A’s routing table

## Slide 45: link-state routing: disseminate full topology information so that nodes can run a shortest-path algorithm
its link costs to each of its neighbors
effectively, every other node (via flooding)
link state
what’s in an advertisement
who gets a node’s advertisement
7
2
1
5
3
5
3
A
F
C
E
D
B
4
1
dst ¦ route ¦ cost |  |  |  | 
B | ¦ | A-B | ¦ | 3
C | ¦ | A-D | ¦ | 7
D | ¦ | A-D | ¦ | 2
E | ¦ | A-F | ¦ | 6
F | ¦ | A-F | ¦ | 1
A’s routing table

## Slide 46: link-state routing: disseminate full topology information so that nodes can run a shortest-path algorithm
its link costs to each of its neighbors
effectively, every other node (via flooding)
link state
what’s in an advertisement
who gets a node’s advertisement
7
2
1
5
3
5
3
A
F
C
E
D
B
4
1
dst ¦ route ¦ cost |  |  |  | 
B | ¦ | A-B | ¦ | 3
C | ¦ | A-D | ¦ | 7
D | ¦ | A-D | ¦ | 2
E | ¦ | A-D | ¦ | 5
F | ¦ | A-F | ¦ | 1
A’s routing table

## Slide 47: link-state routing: disseminate full topology information so that nodes can run a shortest-path algorithm
link state
what’s in an advertisement
its link costs to each of its neighbors
who gets a node’s advertisement
effectively, every other node (via flooding)
7
2
1
5
3
5
3
A
F
C
E
D
B
4
1
we don’t need to “visit” F; we already know the shortest path to it
dst ¦ route ¦ cost |  |  |  | 
B | ¦ | A-B | ¦ | 3
C | ¦ | A-D | ¦ | 7
D | ¦ | A-D | ¦ | 2
E | ¦ | A-D | ¦ | 5
F | ¦ | A-F | ¦ | 1
A’s routing table

## Slide 48: link-state routing: disseminate full topology information so that nodes can run a shortest-path algorithm
its link costs to each of its neighbors
effectively, every other node (via flooding)
link state
what’s in an advertisement
who gets a node’s advertisement
7
2
1
5
3
5
3
A
F
C
E
D
B
4
1
dst ¦ route ¦ cost |  |  |  | 
B | ¦ | A-B | ¦ | 3
C | ¦ | A-D | ¦ | 7
D | ¦ | A-D | ¦ | 2
E | ¦ | A-D | ¦ | 5
F | ¦ | A-F | ¦ | 1
A’s routing table

## Slide 49: link-state routing: disseminate full topology information so that nodes can run a shortest-path algorithm
its link costs to each of its neighbors
effectively, every other node (via flooding)
link state
what’s in an advertisement
who gets a node’s advertisement
7
2
1
5
3
5
3
A
F
C
E
D
B
4
1
dst ¦ route ¦ cost |  |  |  | 
B | ¦ | A-B | ¦ | 3
C | ¦ | A-D | ¦ | 7
D | ¦ | A-D | ¦ | 2
E | ¦ | A-D | ¦ | 5
F | ¦ | A-F | ¦ | 1
A’s routing table

## Slide 50: link-state routing: disseminate full topology information so that nodes can run a shortest-path algorithm
link state
what’s in an advertisement
its link costs to each of its neighbors
who gets a node’s advertisement
effectively, every other node (via flooding)
7
2
1
5
3
5
3
A
F
C
E
D
B
4
1
notice that A’s route doesn’t change, but the cost needs to update
(and the actual path of the packets from A to C has changed)
dst ¦ route ¦ cost |  |  |  | 
B | ¦ | A-B | ¦ | 3
C | ¦ | A-D | ¦ | 6
D | ¦ | A-D | ¦ | 2
E | ¦ | A-D | ¦ | 5
F | ¦ | A-F | ¦ | 1
A’s routing table

## Slide 51: link-state routing: disseminate full topology information so that nodes can run a shortest-path algorithm
its link costs to each of its neighbors
effectively, every other node (via flooding)
link state
what’s in an advertisement
who gets a node’s advertisement
7
2
1
5
3
5
3
A
F
C
E
D
B
4
1
dst ¦ route ¦ cost |  |  |  | 
B | ¦ | A-B | ¦ | 3
C | ¦ | A-D | ¦ | 6
D | ¦ | A-D | ¦ | 2
E | ¦ | A-D | ¦ | 5
F | ¦ | A-F | ¦ | 1
A’s routing table

## Slide 52: link-state routing: disseminate full topology information so that nodes can run a shortest-path algorithm
its link costs to each of its neighbors
effectively, every other node (via flooding)
link state
what’s in an advertisement
who gets a node’s advertisement
7
2
1
5
3
5
3
A
F
C
E
D
B
4
1
dst ¦ route ¦ cost |  |  |  | 
B | ¦ | A-B | ¦ | 3
C | ¦ | A-D | ¦ | 6
D | ¦ | A-D | ¦ | 2
E | ¦ | A-D | ¦ | 5
F | ¦ | A-F | ¦ | 1
A’s routing table

## Slide 53: link-state routing: disseminate full topology information so that nodes can run a shortest-path algorithm
its link costs to each of its neighbors
effectively, every other node (via flooding)
link state
what’s in an advertisement
who gets a node’s advertisement
7
2
1
5
3
5
3
A
F
C
E
D
B
4
1
dst ¦ route ¦ cost |  |  |  | 
B | ¦ | A-B | ¦ | 3
C | ¦ | A-D | ¦ | 6
D | ¦ | A-D | ¦ | 2
E | ¦ | A-D | ¦ | 5
F | ¦ | A-F | ¦ | 1
A’s routing table

## Slide 54: link-state routing: disseminate full topology information so that nodes can run a shortest-path algorithm
its link costs to each of its neighbors
effectively, every other node (via flooding)
link state
what’s in an advertisement
who gets a node’s advertisement
7
2
1
5
3
5
3
A
F
C
E
D
B
4
1
what happens when things fail?
flooding makes link- state routing very resilient to failure
what limits scale?
the overhead of flooding

## Slide 55: Distance-vector Routing
In link-state, nodes calculate full shortest paths. But actually they only need the route (first-hop) to a destination
Advertisement format: Each node's advertisement is a list of all the nodes it knows about, and its current costs to those nodes
  Initially, this advertisement is just [(self, 0)].
Nodes who receive an advertisement: Node X's advertisement will be received only by its neighbors
Integrate step: When node X receives an advertisement from its neighbor Y, this advertisement will be a list of [(dst, cost)] pairs. Each cost represents Y's cost to dst

## Slide 56: Distance-vector Routing
For each (dst, cost) in the advertisement, X needs to check for two things:
  If X is already using Y to get to dst, update the cost information (remember, costs can change!)
  If X is not using Y to get to dst, see if Y could provide a better path; if so, update the routing and cost information

## Slide 57: distance-vector routing: disseminate information about the current costs to each node, rather than the actual topology
its link costs to each of its neighbors
effectively, every other node (via flooding)
link state distance vector
what’s in an advertisement
who gets a node’s advertisement
7
2
1
5
3
5
3
A
F
C
E
D
B
4
1
what happens when things fail?
flooding makes link- state routing very resilient to failure
what limits scale?
the overhead of flooding

## Slide 58: distance-vector routing: disseminate information about the current costs to each node, rather than the actual topology
its link costs to each of its neighbors
effectively, every other node (via flooding)
link state distance vector
what’s in an advertisement
who gets a node’s advertisement
7
2
1
5
3
5
3
A
F
C
E
D
B
4
1
what happens when things fail?
flooding makes link- state routing very resilient to failure
what limits scale?
the overhead of flooding
its current costs to
every node it’s aware of

## Slide 59: distance-vector routing: disseminate information about the current costs to each node, rather than the actual topology
its link costs to each of its neighbors
effectively, every other node (via flooding)
link state distance vector
what’s in an advertisement
who gets a node’s advertisement
7
2
1
5
3
5
3
A
C
F E
D
B
4
1
what happens when things fail?
flooding makes link- state routing very resilient to failure
what limits scale?
its current costs to
every node it’s aware of
A’s advertisement reflects its routing table, and right now, A only knows about its neighbors
the overhead of flooding
F
|
A-F
|
1
dst | route | cost
B | A-B | 7 D | A-D | 2
A’s first advertisement: [(B,7),(D,2),(F,1)]
A could also include (A,0) here
A’s routing table

## Slide 60: distance-vector routing: disseminate information about the current costs to each node, rather than the actual topology
its link costs to each of its neighbors
effectively, every other node (via flooding)
link state distance vector
what’s in an advertisement
who gets a node’s advertisement
7
2
1
5
3
5
3
A
C
F E
D
B
4
1
what happens when things fail?
flooding makes link- state routing very resilient to failure
what limits scale?
its current costs to
every node it’s aware of
F
|
A-F
|
1
A’s first advertisement: [(B,7),(D,2),(F,1)]
A could also include (A,0) here
A’s routing table
only its neighbors
dst | route | cost
B | A-B | 7 D | A-D | 2
the overhead of flooding
A’s advertisement reflects its routing table, and right now, A only knows about its neighbors

## Slide 61: distance-vector routing: disseminate information about the current costs to each node, rather than the actual topology
its link costs to each of its neighbors
effectively, every other node (via flooding)
link state distance vector
what’s in an advertisement
who gets a node’s advertisement
7
2
1
5
3
5
3
A
C
F E
D
B
4
1
what happens when things fail?
flooding makes link- state routing very resilient to failure
what limits scale?
its current costs to
every node it’s aware of
A’s first advertisement: [(B,7),(D,2),(F,1)]
A could also include (A,0) here
A’s routing table
only its neighbors
dst | route | cost
F
|
A-F
|
1
B | A-B | 7 D | A-D | 2
the overhead of flooding
A’s advertisement reflects its routing table, and right now, A only knows about its neighbors

## Slide 62: distance-vector routing: disseminate information about the current costs to each node, rather than the actual topology
its link costs to each of its neighbors
effectively, every other node (via flooding)
link state distance vector
what’s in an advertisement
who gets a node’s advertisement
7
2
1
5
3
5
3
A
C
F E
D
B
4
1
what happens when things fail?
flooding makes link- state routing very resilient to failure
what limits scale?
its current costs to
every node it’s aware of
A’s first advertisement: [(B,7),(D,2),(F,1)]
A could also include (A,0) here
A’s routing table
only its neighbors
dst | route | cost
F
|
A-F
|
1
B | A-B | 7 D | A-D | 2
the overhead of flooding
A’s advertisement reflects its routing table, and right now, A only knows about its neighbors

## Slide 63: distance-vector routing: disseminate information about the current costs to each node, rather than the actual topology
its link costs to each of its neighbors
effectively, every other node (via flooding)
link state distance vector
what’s in an advertisement
who gets a node’s advertisement
7
2
1
5
3
5
3
A
C
F E
D
B
4
1
what happens when things fail?
flooding makes link- state routing very resilient to failure
what limits scale?
its current costs to
every node it’s aware of
A’s first advertisement: [(B,7),(D,2),(F,1)]
A’s neighbors do not forward A’s advertisements; they do send advertisements of their own to A
only its neighbors
A’s routing table
dst | route | cost
F
|
A-F
|
1
B | A-B | 7 D | A-D | 2
the overhead of flooding

## Slide 64: distance-vector routing: disseminate information about the current costs to each node, rather than the actual topology
its link costs to each of its neighbors
effectively, every other node (via flooding)
link state distance vector
what’s in an advertisement
who gets a node’s advertisement
7
2
1
5
3
5
3
A
C
F E
D
B
4
1
what happens when things fail?
flooding makes link- state routing very resilient to failure
what limits scale?
its current costs to
every node it’s aware of
A’s first advertisement: [(B,7),(D,2),(F,1)]
A’s neighbors do not forward A’s advertisements; they do send advertisements of their own to A
only its neighbors
A’s routing table
dst | route | cost
F
|
A-F
|
1
B | A-B | 7 D | A-D | 2
the overhead of flooding

## Slide 65: distance-vector routing: disseminate information about the current costs to each node, rather than the actual topology
its link costs to each of its neighbors
effectively, every other node (via flooding)
link state distance vector
what’s in an advertisement
who gets a node’s advertisement
7
2
1
5
3
5
3
A
C
F E
D
B
4
1
what happens when things fail?
flooding makes link- state routing very resilient to failure
what limits scale?
its current costs to
every node it’s aware of
A’s first advertisement: [(B,7),(D,2),(F,1)]
A’s neighbors do not forward A’s advertisements; they do send advertisements of their own to A
only its neighbors
A’s routing table
dst | route | cost
F
|
A-F
|
1
B | A-B | 7 D | A-D | 2
the overhead of flooding

## Slide 66: distance-vector routing: disseminate information about the current costs to each node, rather than the actual topology
its link costs to each of its neighbors
effectively, every other node (via flooding)
link state distance vector
what’s in an advertisement
who gets a node’s advertisement
7
2
1
5
3
5
3
A
C
F E
D
B
4
1
what happens when things fail?
flooding makes link- state routing very resilient to failure
what limits scale?
its current costs to
every node it’s aware of
A’s first advertisement: [(B,7),(D,2),(F,1)]
A’s neighbors do not forward A’s advertisements; they do send advertisements of their own to A
only its neighbors
A’s routing table
dst | route | cost
F
|
A-F
|
1
B | A-B | 7 D | A-D | 2
the overhead of flooding

## Slide 67: distance-vector routing: disseminate information about the current costs to each node, rather than the actual topology
its link costs to each of its neighbors
effectively, every other node (via flooding)
link state distance vector
what’s in an advertisement
who gets a node’s advertisement
7
2
1
5
3
5
3
A
F
C
E
D
B
4
1
what happens when things fail?
flooding makes link- state routing very resilient to failure
what limits scale?
its current costs to
every node it’s aware of
B’s | first | adv: | [(A,7), | (C,3), | (D,1)] | 
D’s | first | adv: | [(B,1), | (C,5), | (E,3), | (F,4)(A,2)]
F’s | first | adv: | [(A,1), | (D,4), | (E,5)] | 
A receives advertisements
only its neighbors
from B, D, and F
the overhead of flooding
A’s routing table
dst | route | cost
F
|
A-F
|
1
B | A-B | 7 D | A-D | 2

## Slide 68: distance-vector routing: disseminate information about the current costs to each node, rather than the actual topology
its link costs to each of its neighbors
effectively, every other node (via flooding)
link state distance vector
what’s in an advertisement
who gets a node’s advertisement
7
2
1
5
3
5
3
A
F
C
E
D
B
4
1
what happens when things fail?
flooding makes link- state routing very resilient to failure
what limits scale?
its current costs to
every node it’s aware of
only its neighbors
the overhead of flooding
B’s | first | adv: | [(A,7), | (C,3), | (D,1)] | 
A’s routing table
dst | route | cost
F
|
A-F
|
1
B | A-B | 7 D | A-D | 2

## Slide 69: distance-vector routing: disseminate information about the current costs to each node, rather than the actual topology
its link costs to each of its neighbors
effectively, every other node (via flooding)
link state distance vector
what’s in an advertisement
who gets a node’s advertisement
7
2
1
5
3
5
3
A
F
C
E
D
B
4
1
what happens when things fail?
flooding makes link- state routing very resilient to failure
what limits scale?
its current costs to
every node it’s aware of
only its neighbors
the overhead of flooding
A’s routing table
dst | route | cost
F
|
A-F
|
1
B | A-B | 7 C | A-B | 10
D | A-D | 2
B’s | first | adv: | [(A,7), | (C,3), | (D,1)] | 
A's cost to B + B's cost to C

## Slide 70: distance-vector routing: disseminate information about the current costs to each node, rather than the actual topology
its link costs to each of its neighbors
effectively, every other node (via flooding)
link state distance vector
what’s in an advertisement
who gets a node’s advertisement
7
2
1
5
3
5
3
A
F
C
E
D
B
4
1
what happens when things fail?
flooding makes link- state routing very resilient to failure
what limits scale?
its current costs to
every node it’s aware of
only its neighbors
the overhead of flooding
A’s routing table
dst | route | cost
F
|
A-F
|
1
B | A-B | 7 C | A-B | 10
D | A-D | 2
B’s | first | adv: | [(A,7), | (C,3), | (D,1)] | 
D’s | first | adv: | [(B,1), | (C,5), | (E,3), | (F,4)(A,2)]
F’s | first | adv: | [(A,1), | (D,4), | (E,5)] | 

## Slide 71: distance-vector routing: disseminate information about the current costs to each node, rather than the actual topology
its link costs to each of its neighbors
effectively, every other node (via flooding)
link state distance vector
what’s in an advertisement
who gets a node’s advertisement
7
2
1
5
3
5
3
A
F
C
E
D
B
4
1
what happens when things fail?
flooding makes link- state routing very resilient to failure
what limits scale?
its current costs to
every node it’s aware of
only its neighbors
the overhead of flooding
A’s routing table
dst | route | cost
F
|
A-F
|
1
B | A-B | 7 C | A-B | 10
D | A-D | 2
D’s | first | adv: | [(B,1), | (C,5), | (E,3), | (F,4)(A,2)]

## Slide 72: distance-vector routing: disseminate information about the current costs to each node, rather than the actual topology
its link costs to each of its neighbors
effectively, every other node (via flooding)
link state distance vector
what’s in an advertisement
who gets a node’s advertisement
7
2
1
5
3
5
3
A
F
C
E
D
B
4
1
what happens when things fail?
flooding makes link- state routing very resilient to failure
what limits scale?
its current costs to
every node it’s aware of
only its neighbors
the overhead of flooding
A’s routing table
dst | route | cost
F
|
A-F
|
1
B | A-D | 3 C | A-B | 10
D | A-D | 2
D’s | first | adv: | [(B,1), | (C,5), | (E,3), | (F,4)(A,2)]

## Slide 73: distance-vector routing: disseminate information about the current costs to each node, rather than the actual topology
its link costs to each of its neighbors
effectively, every other node (via flooding)
link state distance vector
what’s in an advertisement
who gets a node’s advertisement
7
2
1
5
3
5
3
A
F
C
E
D
B
4
1
what happens when things fail?
flooding makes link- state routing very resilient to failure
what limits scale?
its current costs to
every node it’s aware of
only its neighbors
the overhead of flooding
A’s routing table
dst | route | cost
F
|
A-F
|
1
B | A-D | 3 C | A-D | 7
D | A-D | 2
D’s | first | adv: | [(B,1), | (C,5), | (E,3), | (F,4)(A,2)]

## Slide 74: distance-vector routing: disseminate information about the current costs to each node, rather than the actual topology
its link costs to each of its neighbors
effectively, every other node (via flooding)
link state distance vector
what’s in an advertisement
who gets a node’s advertisement
7
2
1
5
3
5
3
A
F
C
E
D
B
4
1
what happens when things fail?
flooding makes link- state routing very resilient to failure
what limits scale?
its current costs to
every node it’s aware of
only its neighbors
the overhead of flooding
A’s routing table
dst | route | cost
F
|
A-F
|
1
B | A-D | 3 C | A-D | 7
D | A-D | 2
E | A-D | 5
D’s | first | adv: | [(B,1), | (C,5), | (E,3), | (F,4)(A,2)]

## Slide 75: distance-vector routing: disseminate information about the current costs to each node, rather than the actual topology
its link costs to each of its neighbors
effectively, every other node (via flooding)
link state distance vector
what’s in an advertisement
who gets a node’s advertisement
7
2
1
5
3
5
3
A
F
C
E
D
B
4
1
what happens when things fail?
flooding makes link- state routing very resilient to failure
what limits scale?
its current costs to
every node it’s aware of
only its neighbors
the overhead of flooding
A’s routing table
dst | route | cost
F
|
A-F
|
1
B | A-D | 3 C | A-D | 7
D | A-D | 2
E | A-D | 5
B’s | first | adv: | [(A,7), | (C,3), | (D,1)] | 
D’s | first | adv: | [(B,1), | (C,5), | (E,3), | (F,4)(A,2)]
F’s | first | adv: | [(A,1), | (D,4), | (E,5)] | 

## Slide 76: distance-vector routing: disseminate information about the current costs to each node, rather than the actual topology
its link costs to each of its neighbors
effectively, every other node (via flooding)
link state distance vector
what’s in an advertisement
who gets a node’s advertisement
7
2
1
5
3
5
3
A
F
C
E
D
B
4
1
what happens when things fail?
flooding makes link- state routing very resilient to failure
what limits scale?
its current costs to
every node it’s aware of
only its neighbors
F’s first adv: [(A,1), (D,4), (E,5)]
the overhead of flooding
A’s routing table
dst | route | cost
F
|
A-F
|
1
B | A-D | 3 C | A-D | 7
D | A-D | 2
E | A-D | 5

## Slide 77: distance-vector routing: disseminate information about the current costs to each node, rather than the actual topology
its link costs to each of its neighbors
effectively, every other node (via flooding)
link state distance vector
what’s in an advertisement
who gets a node’s advertisement
7
2
1
5
3
5
3
A
F
C
E
D
B
4
1
what happens when things fail?
flooding makes link- state routing very resilient to failure
what limits scale?
its current costs to
every node it’s aware of
only its neighbors
this is A’s routing table after one round of advertisements; note that it does not have knowledge of the min-cost route to C yet
the overhead of flooding
A’s routing table
dst | route | cost
F
|
A-F
|
1
B | A-D | 3 C | A-D | 7
D | A-D | 2
E | A-D | 5

## Slide 78: distance-vector routing: disseminate information about the current costs to each node, rather than the actual topology
its link costs to each of its neighbors
effectively, every other node (via flooding)
link state distance vector
what’s in an advertisement
who gets a node’s advertisement
7
2
1
5
3
5
3
A
F
C
E
D
B
4
1
what happens when things fail?
flooding makes link- state routing very resilient to failure
what limits scale?
its current costs to
every node it’s aware of
only its neighbors
A’s second adv:
[(B,3), (C,7), (D,2), (E,5), (F,1)]
the overhead of flooding
A’s routing table
dst | route | cost
F
|
A-F
|
1
B | A-D | 3 C | A-D | 7
D | A-D | 2
E | A-D | 5

## Slide 79: distance-vector routing: disseminate information about the current costs to each node, rather than the actual topology
its link costs to each of its neighbors
effectively, every other node (via flooding)
link state distance vector
what’s in an advertisement
who gets a node’s advertisement
7
2
1
5
3
5
3
A
F
C
E
D
B
4
1
what happens when things fail?
flooding makes link- state routing very resilient to failure
what limits scale?
its current costs to
every node it’s aware of
only its neighbors
A’s second adv:
[(B,3), (C,7), (D,2), (E,5), (F,1)]
A will learn about the correct min-cost path to C in the next round of advertisements; try that out for yourself!
the overhead of flooding
A’s routing table
dst | route | cost
F
|
A-F
|
1
B | A-D | 3 C | A-D | 7
D | A-D | 2
E | A-D | 5

## Slide 80: distance-vector routing: disseminate information about the current costs to each node, rather than the actual topology
its link costs to each of its neighbors
effectively, every other node (via flooding)
link state distance vector
what’s in an advertisement
who gets a node’s advertisement
what happens when things fail?
what limits scale?
the overhead of flooding
its current costs to
every node it’s aware of
only its neighbors
7
2
1
5
3
5
3
A
F
C
E
D
B
4
1
failures can be complicated because of timing
failure handling
what happens when things fail?
flooding makes link- state routing very resilient to failure

## Slide 81: Problem of INFINITY
When a node A has no route to destination B, it will advertise a cost of INFINITY to B
  A cost of INFINITY B is interpreted as there being no route to B
  So INFINITY must be larger than the longest path in the network
But because the order in which advertisements are sent matters, sometimes nodes can incorrectly think there's a route when there isn't one
This can last for up to INFINITY steps

## Slide 82
A: Self, 0
B: A->B, 1
C: A->B, 2
A: B->A, 1
B: Self, 0
C: B->C, 1

## Slide 84
Notes: 从一端收到的路由信息，不能再从原路被发送回去。

## Slide 85: Link-State Summary
Pros:
  Fast convergence
Cons:
  flooding is costly: 2 x #Node x #Line advertisements
Only good for small networks

## Slide 86: Distance Vector
Pros:
  Low overhead: 2x #Line advertisements
Cons:
  Convergence time is proportional to longest path
  The infinity problem
Only good for small networks

## Slide 87
How to Scale the Routing?

## Slide 88: 3 Ways to Scale
Hierarchy of Routing
  Route between regions, and then within a region
Path-vector Routing
  Advertisements include the path, to better detect routing loops
Topological Addressing
  Assign addresses in contiguous blocks to make advertisements smaller

## Slide 89: Hierarchical Address Assignment & Routing
Two problems of the path vector implementation
  Every attachment point must have a unique address
  The path vector grows in size with the number of attachment points
Hierarchy for better scalability
  Two parts of network address: region & station, e.g., "11,75"
  Regions correspond to the set of closely-connected entities
  E.g., region-11 has only 1 entry in other region routers' table

## Slide 90: Hierarchical Address Assignment & Routing
Region is also as known as AS: Autonomous System

## Slide 91: Hierarchical Address Assignment & Routing
Problems introduced by hierarchy: more complex
  Binding address with location
    Has to change address after changing location
  Paths may no longer be the shortest possible
    Algorithm has less detailed information
More about hierarchy
  Can extend to more levels
  Different places can have different levels

## Slide 92: Routing Hierarchy
Across Region
  Use one routing protocol to route across regions, and a different protocol to route within regions
  Implies that there are devices on the edge of each region that can "translate" between or "speak" both protocols
BGP is the path-vector protocol used across regions
  Border Gateway Protocol

## Slide 93: Topological Addressing
Further reduce the routing table
  Despite being between regions, BGP still routes to IP addresses (e.g., to 18.0.0.1, not to region-3 )
  Addresses are given to regions in contiguous blocks, so that they can be specified succinctly via a particular notation ("CIDR" notation)
    CIDR: Classless Inter Domain Routing
  Keeps advertisements small
CIDR Notation

## Slide 94: Path Vector Exchange
Each participant maintains a path vector
  A complete path to some destination
  E.g., zero-length path to itself
  Gradually learns about other paths
  Construct a new forwarding table from its new path vector
Algorithm
  Advertising
  Path selection

## Slide 95: Path Vector Exchange
A
G
Need coordination to ensure no loop

## Slide 96
96

## Slide 97: Path Vector Exchange
Better for scaling
  Like Distance-Vector, but include the full path in the routing advertisements
  Overhead increases (advertises are larger), but convergence time decreases (avoid counting to infinity)
  Overhead is still lower than Link-State

## Slide 98: Questions on Path Vector
How do we avoid permanent loops?
  When a node updates its paths, it never accepts a path that has itself
What happens when a node hears multiple paths to the same destination?
  It picks the better path
What happens if the graph changes?
  Algorithm deals well with new links
  To deal with links that go down, each router should discard any path that a neighbor stops advertising

## Slide 99: Summary So Far
Feature | Interior Gateway Protocol (IGP) | Exterior Gateway Protocol (EGP)
Scope | Inside an Autonomous System (AS) | Between Autonomous Systems (AS)
Primary Goal | Find the best path; fast convergence | Apply routing policies; control path propagation
Typical Protocols | OSPF, IS-IS, RIP, EIGRP | BGP (the only one currently used)
Focus / Concern | Speed, efficiency, network topology | Policy, reachability, AS path
Scale | Manages hundreds to thousands of routes | Manages the global internet (hundreds of thousands of routes)

## Slide 100
Data Plane: Packet Forwarding

## Slide 101: Network Layer Interface
structure packet
bit_string source
bit_string destination
bit_string end_protocol
bit_string payload

## Slide 102
1 procedure NETWORK_SEND (segment_buffer, destination,
2 net_protocol, end_protocol)
3 packet instance outgoing_packet
4 outgoing_packet.payload ← segment_buffer
5 outgoing_packet.end_protocol ← end_protocol
6 outgoing_packet.source ← MY_NETWORK_ADDRESS
7 outgoing_packet.destination ← destination
8 NETWORK_HANDLE (outgoing_packet, net_protocol)
9 procedure NETWORK_HANDLE (net_packet, net_protocol)
10 packet instance net_packet
11 if net_packet.destination != MY_NETWORK_ADDRESS then
12 next_hop ← LOOKUP (net_packet.destination, forwarding_table)
13 LINK_SEND (net_packet, next_hop, link_protocol, net_protocol)
14 else
15 GIVE_TO_END_LAYER (net_packet.payload,
16 net_packet.end_protocol, net_packet.source)

## Slide 104: Forwarding an IP Packet
Lookup packet's destination in forwarding table
  If known, find the corresponding outgoing link
  If unknown, drop packet
Decrement TTL (Time To Live)
  Drop packet if TTL is zero
Update header checksum
Forward packet to outgoing port
Transmit packet onto link

## Slide 105: Data-plane Case Study: Intel's DPDK
DPDK: Data Plane Development Kit
  Bypass kernel
Network card
  Has several ports
  A port has RX/TX
Processor
  Read packets from RX
    Polling
  Find output port
  Write packets to TX
RX for receiving
TX for sending

## Slide 106: UC Berkeley’s RouteBricks [SOSP’09]

## Slide 107
NAT
(Network Address Translation)

## Slide 108: NAT (Network Address Translation)
Private network
  Public routers do not accept routes to network 10 (e.g., 10.8.8.8)
NAT router: bridge the private networks
  Router between private & public network
  Send: modify source address to temp public address
  Receive: modify back by looking mapping table
Limitations
  Some end-to-end protocols place address in payloads
  The translator may become the bottleneck
  What if two private network merge?

## Slide 109: NAT

## Slide 111
CASE: Ethernet Mapping
Mapping Internet to Ethernet

## Slide 112: Case Study: Mapping Internet to Ethernet
Listen-before-sending rule, collision
Ethernet: CSMA/CD
  Carrier Sense Multiple Access with Collision Detection
Ethernet type
  Experimental Ethernet, 3 mpbs
  Standard Ethernet, 10 mbps
  Fast Ethernet, 100 mbps
  Gigabit Ethernet, 1000 mbps

## Slide 113: Overview of Ethernet
A half duplex Ethernet
  The max propagation time is less than the 576 bit times, the shortest allowable packet
  So that two parties can detect a collision together
  If collision: wait random first time, exponential backoff if repeat
A full duplex & point-to-point Ethernet
  No collisions & the max length of the link is determined by the physical medium

## Slide 114: Difference between Hub and Switch
Hub
  A frame is "broadcast" to every one of its ports
  A 10/100Mbps hub must share its bandwidth with each port
Switch
  Keeps a record of the MAC addresses of all the devices
  A 10/100Mbps switch will allocate a full 10/100Mbps to each of its ports

## Slide 115: Broadcast Aspects of Ethernet
Broadcast network
  Every frame is delivered to every station
  (Compare with forwarding network)
ETHERNET_SEND
  Pass the call along to the link layer
ETHERNET_HANDLE
  Simple, can even be implemented in hardware

## Slide 116: Broadcast Aspects of Ethernet
procedure ETHERNET_HANDLE (net_packet, length)
destination ← net_packet.target_id
if destination = my_station_id
then
GIVE_TO_END_LAYER (net_packet.data,
net_packet.end_protocol,
net_packet.source_id)
else
ignore packet
no need to do any forwarding

## Slide 117: Broadcast Aspects of Ethernet
procedure ETHERNET_HANDLE (net_packet, length)
destination ← net_packet.target_id
if destination = my_station_id
or destination = BROADCAST_ID
then
GIVE_TO_END_LAYER (net_packet.data,
net_packet.end_protocol,
net_packet.source_id)
else
ignore packet

## Slide 118: Layer Mapping: Attach Ethernet to Forwarding Network
L sends a RPC to N by sending to station 18 of link 1
L sends a RPC to E by sending to K, E may have 15 as address, as well as M
15

## Slide 119: Layer Mapping
The Internet network layer
  NETWORK_SEND (data, length, RPC, INTERNET, N)
  NETWORK_SEND (data, length, RPC, ENET, 18)
L must maintain a table

## Slide 120: ARP (Address Resolution Protocol)
NETWORK_SEND ("where is M?", 11, ARP, ENET, BROADCAST)
NETWORK_SEND ("M is at station 15", 18, ARP, ENET, BROADCAST)
L asks E's Ethernet address, E does not hear the Ethernet broadcast, but the router at station 19 does, and it sends a suitable ARP response instead
Manage forwarding table as a cache

## Slide 121: ARP & RARP Protocol
Name mapping: IP address <-> MAC address

## Slide 122: ARP & RARP

## Slide 123: Network Topology
Take SJTU network for example
  Subnet: usually like 192.168.0.2 or 10.0.0.2
  Gateway: usually like 192.168.0.1
    Get the global IP address: 202.120.40.82
    A gateway usually has two (or more) IP address
  Proxy: get proxy's address
    E.g., 106.185.46.164 (Japan)

## Slide 124: Network Topology

## Slide 125: How to Use socket to Access www.baidu.com ?
You code as if your PC connect directly with Baidu
  Call connect() with Baidu's IP address
But how does the system find next hop?

## Slide 126: Putting All Together
App: I want to send a packet to Baidu, here is the packet with Baidu's IP in its header as target IP, and client's IP as source IP (Node-C)
OS: I don't know how to get to Baidu, I'll just send it to the router (gateway). But I cannot change the source IP of the packet, so I'll just change the MAC target address of the packet to the router's MAC address

## Slide 127: Putting All Together
The router-1 (gateway): I get a packet with my MAC as target address. Is it my IP? No… So I'll just forward it to next hop, by changing the target MAC address to next hop's MAC address (NAT: change source IP and source port as well)
Router-2: I connect directly to Baidu, I'll just change the target MAC address to Baidu

## Slide 128: ARP Spoofing
Construct spoofed ARP replies
A target computer could be convinced to send frames destined for computer A to instead go to computer B
Computer A will have no idea that this redirection took place
This process of updating a target computer's ARP cache is referred to as "ARP poisoning"

## Slide 129
A
IP:10.0.0.1
MAC:aa:aa:aa:aa
B
IP:10.0.0.2
MAC:bb:bb:bb:bb
Hacker
IP:10.0.0.3
MAC:cc:cc:cc:cc
switch
IP | MAC
10.0.0.2 | bb:bb:bb:bb
ARP cache
IP | MAC
10.0.0.1 | aa:aa:aa:aa
ARP cache
Spoofed ARP reply
IP:10.0.0.2
MAC:cc:cc:cc:cc
Spoofed ARP reply
IP:10.0.0.2
MAC:cc:cc:cc:cc
Spoofed ARP reply
IP:10.0.0.2
MAC:cc:cc:cc:cc

## Slide 130
A
IP:10.0.0.1
MAC:aa:aa:aa:aa
B
IP:10.0.0.2
MAC:bb:bb:bb:bb
Hacker
IP:10.0.0.3
MAC:cc:cc:cc:cc
switch
IP | MAC
10.0.0.2 | cc:cc:cc:cc
ARP cache
IP | MAC
10.0.0.1 | aa:aa:aa:aa
ARP cache
A's cache is poisoned

## Slide 131: ARP Spoofing
Now all the packets that A intends to send to B will go to the hacker's machine
Cache entry would expire, so it needs to be updated by sending the ARP reply again
  How often?
  depends on the particular system
  Usually every 40s should be sufficient
In addition the hacker may not want his Ethernet driver talk too much
  Accomplish with ifconfig -arp

## Slide 132: Man-in-the-Middle Attack
A hacker inserts his computer between the communications path of two target computers
The hacker will forward frames between the two target computers so communications are not interrupted
E.g., Hunt, Ettercap, etc.
  Can be obtained easily in many web archives

## Slide 133: Man-in-the-Middle Attack
The attack is performed as follows:
  Suppose X is the hacker's computer
  T1 and T2 are the targets
  X poisons the ARP cache of T1 and T2
  T1 associates T2's IP with X's MAC
  T2 associates T1's IP with X's MAC
  All of T1 and T2's traffic will then go to X first, instead of directly to each other

## Slide 134
T1
IP:10.0.0.1
MAC:aa:aa:aa:aa
T2
IP:10.0.0.2
MAC:bb:bb:bb:bb
Hacker
IP:10.0.0.3
MAC:cc:cc:cc:cc
switch
IP | MAC
10.0.0.2 | bb:bb:bb:bb
ARP cache
IP | MAC
10.0.0.1 | aa:aa:aa:aa
ARP cache
Spoofed ARP reply
IP:10.0.0.2
MAC:cc:cc:cc:cc
Spoofed ARP reply
IP:10.0.0.2
MAC:cc:cc:cc:cc
Spoofed ARP reply
IP:10.0.0.2
MAC:cc:cc:cc:cc

## Slide 135
T1
IP:10.0.0.1
MAC:aa:aa:aa:aa
T2
IP:10.0.0.2
MAC:bb:bb:bb:bb
Hacker
IP:10.0.0.3
MAC:cc:cc:cc:cc
switch
IP | MAC
10.0.0.2 | cc:cc:cc:cc
ARP cache
IP | MAC
10.0.0.1 | aa:aa:aa:aa
ARP cache
T1's cache is poisoned

## Slide 136
T1
IP:10.0.0.1
MAC:aa:aa:aa:aa
T2
IP:10.0.0.2
MAC:bb:bb:bb:bb
Hacker
IP:10.0.0.3
MAC:cc:cc:cc:cc
switch
IP | MAC
10.0.0.2 | cc:cc:cc:cc
ARP cache
IP | MAC
10.0.0.1 | aa:aa:aa:aa
ARP cache
Forged ARP replies
IP:10.0.0.1
MAC:cc:cc:cc:cc
Forged ARP replies
IP:10.0.0.1
MAC:cc:cc:cc:cc

## Slide 137
T1
IP:10.0.0.1
MAC:aa:aa:aa:aa
T2
IP:10.0.0.2
MAC:bb:bb:bb:bb
Hacker
IP:10.0.0.3
MAC:cc:cc:cc:cc
switch
IP | MAC
10.0.0.2 | cc:cc:cc:cc
ARP cache
IP | MAC
10.0.0.1 | cc:cc:cc:cc
ARP cache
T2's cache is poisoned

## Slide 138
T1
IP:10.0.0.1
MAC:aa:aa:aa:aa
T2
IP:10.0.0.2
MAC:bb:bb:bb:bb
Hacker
IP:10.0.0.3
MAC:cc:cc:cc:cc
switch
IP | MAC
10.0.0.2 | cc:cc:cc:cc
ARP cache
IP | MAC
10.0.0.1 | cc:cc:cc:cc
ARP cache
Message intended to send to T2
Hacker will
relay the
message

## Slide 139
T1
IP:10.0.0.1
MAC:aa:aa:aa:aa
T2
IP:10.0.0.2
MAC:bb:bb:bb:bb
Hacker
IP:10.0.0.3
MAC:cc:cc:cc:cc
switch
IP | MAC
10.0.0.2 | cc:cc:cc:cc
ARP cache
IP | MAC
10.0.0.1 | cc:cc:cc:cc
ARP cache
Hacker will relay the message
Message
intended to
send to T1

## Slide 140: Defenses against ARP Spoofing
No Universal defense (!)
Use static ARP entries
  Cannot be updated; Spoofed ARP replies are ignored
  ARP table needs a static entry for each machine on the network
  Large overhead
    Deploying these tables; Keep the table up-to-date
Arpwatch
  A free UNIX program which listens for ARP replies on a network
  Build a table of IP/MAC associations and store it in a file
  When a MAC/IP pair changes (flip-flop), an email is sent to an administrator

## Slide 141
Case Study: BGP
Border Gateway Protocol

## Slide 142: Policy Routing
Regions also want to implement their own policies
  Switches make routing decisions based on some policies set by a human
  Routing protocol must disseminate enough info to enable those policies
What policies are typical in BGP?
  Regions don't want to send traffic on a path unless they have financial incentive to do so
  Mechanism of enforcement: selective advertisements
    Region-1 won't tell region-2 about a path unless it will make money by letting region-2 use the path
    Each region will have a different view of the network, and that view will (almost certainly) not contain every physical link

## Slide 143: Typical BGP Relationships
Customer/provider
  Customers pay for access (transit), which the provider provides
Peers
  Peers provide mutual access to a subset of each's routing tables
    The subset that contains their transit customers
  Why peer? Can save money and improve performance
  Why not peer? You'd rather have customers

## Slide 144: Customers and Peers
Customer/Provider ("transit")
  Customer pays provider for transit
Peers
  Peers allow (free) mutual access to each other's customers

## Slide 145: Customers and Peers
Customer/provider ("transit")
  Providers tell everyone about themselves their customers
  and tell their customers about everyone
Peers
  Peers tell each other about their customers

## Slide 146: Import Policies
Customer > peer > provider
  And then a variety of other attributes when this rule isn't sufficient
Goal: make money

## Slide 147: An Example
Z will tell X about C; C is a customer of Z, and X and Z are peers
X will tell Z and Y about C1, C2, and C3
Y will tell X about D
X will not tell Y about C; it makes no money to provide transit from Y to C
X doesn't tell Y about T; it would lose money to provide transit from Y to T
In example, Y appears disconnected from part of the network

## Slide 148: An Example
BGP doesn't prevent this. In practice, it never happens. Because:
  Almost every AS is a customer of someone else (i.e., Y would buy transit from someone)
  Typically: small ASes buy Internet from Tier-3 ISPs, which buy Internet from Tier-2 ISPs, which buy Internet from Tier-1 ISPs. Tier-1's are huge; there are only a handful (10-15)
  Additionally, all Tier-1 ISPs peer with one another. So each Tier-1 ISP can provide global connectivity

## Slide 149: BGP in Distributed Routing
HELLO protocol
  BGP sends KEEPALIVE messages to neighbors
Advertisements: Sent to neighbors
  BGP runs on top of TCP
  Doesn't have to do periodic advertisements to handle failure
Integration: via policies described above
Failures: routes can be explicitly withdrawn in BGP if fail
  Routing loops avoided because BGP is path-vector

## Slide 150: Problems with BGP
Does it scale?
  Yes, it works on the Internet
  But, BGP routing tables are getting big
  Route instability due to misconfigurations or conflicting policies
  One region can buy Internet from more than one ISP -> bigger table
Is it simple?
  Yes to the protocol, but no to the implementation & operation
Is it secure?
  No. A region can advertise a fake vector

## Slide 151: 2017: BGP hijacking! Traffic for Google, Apple, Facebook, Microsoft and other tech giants routed through Russia
http://securityaffairs.co/wordpress/66838/hacking/bgp-hijacking-russia.html