## Slide 1: Distributed training & RDMA (Advanced topic)
SE3331-1 (2025 Fall)
Credits: AI-sys Sp22, CMU15-418
Xingda Wei, Yubin Xia
IPADS, Shanghai Jiao Tong University
https://www.sjtu.edu.cn

## Slide 2: Review: The computation graph abstraction
Computations are expressed as a graph (Directly acrylic graph)
  Vertices are computations (or data)
  Edges are communication channels
  Each vertex has several input and output edges
Inputs
Outputs
Channels (file, pipe, memory)
Processing Vertices

## Slide 3: Case study: Distributed training

## Slide 4: Pseudocode for Stochastic Gradient Descent
// execute on a master
for iter in num_iters:
iter+1
iter
iter
Problem: the graph cannot be parallelized across different nodes!

## Slide 5: Review: Parallelization Opportunities
Data Parallelism: Distribute the processing of data to multiple PEs.
Model Parallelism: Break the model and distribute processing of every layer to multiple PEs
For either approach it is also possible to use synchronous or asynchronous updates

## Slide 6: (Sync) data parallel

## Slide 7: Pseudocode for (iterative) data parallel in action
// high-level code
for iter in num_iters:
iter+1
iter
iter

## Slide 8: Design goal: high GPU utilization (MFU)
Model FLOPs Utilization
Depends on several factors
  Whether the forward + backward can fully utilize the GPUs? (See the last lecture)
  Can we hide the GPU idle time? Yes, via overlapping
  Optimize the synchronization part
0
1
Forward + backward
Sum

## Slide 9: Key operator: allreduce
GPU 2
GPU 3
GPU 4
GPU 1
ALLREDUCE

## Slide 10: Review: parameter server
Each process pushes the data to the parameter server (PS)
After receiving all data, aggregate the data at the PS
3. The PS pushes the data back to the processes
0
1
PS
+
=
Step #1
Step #2
Step #3

## Slide 11: Review: Co-located & sharded PS
The PS is collocated on all the servers
Each server handles the reduce of a portion of data
0
1
2
0
1
2
0
1
2
0
1
2
0
0
0
0
0
Benefit: the inbound bandwidth requirement is reduced by #P

## Slide 12: Review: Decentralized approach w/ only peer connections
Peer connections: GPU 1 only connects to GPU 0 and 2 (its neighbors)
  Question: do the send of GPU to GPU2 needs coordination?
12
0
1
2
3
0 1 2 3

## Slide 13: Try #3: Ring allreduce
Decentralized reduce, each process reduce on a partitioned data (prev/next to it)
  i.e., each process send one partition, compute it, & then sends to the next process
13
0
1
2
3
0 1 2 3
1
0
2
3
1
2
3
0
3
0
1
2

## Slide 14: Ring allreduce
After the individual reduce, each process can scatter to collect results
  Eventually, all the processes will have the same reduced data
0
1
2
3
Question: different partition has a different reduce order, does it ok?

## Slide 15: Why ring allreduce can work?
Assumption: reduce op is associative & communicative
  So we can reorder them to reduce sudden loads at a node
  E.g., we don’t need to collect all the data to do the reduce
Otherwise, we cannot reorder the computation

## Slide 16: Analysis of the communication cost of ring allreduce
N: total parameters, P: # processors
Total communication per-machine
  2 * (P-1) * N / P: the same as partitioned
  O(1) fan-in
Total communication rounds: O(P)
  Much higher than the parameter server approach (O(1))
  A trade-off for reducing network contention due to high fan-in
What are the drawback?
  High latency due to extra rounds

## Slide 17: Allreduce: put it all together
Trade-off between rounds vs. fan-in performance
  P: # processors/machines/GPUs participated in the computation
  N: the size of the data to be reduced
 | Round | Peak node bandwidth | Per-node fan-in
Parameter server (PS) | O(1) | O(N * P) | O(P)
Co-located & sharded PS | O(1) | O(N/P) | O(P)
Decentralized Allreduce | O(P) | O(N) | O(1)
Ring allreduce | O(2 * P) | O(N/P) | O(1)

## Slide 18: More reduce method: Double Binary Tree All-Reduce
https://devblogs.nvidia.com/massively-scale-deep-learning-training-nccl-2-4/
Two overlaid binary reduction trees
Double the fan-in  Log(p) rounds of communication
  Currently used on the NCCL

## Slide 19: More reduce methods exist
Key design goals
  Reduce payload sent per-node
  Reduce fan-in to avoid contention on network resource
  Reduce rounds (grow linearly w/ the number of processors)
  (new) Better suits the underlying hardware (Cloud & HPC)
  (new) In-network computing (e.g., NVIDIA SHARP)
Still an active research field
  E.g., what if the hardware speed between different machines diff?
  What if the link speed changes overtime?

## Slide 20: Case study: NVLink + RDMA
Setup
  Each machine has multiple GPUs for computation
  These GPUs essentially form a distributed (processing) system
NVLink
  Fast interconnects that connect different GPUs
RDMA (Described later)
  Fast networking feature that connects different machines

## Slide 21: What does NVLink Look Like?
8-GPU on single board

## Slide 22: Communication heterogeneity
Different nodes’ link capacity differs
  Internode: high bandwidth (e.g., 450GBps)
  Intranode: relative slow bandwidth (e.g., 100GBps)
Optimization opportunities
  We can do a parameter server within a server, and do rings across servers
  We will see more examples later
GPU 0
GPU 1
GPU 2
GPU 3
GPU 0
GPU 1
GPU 2
GPU 3
NVLink
NVLink
RDMA
Server

## Slide 23: Parallelization Opportunities
Data Parallelism: Distribute the processing of data to multiple PEs.
Model Parallelism: Break the model and distribute processing of every layer to multiple PEs
For either approach it is also possible to use synchronous or asynchronous updates

## Slide 24: Recall: Data Parallelism
Forward
Backward
w
X0
X1
Y0
Y1
w
Forward
Backward
1
Sum
0
Question: What is the assumption of W?

## Slide 25: Drawback of data parallelism: replicated model
Data parallelism assumes the model (parameters) are replicated on all the processes
  Such that they can do the forward & backward pass dependently
  What if the model cannot fit onto the device?
Current trends: models are becoming larger and larger
  No country (or company) can tolerate the risk of falling behind in the AI race

## Slide 26: Trend: Training Large Models
Amir Gholami, Zhewei Yao, Sehoon Kim, Michael W. Mahoney, Kurt Keutzer, AI and Memory Wall, Riselab Medium Blogpost, 2021.
Beyond single chip memory

## Slide 27: Model parallelism
Partition the parameters of a model, typically done in two ways:
  Partition on the layer: pipeline parallelism
  Partition on the W: tensor parallelism
Forward
w
X
Y
W1
W2

## Slide 28: Pipeline parallelism
Partition the computation layer-by-layer, each partition is deployed on a device
  Note that different layers can be grouped together
  The strategy is out of the scope of this course
Layer #1
w1
X
Y
Layer #2
w2
The model
The partitioned computation graph

## Slide 29: Pipeline parallelism
Time
Bubble where processes are idle
How to reduce bubble?
Note that each stage may contain multiple layers, where the detailed number is configurable

## Slide 30: Technique: micro-batching
Reducing the bubble size by breaking the batch size into smaller pieces to reduce the idle time of the processes
  Reduces bubble size in an easy way to implement
Question: to what extent can micro-batching improves performance?
  The bubble size depends on the #partitions (p)
  The ratio bubble overhead depends on the overall pipeline numbers (m)
m
p

## Slide 31: Pipeline parallelism & the number of micro-batch
Question: what is the bubble size ?
  p – 1 (p == #devices)
Question: what is the overhead?
  : time of a forward of a micro-batch (m)
  : time of a backward of a micro-batch (m)
  Ideal process time:
  Wasted time of bubble:
  Bubble time fraction:

## Slide 32: Pipeline parallelism & the number of micro-batch
Question: what is the overhead of pipeline parallelism?
  Bubble time fraction:
Optimization directions
  1. increase m (e.g., increase the batch size)
  2. reduce p (reduce the #partitions)

## Slide 33: Why increase M requires increasing the batch size?
A too small batch size is inefficient in GPU utilization
  Intuitively, the W is reused across each request
  Thus, increase batch size by 2X would lead to only < 2X increased execution time
P0
P1
P0
P1
*
di
B
W
X
di
  Case study: LLM inference performance (see Fast LLM Post-training via Decoupled and Fastest-of-N Speculation)

## Slide 34: Problems with Large Batch Training
Larger Batch leads to sub-optimal generalization
A common belief is that large batch training gets attracted to “sharp minimas”
Keskar et al., On Large-Batch Training for Deep Learning: Generalization Gap and Sharp Minima, ICLR’16.
Z. Yao, A. Gholami, Q. Lei, K. Keutzer, M. Mahoney. Hessian-based Analysis of Large Batch Training and Robustness to Adversaries, NeurIPS’18.
Ginsburg, Boris, Igor Gitman, and Yang You. "Large Batch Training of Convolutional Networks with LARS." arXiv:1708.03888, 2018.
Key takeaway: improving system should consider application properties

## Slide 35: Problems with large batch size
P#0. (Possible) Decreased accuracy
P#1. Increased memory at each device
  Memory used for storing the activation memory
Though some optimizations exist
  E.g., Re-computation, throw away the intermedia activations generated during the forward path, re-compute it during the backward path
  Cons: trades performance for memory usage

## Slide 36: Can we reduce the number of pipeline stages (p)?
Typically, also challenging because AI models are really really large
Example: GPT-4
  Setup: 1.8 trillion parameters
  120 layers
  Assuming 4B for each parameter, we have 60 GB per-layer
What are the memory capacity of GPU?
  80 GB for H100, 140 GB for H200
  Note that we also need to store activations & input data ( & optimization state)

## Slide 37: Tensor parallelism (TP)
Partition the parameters of a layer
  Each partition is deployed on a separate GPU
A group of GPUs hosting a complete set of W is treated as a large logical GPU to simplify the analysis
Layer #1
w1
X
Y
Layer #2
w2

## Slide 38: Model Parallelism (use matrix multiplication as an example): Forward Pass
P0
P1
P0
P1
*
di/P
di
B
W
X
di
P0
P1
di/P
B
Ylocal
P0
P1
Y
Requires an all gather communication so that all processes get each others activation data
Suppose with a simple forward, each node needs to send ~=
Notes: \begin{align*}
\sum_{i=1}^{L} \beta (P-1) \frac{Bd_i}{P}\right)
\end{align*}
\begin{align*}
T_{{comm}}({domain}) = &\sum_{i=1}^{L}\left(\alpha {\log(P)}+ \beta \frac{P-1}{P} Bd_i\right)\\
+2&\sum_{i=2}^{L}\left(\alpha {\log(P)}+ \beta \frac{P-1}{P} d_{i-1}\right)
\end{align*}

## Slide 39: Model Parallelism: Backward Pass
P0, P1
*
XT
∇Y
P0
P1
di/P
∇W
No communication needed as every processor only needs the gradient of its own parameters
P0
P1
Notes: \begin{align*}
\sum_{i=1}^{L} \beta (P-1) \frac{Bd_i}{P}\right)
\end{align*}
\begin{align*}
T_{{comm}}({domain}) = &\sum_{i=1}^{L}\left(\alpha {\log(P)}+ \beta \frac{P-1}{P} Bd_i\right)\\
+2&\sum_{i=2}^{L}\left(\alpha {\log(P)}+ \beta \frac{P-1}{P} d_{i-1}\right)
\end{align*}

## Slide 40: Backward Pass
P0
P1
P0
P1
*
di/P
di
B
WT
∇Y
di
P0
P1
∇X local
P0
P1
∇X
Aggregating input gradient requires an allreduce operation
Cost (using ring): )
Notes: \begin{align*}
2\sum_{i=2}^{L}\left(\beta (P-1) \frac{Bd_i}{P}\right)
\end{align*}

## Slide 41: The cost of model parallelism
Networking cost during model parallelism
0
0
The network communication time

## Slide 42: Analysis of the network cost of model parallelism
One layer (deployed on 2 GPUs w/ Tensor parallelism)
One layer (deployed on 2 GPUs w/ Tensor parallelism)
Pipeline parallelism
  See: Attention is all you need

## Slide 43: Analysis of the network cost of model parallelism
P0
P1
P0
P1
*
di/P
di
B
W1
X
di
P0
P1
di/P
B
Ylocal
P0
P1
Y
[Y] = max(0, Y)
P0
P1
Y’

## Slide 44: Analysis of the network cost of model parallelism
P0
P1
P0
P1
*
di/P
di
B
W2
Y’
di
P0
P1
di/P
B
Zlocal
P0
P1
Z

## Slide 45: Analysis of the network cost of model parallelism
One layer (deployed on 2 GPUs w/ Tensor parallelism)
One layer (deployed on 2 GPUs w/ Tensor parallelism)
Pipeline parallelism
Z
Tensor parallelism cost:
Forward ~=
Backward ~=
Note that the actual cost is much higher because we need to consider other blocks like attention (model-specific details are out of the scope of this lecture), and possible multiple layers per pipeline stage

## Slide 46: Analysis of the network cost of model parallelism
One layer (deployed on 2 GPUs w/ Tensor parallelism)
One layer (deployed on 2 GPUs w/ Tensor parallelism)
Pipeline parallelism
Z
Pipeline parallelism cost:
Forward ~=
Backward ~=

## Slide 47: Review: Communication heterogeneity
Different nodes’ link capacity differs
  Internode: high bandwidth (e.g., 450GBps)
  Intranode: relative slow bandwidth (e.g., 100GBps)
Optimization opportunities
  We can do a parameter server within a server, and do rings across servers
GPU 0
GPU 1
GPU 2
GPU 3
GPU 0
GPU 1
GPU 2
GPU 3
NVLink
NVLink
RDMA
Server
Layers with TP

## Slide 48: Review: Communication heterogeneity
Different nodes’ link capacity differs
  Internode: high bandwidth (e.g., 450GBps)
  Intranode: relative slow bandwidth (e.g., 100GBps)
Optimization opportunities
  We can do a parameter server within a server, and do rings across servers
GPU 0
GPU 1
GPU 2
GPU 3
GPU 0
GPU 1
GPU 2
GPU 3
NVLink
NVLink
RDMA
Server
Layers with TP
A layer with TP
PP

## Slide 49: The US conducted a GPU ban on China, mainly restricting GPU communication performance

## Slide 50: Case study: A100 vs. A800
Notes: * 采用稀疏技术

## Slide 51: Summary: model parallelism
Two forms: pipeline parallelism + tensor parallelism
Pipeline parallelism
  Partition the computation graph by layers
  Pros: reduced communication
  Cons: bubbles
Tensor parallelism
  Partition the parameters of a layer (or a set of layers )
  Pros: better support for large models
  Cons: high communication cost
Key system design principles: algorithm-hardware-aware co-design

## Slide 52: Put it altogether: parallelize distributed training

## Slide 53: Parallelization Opportunities
Data Parallelism: Distribute the processing of data to multiple PEs.
Model Parallelism: Break the model and distribute processing of every layer to multiple PEs
For either approach it is also possible to use synchronous or asynchronous updates

## Slide 54: Recall: data parallel execution
Machine 1
Machine 2
Machine 3
Iteration
Iteration
Iteration
Barrier
Compute
Communicate
Iteration
Iteration
Iteration
Compute
Waste
Waste
Barrier
Waste
w
w
w
w1
w2
w3
w
w
w
Allreduce
Problem: may have idle time at each process due to stragglers

## Slide 55: Straggler is also common, e.g., in LLM post-training
  Source: LLM inference performance (see Fast LLM Post-training via Decoupled and Fastest-of-N Speculation)

## Slide 56: Asynchronous Execution
Key idea: each process does not wait for others
  Update the gradients upon receive a messages, no iteration barrier
Machine 1
Machine 2
Machine 3
Iteration
Iteration
Iteration
Compute
Communicate
Iteration
Iteration
Iteration
Compute

## Slide 57: Async vs. Sync execution
Async
  Pros: efficiency
  Cons: trade accuracy for performance
Sync
  Pros: Preserve the SGD training property
  Cons: poor performance
Which is better?
  Hard to tell. But, as a system designer, preserving the algorithms property is very important. Any design that alter the training property should be justified
Common: nearly all (pre) training currently adopts a synchronous approach

## Slide 58: Advanced topic: RDMA Fast networking powering modern datacenter applications

## Slide 59: Networking is a key component in distributed systems
File server
File:
image
File server
File:
image
File server
File:
image
…
Distributed file system
Database server
Database
user, price
Database server
Database
user, price
…
Distributed database
Caching
Caching server
Caching
Caching server
Caching
Caching server
…
Distributed caching
Load
Balance
Application #1
generate the page
Application server
Application #2
add the order
Application server
…
Internet
…
Users
CDN
Message queue
Example: large-scale websites
  How each component communicates? Networking!

## Slide 60: An overview of traditional networking
OSI
  The open systems interconnection (OSI) model
  7-layer architecture

## Slide 61: The OS implements the traditional network stack
CPU copy
CPU copy
DMA copy
DMA copy
Protocol
Processing

## Slide 62: The OS implements the traditional network stack
Linux provides simple socket interfaces
  socket()
  bind()
  listen()
  connect()
  accept()
  read()
  write()
Can be a little complex if want high-performance
  epoll(), etc
Does the software interfaces
that simple as it seems?

## Slide 63: Packet processing in Linux
User space
Kernel space
Network card
  TX/RX queues
  Ring Buffer
  Driver
  TCP/IP
  Socket
  Application
  read(), write()

## Slide 64: Linux networking software stack

## Slide 65: What are the costs of such a complex networking stack?
Physical limit | ~1-10us
Linux/TCP/IP/stack | ~50-200us
Apps (e.g. KV) latency | ~8-100us
Notes: 包括call kernel的overhead和kernel-space 处理的开销

## Slide 66
Maybe work for 10Gbps network
But what about 100Gbps?

## Slide 67: What are the costs of such a complex networking stack?
Physical limit | ~1-10us
Linux/TCP/IP/stack | ~50-200us
Apps (e.g. KV) latency | ~8-100us
Can we remove the
kernel overhead?

## Slide 68: Kernel-bypassing network
DPDK
  Set of user-space driver library to use the network card
DPDK directly exposes network queues to the user-space
  Forward network packets to/from NIC from/to user applications
    Without any kernel networking stack!
How to achieve so?
  OS will map the NIC’s TX (transmit queue) and RX (receive queue) to the user-land

## Slide 69: Packet processing with DPDK
User space
Kernel space
Network card
  TX/RX queues
  Ring Buffer
  Application
  DPDK

## Slide 70: Pros & Cons of DPDK
Pros
  Bypasses the kernel
  Reduced memcpy overhead
  User can customize the networking, e.g., not using TCP/IP
    E.g., co-design key-value store w/ DPDK (MICA@SIGCOMM’14)
Cons
  Not compatible to traditional networking
  Still need a transport layer at the user applications, e.g., mTCP
    Which has non-trivial overheads
Can we put the networking stack into the hardware?

## Slide 71: RDMA: offload the complete network stack to the NIC
RDMA = Remote Direct Memory Access
Direct memory-to-memory data communication over network.

## Slide 72: RDMA: offload the complete network stack to the NIC
RDMA is a Trending Topic in Cloud Systems.

## Slide 73: RDMA implementations: IB
Native infiniband (IB)
  Complete new protocol stack
  Best Performance
  Need specialized IB NIC and IB Switch (High Cost)

## Slide 74: RDMA implementations: RoCE-v1
RDMA over Converged Ethernet Version 1
  Based on Ethernet in link layer.
    Compatible with the current network infrastructure.

## Slide 75: RDMA implementations: RoCE-v2
RDMA over Converged Ethernet Version 1
  Carried by IP and UDP in network layer.
  More flexible & scalable than RoCE v1
  Most cloud datacenters choose RoCEv2 for large-scale deployments.

## Slide 76: RDMA implementations: iWrap
An attempt to patch up on existing LAN/WAL network
  Layered on existing TCP/IP protocols
  In contrast, RoCE is a purpose-built RDMA transport protocol for Ethernet

## Slide 77
Programming w/ RDMA (verbs)
The API is simplified for hardware offloading!
Notes: https://ongardie.net/static/raft/userstudy/

## Slide 78: High-level concepts of RDMA
Queue Pairs (Send Queue, Complete Queue and Receive Queue)
  SQ, CQ & RQ
  A group of queues form an RDMA connection
    Analog to connections in TCP/IP
User posts networking requests to the SQ
  Two-sided: message datagram (like send/recv)
  One-sided: remote read/write (will be talked about later)
Get the completion events of the send requests from the CQ
Receive two-sided messages from the RQ
Message buffers must be pre-allocated

## Slide 79: Queue Pairs have different models
Reliable connected (RC)
  Like TCP/IP socket, provides reliable communications, supports all RDMA requests
Unreliable datagram (UD)
  Like UDP socket
  No reliability guarantees, limited RDMA requests type supported
Others
  Less commonly used
We focus on RC queue pair in this lecture

## Slide 80: Reliable connection Queue Pairs (QP)s
Two QP must first establish a connection via handshake so as to proceed
  Similar to handshakes in TCP/IP
  We will talk about the connection establishment later
An reliable connection QP must be only connected to one other
Send
Comp
Recv
Send
Comp
Recv
Queue
pairs
Queue
pairs
RDMA
Pair

## Slide 81: RDMA queue pair bring up
(Reliable connected) Queue pairs (QP) are connected before can be used
  Simplify reliable guarantees, etc.
  We call this bring up QP in this lecture
RDMA needs a handshake protocol to bring up two QPs
  Similar to TCP/IP handshake, but is not specified by the protocol
Send
Comp
Recv
Send
Comp
Recv
Queue
pairs
Queue
pairs
RDMA
Pair

## Slide 82: First step: RDMA queue pair bring up
Needs to exchange a piece of connection data by the applications
  Not specified in the RDMA specification!!!
Users typically implements their own exchange method
  Typically, through another network: TCP/UDP, etc.
Queue
pairs
Network
RDMA

## Slide 83: RDMA queue pair bring up
Requester creates its queue pairs
Queue
pairs
Network
RDMA
Send
Comp
Recv

## Slide 84: RDMA queue pair bring up
Requester creates its queue pairs
Extract the queue pair information (via query_qp), send to the responder
Queue
pairs
RDMA
Send
Comp
Recv
query_qp
Network
Notes: d

## Slide 85: RDMA queue pair bring up
Requester creates its queue pairs
Extract the queue pair information (via query_qp), send to the responder
(Optional) Responder creates its queue pairs
  If it already has a created queue pair, can be ignored
Queue
pairs
RDMA
Send
Comp
Recv
query_qp
Network
Send
Comp
Recv
Notes: d

## Slide 86: RDMA queue pair bring up
Requester creates its queue pairs
Extract the queue pair information, send to the responder
(Optional) Responder creates its queue pairs
Responder modify its queue pair to a connected state
Queue
pairs
Send
Comp
Recv
Network
Send
Comp
Recv
ibv_modify_qp()...
RDMA
Note that the hardware will do
all the connections in the modify QP
Notes: d

## Slide 87: RDMA queue pair bring up
Extract the queue pair information, send to the requester
Queue
pairs
Send
Comp
Recv
Send
Comp
Recv
RDMA
query_qp
Network
Notes: d

## Slide 88: RDMA queue pair bring up
Extract the queue pair information, send to the requester
Requester modify its queue pair to a connected state with the received queue pair information
Queue
pairs
Send
Comp
Recv
Send
Comp
Recv
RDMA
Network
ibv_modify_qp()...
Notes: d

## Slide 89: RDMA queue pair bring up
Extract the queue pair information, send to the requester
Requester modify its queue pair to a connected state with the received queue pair information
Done!
  Both queue pairs can send/receive RDMA requests from the others
Send
Comp
Recv
Send
Comp
Recv
Queue
pairs
Queue
pairs
RDMA
Pair
Notes: d

## Slide 90: Next: send message with RDMA
RDMA
“Hello”
Bob
Alice
Send
Comp
Recv
Send
Comp
Recv
Queue
pairs
Queue
pairs

## Slide 91: Register a message buffer to receive incoming message
RDMA
“Hello”
Bob
Alice
Send
Comp
Recv
Send
Comp
Recv
Queue
pairs
Queue
pairs
struct ibv_sge list = { .addr = msg_buf, .length=5 };
struct ibv_recv_wr wr = {
.sg_list = &list,
..., // other fields
};
ibv_post_recv(alice_qp, &wr, ...); // post to the receive queue
Alice
ibv_post_recv

## Slide 92: Send the message with post_send
RDMA
“Hello”
Bob
Alice
Send
Comp
Recv
Send
Comp
Recv
Queue
pairs
Queue
pairs
struct ibv_sge list = { .addr = (uintptr_t)"Hello", .length=5 };
struct ibv_send_wr wr = {
.sg_list = &list,
.op_code = IBV_WR_SEND // send a two-sided message
..., // other fields
};
ibv_post_send(bob_qp, &wr, ...); // send queue
bob

## Slide 93: Poll the completion of the send via polling
RDMA
“Hello”
Bob
Alice
Send
Comp
Recv
Send
Comp
Recv
Queue
pairs
Queue
pairs
do {
num_completions = ibv_poll_cq(bob_com_qp, ...);
} while (num_completions == 0);
// The request has been successfully sent to the remote
// or an error happens
bob

## Slide 94: Poll the received message from Alice
RDMA
“Hello”
Bob
Alice
Send
Comp
Recv
Send
Comp
Recv
Queue
pairs
Queue
pairs
do {
num_completions = ibv_poll_cq(alice_receive_qp, ...);
} while (num_completions == 0);
// The message must be stored in msg_buf if no error
Print(msg_buf) // Hello
bob

## Slide 95: Lifecycles of the sent message
Secrets behind RDMA: MMIO & DMA
  MMIO: Using LOAD and STORE
  DMA: Device directly read/write the memory (provided by PCIe)
Credit: Anuj Kalia’s SIGCOMM talk
CPU,RAM
NIC
RAM
NIC
1. Request descriptor, MMIO (post_send)
2. Payload, DMA read
4. Payload, DMA write
6. Completion DMA write
(poll_cq)
Requester
Responder
5. RDMA ACK
3. Two-sided request
1
2
3
4
5
6
CPU
7. Memory read to poll
the message
(poll_cq)
7
Notes: 问题： 6， 7谁先谁后？

## Slide 96: RDMA vs. DPDK
Common
  Both are kernel bypassing
Advantage of RDMA
  Fully supported network in the hardware
  Fully zero copy
Advantage of DPDK
  More flexible, i.e., can use a customized network protocol
    RDMA’s black-boxed network protocol may result in poor performance if not using properly! (we will see)

## Slide 97: Performance of RDMA (message)
Source: Fast Remote Memory@NSDI’14

## Slide 98
Is DPDK & RDMA (messaging) sufficient?

## Slide 99: CPU is becoming the problem

## Slide 100: CPU is the problem
CPU cannot become faster
  Power wall (e.g., dennard scaling), The decline of Moore's Law
NIC is continuously becoming faster
  Lower latency (down to 600ns)
  Higher bandwidth (up to 400Gbps)

## Slide 101: Maybe we do not need such high bandwidth?
Most of the time the workload is idle
  Latency is more important than the bandwidth when the workload is idle
CPU achieves relatively low latency if idle w/ kernel-bypassing network
  No request queuing effect
  e.g., Two-sided RDMA achieves 2.2us RTT
  NIC RTT: ~1.5us

## Slide 102: A hidden assumption of low-latency two-sided RDMA is using polling
do {
num_completions = ibv_poll_cq(alice_receive_qp, ...);
} while (num_completions == 0);
// The message must be stored in msg_buf if no error
Print(msg_buf) // Hello
bob
Example: Bob uses polling to receive messages from the receive queue
  The while loop can easily burn the CPU!
Problems of polling
  Extra CPU core usage (CPU cannot be used for others )
  Extra energy consumptions

## Slide 103: Can we use interrupt to reduce the energy?
Interrupt:
  Yield to the kernel, will be scheduled back once the message is received
  Energy efficient: CPU has nearly zero costs if no interrupt comes

## Slide 104: Can we use interrupt to reduce the energy?
Interrupt:
  Yield to the kernel, will be scheduled back once the message is received
Problem:
  1000X latency increases! (2us vs. 2ms)
    Due to the kernel and scheduling effects of the CPU
Dilemma between energy & performance!

## Slide 105
Does kernel-bypassing networking sufficient?
Not sufficient!

## Slide 106
Efficiency = performance + low power consumption

## Slide 107
We also need CPU bypassing!

## Slide 108: High-level concepts of RDMA
Queue Pairs (Send Queue, Complete Queue and Receive Queue)
  SQ, CQ & RQ
  A group of queues form an RDMA connection
    Analog to connections in TCP/IP
User posts networking requests to the SQ
  Two-sided: message datagram (like send/recv)
  One-sided: remote read/write (in a CPU bypassing way!)
Get the completion events from the CQ
Receive two-sided messages from the RQ

## Slide 109: One-sided RDMA
Observation:
  Remote read/write operations is common in applications
    We can let NIC do all these operations!

## Slide 110: One-sided RDMA
Observation:
  Remote read/write operations is common in applications
    We can let NIC do all these operations!
One-sided RDMA
  READ
    The NIC can directly read the server memory bypassing server CPU
  WRITE
    The NIC can directly write the server memory bypassing server CPU
  ATOMICS (fetch & add, compare & swap)
    The NIC can directly execute atomic operations bypassing server CPU

## Slide 111: Example: remote memory copy
DRAM
Suppose we want to implement a remote procedure call (RPC) with RDMA
  The RPC will simply do a memory copy (memcpy)
  For simplicity, we assume only the requester copies to the responder
RDMA
Bob
Alice
DRAM
Copy

## Slide 112: Existing approach: two-sided RDMA based RPC
CPU,RAM
NIC
RAM
NIC
1. Request descriptor, MMIO
2. Payload, DMA read
4. Payload, DMA write
6. Completion DMA write
Requester
Responder
5. RDMA ACK
3. Two-sided request
1
2
3
4
5
6
CPU
The message contains:
1. Remote address
2. Size of the payload
7. Poll the two-sided request
8
9
8. Do the memory copy
10
10. Request descriptor, MMIO + payload DMA
11
11. Poll the two-sided request (reply), done

## Slide 113: Remote memory copy with one-sided RDMA WRITE
RDMA
Bob
Send
Comp
Recv
Queue
pairs
struct ibv_sge list = { .addr = src, length=size };
struct ibv_send_wr wr = {
.sg_list = &list,
.op_code = IBV_WR_RDMA_WRITE, // to the the one-sided WRITE
.wr.wr.rdma.remote_addr = dst,
..., // other fields
};
ibv_post_send(bob_qp, &wr, ...); // send queue
bob
One-sided
Request

## Slide 114: Remote memory copy with one-sided RDMA WRITE
CPU,RAM
NIC
RAM
NIC
1. Request descriptor, MMIO
2. Payload, DMA read
4. Payload, DMA write
6. Completion DMA write
Requester
Responder
5. RDMA ACK
3. RDMA Write request
1
2
3
4
5
6

## Slide 115: One-sided RDMA WRITE vs. Two-sided RDMA
Notes: 性能

## Slide 116: Question: how can RDMA access the remote memory?
RDMA can directly access the virtual address of the remote end
  How can the NIC find the DMA address?
  How can the remote end do the authentication?
    E.g., some virtual address cannot be exposed to the others
struct ibv_sge list = { .addr = src, length=size };
struct ibv_send_wr wr = {
.sg_list = &list,
.op_code = IBV_WR_RDMA_WRITE, // to the the one-sided WRITE
.wr.wr.rdma.remote_addr = dst,
..., // other fields
};
ibv_post_send(bob_qp, &wr, ...); // send queue

## Slide 117: Memory registration (MR)
RDMA uses memory registrations to expose the virtual memory
If Alice wants to expose the memory, she must first register it to the RNIC
  Via ibv_reg_mr()
  Access flags: read/write,etc.
  Return: rkey
NIC will create an internal mapping
Alice
DRAM
Start
End
ibv_reg_mr(..., start, end– start, access_flags, ...)
Virtual – Physical mapping

## Slide 118: One-sided RDMA with Memory Registration
RDMA
Bob
Send
Comp
Recv
Queue
pairs
struct ibv_sge list = { .addr = src, length=size };
struct ibv_send_wr wr = {
.sg_list = &list,
.op_code = IBV_WR_RDMA_WRITE, // to the the one-sided WRITE
.wr.wr.rdma.remote_addr = dst,
.wr.wr.rdma.rkey = ...,
..., // other fields
};
ibv_post_send(bob_qp, &wr, ...); // send queue
bob
One-sided
Request

## Slide 119: One-sided RDMA with Memory Registration
CPU,RAM
NIC
RAM
NIC
1. Request descriptor, MMIO
2. Payload, DMA read
4. Payload, DMA write
6. Completion DMA write
Requester
Responder
5. RDMA ACK
3. RDMA Write request
1
2
3
4
5
6
4.1 Lookup the table
4.2 Check the rkey
4.3 Do the write

## Slide 120: One-sided RDMA with Memory Registration
CPU,RAM
NIC
RAM
NIC
1. Request descriptor, MMIO
2. Payload, DMA read
4. Payload, DMA write
6. Completion DMA write
Requester
Responder
5. RDMA ACK
3. RDMA Write request
1
2
3
4
5
6
4.1 Lookup the table
4.2 Check the rkey
4.3 Do the write
Question: what about the local DMA?

## Slide 121: Local RDMA access also needs MR
The same API ibv_reg_mr()
  Will return two keys: lkey & rkey
    Lkey is used for local accesses
    Rkey is used for remote accesses
struct ibv_sge list = { .addr = src, length=size, lkey = lkey };
struct ibv_send_wr wr = {
.sg_list = &list,
.op_code = IBV_WR_RDMA_WRITE, // to the the one-sided WRITE
.wr.wr.rdma.remote_addr = dst,
.wr.wr.rdma.rkey = ...,
..., // other fields
};
ibv_post_send(bob_qp, &wr, ...); // send queue
bob

## Slide 122: Question: where is the mapping table stored?
Stored in DRAM
  Problem: NIC will use one DMA to fetch for the check (inefficient!)
NIC will uses a small SRAM for the cache
  Avoiding extra lookups for the MR
Alice
DRAM
End
ibv_reg_mr(..., start, end– start, access_flags, ...)
Virtual – Physical mapping

## Slide 123: Performance summary of RDMA
We use one-sided RDMA WRITE as an example
  MMIO: 200-800ns (on Intel x864 machines)
  + (4) DMA: (about) 1us
  + (5): network, depends on the distance & speed of light
    << 1us in rack-scale clusters
  Memory access
    100-400ns
Total RTT: 2-5us
CPU,RAM
NIC
RAM
NIC
1. Request descriptor, MMIO
2. Payload, DMA read
4. Payload, DMA write
6. Completion DMA write
5. RDMA ACK
3. RDMA Write request
1
2
3
4
5
6

## Slide 124: Short recap of RDMA
RDMA: a new networking protocol & API
  Extremely fast: 2-5us in a local rack-scale cluster
Kernel, Network protocol bypassing
  All RDMA operations
CPU-bypassing
  One-sided RDMA operations
    READ,WRITE and ATOMICS