## Slide 1: Non-volatile Memory
Computer System Principles, Fall 2020 (IPADS, SJTU)
An emerging technology
Yubin Xia
Some slides from http://research.cs.wisc.edu/sonar/tutorial/

## Slide 2: NVM: What & Why
What is non-volatile memory?

## Slide 3: NVM Technologies
Persistent
Short access time
Byte addressable

## Slide 4: NVDIMM
Store data in DRAM backed by NAND Flash
Capacity is hard to scale

## Slide 5: Phase-Change Memory (PCM)
Store data within phase-change material
  Amorphous phase: high resistivity (0)
  Crystalline phase: low resistivity (1)
Set phase via current pulse
  Fast cooling → Amorphous
  Slow cooling → Crystalline

## Slide 6: Resistive RAM (RRAM)
Store data by dissolving ions within electrolyte memristive material (e.g., TiOx)

## Slide 7: Spin-Transfer Torque RAM (STT-RAM)
Store data within magnetic-tunnel junction
  Anti-parallel orientation: high resistance (0)
  Parallel orientation: low resistance (1)

## Slide 8: 3D-XPoint
Figure from https://fortune.com/2015/07/28/intel-micron-memory/
Notes: Original link (broken): http://www.intelsalestraining.com/memorytimeline/

## Slide 9: Intel Optane DC Persistent Memory
Figure from Intel, https://www.intel.com/content/www/us/en/architecture-and-technology/optane-dc-persistent-memory.html
Available last year

## Slide 10: Summary

## Slide 11: Where to use

## Slide 12: Ecosystem Overview
NVM Library / libFS
&
kernel module
Applications
user
kernel
NVM Library
BTT
Byte-addressable NVM (Persistent Memory)
DiskFS
NVMFS
read/write
Block I/O
load/store
Direct to NVM (XIP/DAX)
read/write
mmap
mmap

## Slide 13: DiskFS on NVM
Applications
user
kernel
BTT
NVM
DiskFS
read/write
Block I/O
Traditional DiskFS
  Ext2/3/4, XFS, BtrFS, F2FS,...
Block Translation Table (BTT)
  Block interface over NVM
  Atomicity
Q: Why DiskFS on NVM?

## Slide 14: NVMFS
Designed for NVM
  BPFS, PMFS, NOVA, SoupFS,...
Direct Access (DAX)
  Direct load/store on NVM
  Exposed to app using mmap
Applications
user
kernel
NVM
NVMFS
load/store
Direct to NVM (XIP/DAX)
read/write
mmap

## Slide 15: NVM Library over FS
Relies on FS
  PMDK,...
  FS organizes the space
  Library/App controls how to use
Interfaces
  Objects, transactions, memory pool,...
Applications
user
kernel
NVM Library
NVM
NVMFS
load/store
Direct to NVM (XIP/DAX)
read/write
mmap
mmap
Q: Why are they built upon FS?

## Slide 16: NVM Library / libFS with Kernel Module
User-kernel space co-design
  Mnemosyne, Aerie,...
  Better performance
Interfaces
  Objects, transactions, memory pool,...
  FS
NVM Library / libFS
&
kernel module
Applications
user
kernel
NVM
load/store

## Slide 17: Ecosystem Overview
NVM Library / libFS
&
kernel module
Applications
user
kernel
NVM Library
BTT
Byte-addressable NVM (Persistent Memory)
DiskFS
NVMFS
read/write
Block I/O
load/store
Direct to NVM (XIP/DAX)
read/write
mmap
mmap

## Slide 18: Why?
Why FS?
  FS interfaces matter
  Backward compatibility
Why NVMFS?

## Slide 19: DiskFS
FS designed for block-based disks
  Needs BTT for correctness
  Too many layers leading to inefficiency
App
System call interface
VFS
Generic Block Layer
DiskFS
I/O Scheduler
App
Device Driver
(including BTT)
Device Driver
I/O Bus
Memory Bus

## Slide 20: NVMFS
FS designed for byte-addressable NVM
  Simplified stack
  High performance
System call interface
VFS
Generic Block Layer
NVMFS
I/O Scheduler
App
Device Driver
(including BTT)
Memory Bus
Byte-addressability
Const. access latency
load/store interface

## Slide 21: Challenges
Nothing comes free in life...

## Slide 22: Cache and Write-back
 | DISK | NVM
Data cached in | DRAM | CPU cache
Write-back controlled by | Software | Hardware

## Slide 23: Volatile Memory Ordering
Write-back caching
  Improves performance
  Reorders writes to DRAM
Reordering to DRAM does not break correctness

## Slide 24: Non-volatile Memory Ordering
Recovery depends on write ordering

## Slide 25: Non-volatile Memory Ordering
Recovery depends on write ordering
Reordering breaks recovery
Recovery incorrectly considers garbage as valid data

## Slide 26: Simple Solutions
Disable caching
Write-through caching
Flush entire cache at commit
Significantly affect performance!

## Slide 27: Ordering with Existing Hardware
Order writes by flushing cachelines via CLFLUSH
But CLFLUSH
  Stalls the CPU pipeline and serializes execution
  Invalidates the cacheline

## Slide 28: Fixing CLFLUSH: Intel x86 Extensions
CLFLUSHOPT
  Unordered version of CLFLUSH
CLWB
  Same as CLFLUSHOPT
  Does not invalidate cache

## Slide 29: Example: Copy-on-Write

## Slide 30: Example: Copy-on-Write
STORE Y’
STORE Z’
CLWB Y’
CLWB Z’
SFENCE
STORE R’
CLWB R’

## Slide 31: Example: Copy-on-Write
STORE Y’
STORE Z’
CLWB Y’
CLWB Z’
SFENCE
STORE R’
CLWB R’
SFENCE
STORE X’
STORE Z’’
CLWB X’
CLWB Z’’
SFENCE
STORE R’
CLWB R’

## Slide 32: Case study: BPFS
Back to NVMFS
[Condit, SOSP’09]

## Slide 33: BPFS: A BPRAM File System
Guarantees that all file operations execute atomically and in program order
Despite guarantees, significant performance improvements over NTFS on the same media
Short-circuit shadow paging often allows atomic, in-place updates

## Slide 34: BPFS: A BPRAM File System
file
directory
inode
file
root pointer
indirect blocks
inodes
file

## Slide 35: Enforcing FS Consistency Guarantees
What happens if we crash during an update?
  Disk: Use journaling or shadow paging
  BPRAM: Use short-circuit shadow paging

## Slide 36: Review 1: Journaling
Write to journal, then write to file system
A
B
file system
journal
A’
B’
B’
A’
Reliable, but all data is written twice

## Slide 37: Review 2: Shadow Paging
Use copy-on-write up to root of file system
B
A
A’
B’
file’s root pointer
Any change requires bubbling to the FS root
Small writes require large copying overhead

## Slide 38: Short-Circuit Shadow Paging
Inspired by shadow paging
  Optimization: In-place update when possible

## Slide 39: Short-Circuit Shadow Paging
Uses byte-addressability and atomic 64b writes
B
A
A’
B’
file’s root pointer
Inspired by shadow paging
  Optimization: In-place update when possible

## Slide 40: Opt. 1: In-Place Writes
Aligned 64-bit writes are performed in place
  Data and metadata
file’s root pointer
in-place write

## Slide 41: Opt. 2: Exploit Data-Metadata Invariants
Appends committed by updating file size
file’s root pointer + size
in-place append
file size update

## Slide 42: BPFS Example
directory
file
directory
inode
file
root pointer
indirect blocks
inodes
add entry
remove entry
Cross-directory rename bubbles to common ancestor

## Slide 43: Case study: PMFS
Another
[Kumar, EuroSys’14]

## Slide 44: PMFS Layout

## Slide 45: Consistency
Three existing techniques:
  Copy-on-Write (Shadow Paging)
  Journaling
  Log-structured updates
One more NVM specific technique
  Atomic in-place writes
Used for updates on Data Area
Used for updates on Metadata (e.g. inodes)
Used for updates of small portion of data

## Slide 46: Extended Atomic In-place Writes
8 bytes
  CPU natively supports 8-byte atomic writes
  Update inode’s access time
16 bytes
  Using cmpxchg16b instruction
  Update inode’s size and modification time
64 bytes
  Using RTM (introduced in Haswell)
  Update a number of inode fields like delete

## Slide 47: Write Protection Stray Writes
Supervisor Mode Access Protection (SMAP)
  Prohibit writes into user area
Write windows (introduced in PMFS)
  Mount as read-only When writing, CR0.WP is set to zero
Right) http://en.wikipedia.org/wiki/Protection_ring

## Slide 48: Case study: NOVA
One more
[Xu, FAST’16]

## Slide 49: A Log-structured File System
Log-structuring provides cheaper atomicity than journaling and shadow paging
NVMM supports fast, highly concurrent random accesses
  Using multiple logs does not negatively impact performance
  Log does not need to be contiguous
Rethink and redesign log-structuring entirely

## Slide 50: NOVA design goals
Atomicity
  Combine log-structuring, journaling and copy-on-write
High performance
  Split data structure between DRAM and NVM
Efficient garbage collection
  Fine-grained log cleaning with log as a linked list
  Log only contains metadata
Fast recovery
  Lazy rebuild
  Parallel scan

## Slide 51: Atomicity
Log-structuring for single log update
  Write, msync, chmod, etc
  Strictly commit log entry to NVMM before updating log tail
Lightweight journaling for update across logs
  Unlink, rename, etc
  Journal log tails instead of metadata or data
Copy-on-write for file data
  Log only contains metadata
  Log is short

## Slide 52: Atomicity
Log-structuring for single log update
  Write, msync, chmod, etc
  Strictly commit log entry to NVMM before updating log tail
Lightweight journaling for update across logs
  Unlink, rename, etc
  Journal log tails instead of metadata or data
Copy-on-write for file data
  Log only contains metadata
  Log is short

## Slide 53: Performance
Per-inode logging allows for high concurrency
Split data structure between DRAM and NVM
  Performance log is simple and efficient
  Volatile tree structure has no consistency overhead

## Slide 54: Performance
Per-inode logging allows for high concurrency
Split data structure between DRAM and NVM
  Performance log is simple and efficient
  Volatile tree structure has no consistency overhead

## Slide 55: NOVA layout
Put allocator in DRAM
High scalability
  Per-CPU NVM free list, journal and inode table
  Concurrent transactions and allocation/deallocation

## Slide 56: Fast garbage collection
Log is a linked list
Log only contains metadata
Fast GC deletes dead log pages from the linked list
No copying

## Slide 57: Thorough garbage collection
Starts if valid log entries < 50% log length
Format a new log and atomically replace the old one
Only copy metadata

## Slide 58: Case study: Aerie
A final
[Volos, EuroSys’14]

## Slide 59: POSIX File: Expensive abstraction
Universal abstraction: Everything is a file
  Has generic-overhead cost

## Slide 60: POSIX File: Expensive abstraction
Rigid interface and policies
  Has fixed components and costs
  Hinders application-specific customization

## Slide 61: POSIX File: Expensive abstraction
Generic-overhead costs
Rigid interfaces and policies
~2.5us ≈ 25x NVM latency

## Slide 62: Customizing the file system today
Modify the kernel
Add a layer over existing kernel file system
Use a user-mode framework such as FUSE
Need flexible interfaces

## Slide 63: Kernel safely multiplexes NVM
Allocation: allocates NVM regions
Addressing: Memory-maps NVM regions
Protection: Keep track of region access rights
HW
Kernel
allocation, protection, addressing

## Slide 64: Library implements functionality
HW
Kernel
allocation, protection, addressing
APP
LibFS
(layout, logic)
API
APP
LibFS
(layout, logic)
API
APP
Other LibFS
(layout, logic)
API
USER

## Slide 65: Integrity via Trusted File Service
HW
Kernel
allocation, protection, addressing
APP
LibFS
(layout, logic)
API
Trusted
FS
Service
(TFS)
APP
Other LibFS
(layout, logic)
API
USER

## Slide 66: Integrity via Trusted File Service
HW
APP
Trusted
FS
Service
(TFS)
APP
LibFS
File data
Metadata
Lease Manager
(sharing)
RPC
Update
Read/
Write
LibFS
(layout, logic)
API
Read
Metadata
Server
(integrity)
Read/
Write
USER

## Slide 67: Questions
Notes: Time: 1:18:00