## Slide 1: Transparent and Efficient CFI Enforcement with Intel Processor Trace (IPT)
Yutao Liu, Peitao Shi, Xinran Wang, Haibo Chen, Binyu Zang, Haibing Guan
Institute of Parallel and Distributed System (IPADS)
Shanghai Jiao Tong University
http://ipads.se.sjtu.edu.cn
IPADS
Institute of Parallel and Distributed Systems
Control Flow Integrity

## Slide 2: Control Flow Hijacking Attacks
Memory corruption bugs
Victim memory
Overwrite
Shellcode execution
Code reuse
BAD
THING
Attackers

## Slide 3: Attacks & Defenses
Defenses
Control flow hijacking attacks
Randomization
Enforcement

## Slide 4: Program’s Control Flow
BB-1
BB-2
BB-3
BB-4
BB-5
BB-6
BB-7
BB-8
BB-9
BB-10
Program consists of basic block (BB)
Control flow from one BB to other BB
Each BB has limited valid targets
CFG can be pre-generated
Control Flow Graph (CFG)
Attack: issues an invalid control flow transfer
BB-11
INVALID
Control Flow Integrity (CFI):
Enforce control flow as CFG during runtime

## Slide 5: Runtime CFI Enforcement
Method #1: instrumented checking
Method #2: transparent monitoring
jmp *%ecx
…
call *%ebx
…
ret
check(%ecx)
jmp *%ecx
…
check(%ebx)
call *%ebx
…
check(stack)
ret
Compiler
based
Binary
rewriting
Check all branches
Break code integrity
COTS unfriendly
Share library unfriendly
Binary
Analysis
Binary
RUNTIME
Compare
Transparent to applications

## Slide 6: Transparent Monitoring
How to TRACE?
When to TRIGGER?
What to CHECK?

## Slide 7: How to Trace
Trace by hardware (performance counter)
  Two choices before: BTS & LBR
Branch trace store (BTS)
  Trace every branch in memory: source,destination, type
  Sufficient information, but extraordinarily slow
Last branch record (LBR)
  Only trace most recent (16 or 32) branches in register
  Very fast, but with insufficient information
  History flush attacks

## Slide 8: When to trigger
When the trace buffer is full
  Buffer size matters
  Trade-off between performance and security
When specific events happen
  Whenever attack may happen
  Cross-boundary points
Security sensitive system call

## Slide 9: What to check
Heuristic checking
  Ensure that control flow obeys some simple rules:
    Call to a function entry
    Return to instruction right after call
    Etc.
Strict CFG enforcement
  Pre-generate CFG,and enforce it at runtime
  Fine- or coarse-grained CFG
    Shadow stack?
Fine-grained CFG enforcement

## Slide 10: In a Summary…
Efficient trace with sufficient runtime information
  BTS and LBR cannot survive
Appropriate triggering point
  Prevent attacks without sacrificing too much performance
Fine-grained CFG enforcement
  Heuristic check is not enough

## Slide 11
Intel Processor Trace (IPT)
  Introduced in Intel Broadwell
  Fast tracing
  Can trace sufficient information in memory
IPT to the Rescue
BUT WHY>>>

## Slide 12
IPT uses aggressive compression
  Unconditional direct branches are not logged at all
  Conditional branches are compressed to a single bit
  Each indirect branch is traced as one target address
  Result in average <1 bit per retired instruction
Background: Demystify IPT Fast Trace

## Slide 13
TIP packet: target address of indirect branch
TNT packet: indication of taken or non-taken conditional branch
Background: IPT Trace Example

## Slide 14
The performance overhead is shifted from tracing to decoding
  Decoding is several orders of magnitude slower than tracing.
Challenges: Fast Trace vs. Slow Decode
 | Precise | Tracing | Decoding | Filtering
BTS | Full | Slow (50X) | Fast | None
LBR | Low | Very Fast (< 1%) | Fast | CPL, CoFI
IPT | Full | Fast (3%) | Slow (200X) | CPL, CR3, IP

## Slide 15: Contribution
FlowGuard: practical CFI with IPT
  Transparent monitor without instrumentation
  Efficient trace and check by separating fast and slow paths
  Precise CFI enforcement with fine-grained CFG and runtime information
Evaluation results
  Apply FlowGuard to server applications
  Prevent a various of code reuse attacks
  Less than 4% performance overhead for normal use cases

## Slide 16: Outline
  Efficient trace and check
  Precise CFI enforcement
Implementation and evaluation

## Slide 17
Main problem: inconsistency between static generated CFG and IPT traced data
Why Slow Decode is Required?
BB-1
BB-2
BB-3
BB-4
BB-5
BB-6
BB-7
BB-8
BB-9
BB-10
N
T
Traditional static generated CFG
Indirect edge
Direct edge
Conditional branch information
IPT traced data
N
T
BB-2
BB-3
BB-5
BB-7
BB-9
BB-10

## Slide 18
Indirect targets connected CFG (ITC-CFG)
  Nodes left: BB with incoming indirect edges (IT-BB)
  Edges reconnection: two IT-BBs are connected if and only if:
    There is only one indirect edge in the path from BB-x to BB-y
    This indirect edge is targeted at BB-y
Solution: IPT Compatible CFG Construction
BB-2
BB-3
BB-5
BB-7
BB-9
BB-10
BB-1
BB-2
BB-3
BB-4
BB-5
BB-6
BB-7
BB-8
BB-9
BB-10
N
T
Static
analysis

## Slide 19
Fast Path Check in Runtime
BB-2
BB-3
BB-5
BB-7
BB-9
BB-10
IPT traced data
ITC-CFG
IPT traced data can be directly matched on the ITC-CFG
TIP
BB-2
TIP
BB-3
TIP
BB-7
TIP
BB-9
?
……

## Slide 20: Outline
  Efficient trace and check
  Precise CFI enforcement
Implementation and evaluation

## Slide 21
Coarse-grained CFI
  Over-approximated CFG generation
  Result in large false negative
  Not benefit from the whole dynamic information
Precision loss
  Average indirect targets allowed (AIA)
Fast Path (ITC-CFG) Problem
Main reason:
lack of TNT information
This can be solved by slow decode!

## Slide 22
Solution: Separate Fast and Slow Path
Attack detected
IPT traced data
ITC-CFG
Edges
matched?
No attack
N
Y
Edges
matched?
Attack detected
N
No attack
Credible
edges
matched?
Y
Y
Slow path
N
Binary
IPT traced data
Credit
labeled
ITC-CFG
Pre-generated
Fast path
Slow path
How?

## Slide 23
Dynamic training to label ITC-CFG edges with credits
  The credit of each edge depends on its occurrence during the training phase
  Each edge is also associated with the TNT information
Dynamic Fuzzing Training
BB-2
BB-3
BB-5
BB-7
BB-9
BB-10
ITC-CFG
BB-2
BB-3
BB-5
BB-7
BB-9
BB-10
Credit Labeled ITC-CFG
NULL
NULL
T

## Slide 24
Dynamic training to label ITC-CFG edges with credits
  The credit of each edge depends on its occurrence during the training phase
  Each edge is also associated with the TNT information
We use a fuzzing based approach
  AFL: a coverage-oriented fuzzer
Note: the security of FlowGuard does not rely on the coverage
Dynamic Fuzzing Training (cont’)

## Slide 25
We have a default setting with 7 security-sensitive system calls
  read, write, execve, mmap, mprotect, sigaction, sigreturn
Provide users with interface to specify their own endpoints
System Call Interception

## Slide 26: Outline
  Efficient trace and check
  Precise CFI enforcement
Implementation and evaluation

## Slide 27: FlowGuard Architecture
Kernel
Module
Syscall Interceptor
Flow
Checker
Fast
Path
Slow
Path
Cores
Process
Executable
Libraries
Static
Binary
Analysis
Dynamic
Fuzzing
Training
Credit
Labeled
ITC-CFG
Memory
User
Kernel
1
2
3
4
5

## Slide 28: Experimental Setup
Intel Skylake machine with IPT support
  8 cores & 16GB RAM
  Debian 8.0, Linux kernel 4.3.0
Dyninst plugin for static binary analysis
AFL for fuzzing the software and collecting training inputs
  desock to channel socket communication to the console

## Slide 29: Security Analysis
Attack detected
  ROP: during write() syscall
  SROP: during sigreturn() syscall
Average Indirect-targets Allowed (AIA) summary

## Slide 30: Performance Evaluation
Macro Benchmarks

## Slide 31: Summary
FlowGuard: leverage IPT for practical CFI
  Transparent monitor without instrumentation
  Efficient trace and check by separating fast and slow paths
  Precise CFI enforcement with fine-grained CFG and runtime information
A working prototype on Intel Skylake with promising result
  Successfully detect ROP like attacks and optimize AIA
  Small Performance impact
IPADS
Institute of Parallel and Distributed Systems

## Slide 32
Questions
http://ipads.se.sjtu.edu.cn
Institute of Parallel And Distributed Systems
IPADS
Institute of Parallel and Distributed Systems
Thanks